Name:  								Id#

COE 405, Term 031

Design & Modeling of Digital Systems

Quiz# 4

Date: Tuesday, Dec. 23, 2003

# Given the following Entity Description for a JK Flip-Flop:

# ENTITY JKFF IS 
GENERIC (delay : TIME := 4 NS); 
PORT (j, k, clk, reset : IN BIT; q, qb : OUT BIT); 
END JKFF;

## Model the JK-FF using a BLOCK statement with a GUARD expression and conditional signal assignment, assuming that reset is synchronous and the JK-FF is rising-edge triggered.

## Model the JK-FF using a BLOCK statement with a GUARD expression and slective signal assignment, assuming that reset is synchronous and the JK-FF is rising-edge triggered.

## Model the JK-FF using a BLOCK statement with a GUARD expression and conditional signal assignment, assuming that reset is asynchronous and the JK-FF is rising-edge triggered.