Name:									Id#

COE 405, Term 131

Design & Modeling of Digital Systems

Quiz# 4

Date: Sunday, Dec. 15, 2013

# Consider the logic network below with inputs {a, b, c, d, e} and output {k}:

# Assume that the delay of the inverter gate is 1 and that the delay of the 2-input NAND gate is 2.  Also, assume that the input data-ready times are zero except for input a, which is equal to 2.

## Compute the data ready times and slacks for all vertices in the network.

## Determine the topological critical path.

## Suggest an implementation of the function k using only inverters and 2-input NAND gates to reduce the delay of the circuit to the minimum possible and determine the maximum propagation delay in the optimized circuit. Has the area been affected?

# Determine possible circuits that will be synthesized by each of the following modules:

- module m1  (output [1:0] y, input x1, x2, x3);

assign y = x1?1:x2?2:x3?3:0;

endmodule

- module m2 (output  reg y, input e1, e2, e3, x1, x2, x3 );

always @ (e1, e2, e3, x1, x2, x3) begin

if (e1) y=x1;

if (e2) y=x2;

if (e3) y=x3;

end

endmodule

- module m3 (output reg [3:0] Data_out, input DIN, clock, reset);

always @ (posedge clock,  posedge reset) begin

if (reset) Data_out = 0;

else begin

Data_out[0]=DIN;

Data_out[1]=Data_out[0];

Data_out[2]=Data_out[1];

Data_out[3]=Data_out[2];

end

end

endmodule

- module  m4 (output reg Y1, Y2, input  A, B, C, D, sel, clk);

always @ (posedge clk) begin

Y1= A | B; Y2 = Y1 | C;

if (sel) Y1 = Y2 | D;

end

endmodule