Name:  KEY								Id#

COE 405, Term 031

Design & Modeling of Digital Systems

Quiz# 4

Date: Tuesday, Dec. 23, 2003

# Given the following Entity Description for a JK Flip-Flop:

# ENTITY JKFF IS 
GENERIC (delay : TIME := 4 NS); 
PORT (j, k, clk, reset : IN BIT; q, qb : OUT BIT); 
END JKFF;

## Model the JK-FF using a BLOCK statement with a GUARD expression and conditional signal assignment, assuming that reset is synchronous and the JK-FF is rising-edge triggered.

Architecture Sreset of JKFF is

begin

edge: BLOCK ( clk = '1' AND NOT clk'STABLE )

BEGIN

q <= GUARDED '0' after delay when reset = '1'  else '1' after delay when 			j='1' and k='0' else '0' after delay when j='0' and k='1' else not q after delay 		when j='1' and k='1' else q;

qb <=  NOT q;

END BLOCK;

end Sreset;

## Model the JK-FF using a BLOCK statement with a GUARD expression and slective signal assignment, assuming that reset is synchronous and the JK-FF is rising-edge triggered.

Architecture Sreset2 of JKFF is

signal s : bit_vector(2 downto 0);

begin

s <= reset & j & k;

edge: BLOCK ( clk = '1' AND NOT clk'STABLE )

BEGIN

with s select

q <= GUARDED '0' after delay when "001",

'1' after delay when "010",

not q after delay when "011",

q after delay when "000",

'0' after delay when others;

qb <=  NOT q;

END BLOCK;

end Sreset2;

## Model the JK-FF using a BLOCK statement with a GUARD expression and conditional signal assignment, assuming that reset is asynchronous and the JK-FF is rising-edge triggered.

Architecture ASreset of JKFF is

begin

edge: BLOCK ( reset='1' OR (clk = '1' AND NOT clk'STABLE ) )

BEGIN

q <= GUARDED '0' after delay when reset = '1'  else '1' after delay when j='1' and k='0' else '0' after delay when j='0' and k='1' else not q after delay when j='1' and k='1' else q;

qb <=  NOT q;

END BLOCK;

end ASreset;