Name: KEY									Id#

COE 405, Term 122

Design & Modeling of Digital Systems

Quiz# 4

Date: Monday, April 29, 2013

# Consider the logic network below with inputs {a, b, c, d, e, f} and output {X}:

# Assume that the delay of a gate is related to the number of its inputs i.e. the delay of a 2-input AND gate is 2.  Also, assume that the input data-ready times are zero for all inputs except input a, which has a data-ready time of 2.

## Compute the data ready times and slacks for all vertices in the network.

## Determine the topological critical path.

## Suggest an implementation of the function X to reduce the delay of the circuit to the minimum possible and determine the maximum propagation delay in the optimized circuit. Has the area been affected?