## Slide 1: COE 561 Digital System Design & Synthesis Introduction to VHDL: Part II
Dr. Aiman H. El-Maleh
Computer Engineering Department
King Fahd University of Petroleum & Minerals

## Slide 2: Outline
Behavioral Modeling of ASM
Signal attributes
Subprograms, Packages, and Libraries
Data types in VHDL
FILE I/O
VHDL coding styles for synthesis

## Slide 3: Behavioral Modeling of ASM
entity Controller is
port (Clr_P1_P0, Ld_P1_P0, Ld_R0: out bit;
En, Ld, clk, rst: in bit);
end Controller;
Architecture Behavioral of Controller is
Constant S_idle: bit_vector(1 downto 0) := "00";
Constant S_1: bit_vector(1 downto 0) := "01";
Constant S_full: bit_vector(1 downto 0) := "10";
Constant S_wait: bit_vector(1 downto 0) := "11";
Signal state, next_state:bit_vector(1 downto 0);
begin
process(clk) begin
If (Clk'EVENT and Clk = '1‘) Then
if (rst='1') then state <= S_idle;
else state <= next_state; end if;
end if;
End process;
process(state, En, Ld) begin
Clr_P1_P0 <= '0'; Ld_P1_P0<='0'; Ld_R0<='0';
case state is
when S_idle =>
if (En='1') then next_state<=S_1; Ld_P1_P0<='1';
else next_state<=S_idle; end if;

## Slide 4: Behavioral Modeling of ASM
When S_1 => next_state<=S_full; Ld_P1_P0<='1';
When S_full =>
if (Ld='0') then next_state<=S_wait;
else
Ld_R0<='1';
if (En='1') then
next_state<=S_1; Ld_P1_P0<='1';
else
next_state<=S_idle; Clr_P1_P0<='1';
end if;
end if;
When S_wait =>
if (Ld='0') then next_state<=S_wait;
else Ld_R0<='1';
if (En='1') then next_state<=S_1; Ld_P1_P0<='1';
else next_state<=S_idle; Clr_P1_P0<='1';
end if;
end if;
end case;
end process;
end Behavioral ;

## Slide 5: Signal Attributes…
Attributes are named characteristics of an Object (or Type) which has a value that can be referenced.
Signal Attributes
  S`Event -- Is TRUE if Signal S has changed.
  S`Stable(t) -- Is TRUE if Signal S has not changed for the last ``t`` period. If t=0; it is written as S`Stable
  S`Last_Value -- Returns the previous value of S before the last change.
  S`Active -- -- Is TRUE if Signal S has had a transaction in the current simulation cycle.
  S`Quiet(t) -- -- Is TRUE if no transaction has been placed on Signal S for the last ``t`` period. If t=0; it is written as S`Quiet
  S`Last_Event -- Returns the amount of time since the last value change on S.

## Slide 6: …Signal Attributes
architecture ex of example is
signal a, a4: bit; signal a1, a2, a3 : Boolean;
begin
a <= '0' after 5 ns, '1' after 10 ns, '1' after 15 ns, '0' after 20 ns;
a1 <= a'event;
a2 <= a'stable(2 ns);
a3 <= a'quiet;
a4 <= a'last_value;
end ex;

## Slide 7: Subprograms…
Subprograms consist of functions and procedures.
Subprograms are used to
  Simplify coding,
  Achieve modularity,
  Improve readability.
Functions return values and cannot alter values of their parameters.
Procedures used as a statement and can alter values of their parameters.
All statements inside a subprogram are sequential.

## Slide 8: …Subprograms
Subprograms
  Concurrent
  Sequential
Concurrent subprograms exist outside of a process or another subprogram.
Sequential subprograms exist in a process statement or another subprogram.
A procedure exists as a separate statement in architecture or process.
A function usually used in assignment statement or expression.

## Slide 9: Functions
Function specification:
  Name of the function
  Formal parameters of the function
    Class constant is default
    Name of the parameter
    Mode IN is default & only allowed mode
    Type of the parameter
  Return type of the function
  Local declarations
A function body
  Must contain at least one return statement
  May not contain a wait statement

## Slide 10: A Left-Shift Function
Subtype Byte IS Bit_Vector (7 Downto 0);
Function SLL (V: Byte; N: Natural; Fill: Bit) Return Byte IS
Variable Result: Byte := V;
Begin
For I IN 1 To N Loop
Result := Result (6 Downto 0) & Fill;
End Loop;
Return Result;
End SLL;

## Slide 11: Using the Function
Architecture Functional Of LeftShifter IS
Subtype Byte IS Bit_Vector (7 Downto 0);
Function SLL (V: Byte; N: Natural; Fill: Bit) Return Byte is
Variable Result: Byte := V;
Begin
For I IN 1 To N Loop
Result := Result (6 Downto 0) & Fill;
End Loop;
Return Result;
End SLL;
Begin
Sout <= SLL(Sin, 1, ‘0’) After 12 ns;
End Functional;

## Slide 12: A Single-Bit Comparator
Entity Bit_Comparator IS
Port ( a, b, -- data inputs
gt, -- previous greater than
eq, -- previous equal
lt: IN BIT; -- previous less than
a_gt_b, -- greater
a_eq_b, -- equal
a_lt_b: OUT BIT); -- less than
End Bit_Comparator;
a_gt_b = a . gt + b` . gt + a . b`
a_eq_b = a . b . eq + a` . b` . eq
a_lt_b = b . lt + a` . lt + b . a`

## Slide 13: A Single-Bit Comparator using Functions
Architecture Functional of Bit_Comparator IS
Function fgl (w, x, gl: BIT) Return BIT IS
Begin
Return (w AND gl) OR (NOT x AND gl) OR (w AND NOT x);
End fgl;
Function feq (w, x, eq: BIT) Return BIT IS
Begin
Return (w AND x AND eq) OR (NOT w AND NOT x AND eq);
End feq;
Begin
a_gt_b <= fgl (a, b, gt) after 12 ns;
a_eq_b <= feq (a, b, eq) after 12 ns;
a_lt_b <= fgl (b, a, lt) after 12 ns;
End Functional;

## Slide 14: Binary to Integer Conversion Function
Function To_Integer (Bin : BIT_VECTOR) Return Integer IS
Variable Result: Integer;
Begin
Result := 0;
For I IN Bin`RANGE Loop
If Bin(I) = ‘1’ then
Result := Result + 2**I;
End if;
End Loop;
Return Result;
End To_Integer;

## Slide 15: Procedure Specification
Name of the procedure
Formal parameters of the procedure
  Class of the parameter
    optional
    defaults to constant
  Name of the parameter
  Mode of the parameter
    optional
    defaults to IN
  Type of the parameter
Local declarations

## Slide 16: A Left-Shift Procedure
Subtype Byte is Bit_Vector (7 downto 0);
Procedure SLL (Signal Vin : In Byte; Signal Vout :out Byte; N: Natural; Fill: Bit; ShiftTime: Time) IS
Variable Temp: Byte := Vin;
Begin
For I IN 1 To N Loop
Temp := Temp (6 downto 0) & Fill;
End Loop;
Vout <= Temp after N * ShiftTime;
End SLL;

## Slide 17: Using the Procedure
Architecture Procedural of LeftShifter is
Subtype Byte is Bit_Vector (7 downto 0);
Procedure SLL (Signal Vin : In Byte; Signal Vout :out Byte; N: Natural; Fill: Bit; ShiftTime: Time) IS
Variable Temp: Byte := Vin;
Begin
For I IN 1 To N Loop
Temp := Temp (6 downto 0) & Fill;
End Loop;
Vout <= Temp after N * ShiftTime;
End SLL;
Begin
Process (Sin)
Begin
SLL(Sin, Sout, 1, ‘0’, 12 ns) ;
End process;
End Procedural;

## Slide 18: Binary to Integer Conversion Procedure
Procedure Bin2Int (Bin : IN BIT_VECTOR; Int: OUT Integer) IS
Variable Result: Integer;
Begin
Result := 0;
For I IN Bin`RANGE Loop
If Bin(I) = ‘1’ Then
Result := Result + 2**I;
End If;
End Loop;
Int := Result;
End Bin2Int;

## Slide 19: Integer to Binary Conversion Procedure
Procedure Int2Bin (Int: IN Integer; Bin : OUT BIT_VECTOR) IS
Variable Tmp: Integer;
Begin
Tmp := Int;
For I IN 0 To (Bin`Length - 1) Loop
If ( Tmp MOD 2 = 1) Then
Bin(I) := ‘1’;
Else Bin(I) := ‘0’;
End If;
Tmp := Tmp / 2;
End Loop;
End Int2Bin;

## Slide 20: Packages…
A package is a common storage area used to hold data to be shared among a number of entities.
Packages can encapsulate subprograms to be shared.
A package consists of
  Declaration section
  Body section
The package declaration section contains subprogram declarations, not bodies.
The package body contains the subprograms’ bodies.
The package declaration defines the interface for the package.

## Slide 21: …Packages
All items declared in the package declaration section are visible to any design unit that uses the package.
A package is used by the USE clause.
The interface to a package consists of any subprograms or deferred constants declared in the package declaration.
The subprogram and deferred constant declarations must have a corresponding subprogram body and deferred constant value in the package body.
Package body May contain other declarations needed solely within the package body.
  Not visible to external design units.

## Slide 22: Package Declaration
The package declaration section can contain:
  Subprogram declaration
  Type, subtype declaration
  Constant, deferred constant declaration
  Signal declaration creates a global signal
  File declaration
  Alias declaration
  Component declaration
  Attribute declaration, a user-defined attribute
  Attribute specification
  Use clause

## Slide 23: Package Body
The package body main purpose is
  Define the values of deferred constants
  Specify the subprogram bodies for subprograms declared in the package declaration
The package body can also contain:
  Subprogram declaration
  Subprogram body
  Type, subtype declaration
  Constant declaration, which fills in the value for deferred constants
  File declaration
  Alias declaration
  Use clause

## Slide 24: Existing Packages
Standard Package
  Defines primitive types, subtypes, and functions.
  e.g. Type Boolean IS (false, true);
  e.g. Type Bit is (‘0’, ‘1’);
TEXTIO Package
  Defines types, procedures, and functions for standard text I/O from ASCII files.

## Slide 25: Package Example for Component Declaration
Package simple_gates is
COMPONENT n1 PORT (i1: IN BIT; o1: OUT BIT); END COMPONENT ;
COMPONENT n2 PORT (i1,i2: IN BIT;o1:OUT BIT);END COMPONENT;
COMPONENT n3 PORT (i1, i2, i3: IN BIT; o1: OUT BIT); END COMPONENT;
end simple_gates;
Use work.simple_gates.all;
ENTITY bit_comparator IS
PORT (a, b, gt, eq, lt : IN BIT; a_gt_b, a_eq_b, a_lt_b : OUT BIT);
END bit_comparator;
ARCHITECTURE gate_level OF bit_comparator IS
FOR ALL : n1 USE ENTITY WORK.inv (single_delay);
FOR ALL : n2 USE ENTITY WORK.nand2 (single_delay);
FOR ALL : n3 USE ENTITY WORK.nand3 (single_delay);
--Intermediate signals
SIGNAL im1,im2, im3, im4, im5, im6, im7, im8, im9, im10 : BIT;
BEGIN
-- description of architecture
END gate_level;

## Slide 26: Package Example…
Package Shifters IS
Subtype Byte IS Bit_Vector (7 Downto 0);
Function SLL (V: Byte; N: Natural; Fill: Bit := ‘0’) Return Byte;
Function SRL (V: Byte; N: Natural; Fill: Bit := ‘0’) Return Byte;
Function SLA (V: Byte; N: Natural; Fill: Bit := ‘0’) Return Byte;
Function SRA (V: Byte; N: Natural) Return Byte;
Function RLL (V: Byte; N: Natural) Return Byte;
Function RRL (V: Byte; N: Natural) Return Byte;
End Shifters;

## Slide 27: …Package Example…
Package Body Shifters IS
Function SLL (V: Byte; N: Natural; Fill: Bit) Return Byte is
Variable Result: Byte := V;
Begin
If N >= 8 Then
Return (Others => Fill);
End If;
For I IN 1 To N Loop
Result := Result (6 Downto 0) & Fill;
End Loop;
Return Result;
End SLL;
.
.
.
End Shifters;

## Slide 28: …Package Example
USE WORK.Shifters.ALL
Architecture Functional of LeftShifter IS
Begin
Sout <= SLL(Sin, 1, ‘0’) After 12 ns;
End Functional;

## Slide 29: Another Package Example…
Package Basic_Utilities IS
Type Integers IS Array (0 to 5) of Integer;
Function fgl (w, x, gl: BIT) Return BIT;
Function feq (w, x, eq: BIT) Return BIT;
Procedure Bin2Int (Bin : IN BIT_VECTOR; Int: OUT Integer);
Procedure Int2Bin (Int: IN Integer; Bin : OUT BIT_VECTOR);
Procedure Apply_Data (
Signal Target: OUT Bit_Vector (3 Downto 0);
Constant Values: IN Integers;
Constant Period: IN Time);
Function To_Integer (Bin : BIT_VECTOR) Return Integer;
End Basic_Utilities;

## Slide 30: …Another Package Example…
Package Body Basic_Utilities IS
Function fgl (w, x, gl: BIT) Return BIT IS
Begin
Return (w AND gl) OR (NOT x AND gl) OR (w AND NOT x);
End fgl;
Function feq (w, x, eq: BIT) Return BIT IS
Begin
Return (w AND x AND eq) OR (NOT w AND NOT x AND eq);
End feq;
.
.
.
End Basic_Utilities;

## Slide 31: …Another Package Example
USE WORK.Basic_Utilities.ALL
Architecture Functional of Bit_Comparator IS
Begin
a_gt_b <= fgl (a, b, gt) after 12 ns;
a_eq_b <= feq (a, b, eq) after 12 ns;
a_lt_b <= fgl (b, a, lt) after 12 ns;
End Functional;

## Slide 32: Design Libraries…
VHDL supports the use of design libraries for categorizing components or utilities.
Applications of libraries include
  Sharing of components between designers
  Grouping components of standard logic families
  Categorizing special-purpose utilities such as subprograms or types
Two Types of Libraries
  Working Library (WORK) {A Predefined library into which a Design Unit is Placed after Compilation.},
  Resource Libraries {Contain design units that can be referenced within the design unit being compiled}.

## Slide 33: … Design Libraries…
Only one library can be the Working library
Any number of Resource Libraries may be used by a Design Entity
There is a number of predefined Resource Libraries
The Library clause is used to make a given library visible
The Use clause causes Package Declarations within a Library to be visible
Library management tasks, e.g. Creation or Deletion, are not part of the VHDL Language Standard  Tool Dependent

## Slide 34: … Design Libraries…
Exiting libraries
  STD Library
    Contains the STANDARD and TEXTIO packages
    Contains all the standard types & utilities
    Visible to all designs
  WORK library
    Root library for the user
IEEE library
  Contains VHDL-related standards
  Contains the std_logic_1164 (IEEE 1164.1) package
    Defines a nine values logic system
    De Facto Standard for all Synthesis Tools

## Slide 35: …Design Libraries
To make a library visible to a design
  LIBRARY libname;
The following statement is assumed by all designs
  LIBRARY WORK;
To use the std_logic_1164 package
  LIBRARY IEEE
  USE IEEE.std_logic_1164.ALL
By default, every design unit is assumed to contain the following declarations:
  LIBRARY STD , work ;
  USE STD.Standard.All ;

## Slide 36: Arithmetic & Logical Operators for std_logic : Example
library ieee;
use ieee.std_logic_1164.all;
use ieee.std_logic_unsigned.all;
entity example is
port (a, b: IN std_logic_vector (7 downto 0));
end example;
architecture try of example is
signal x1, x2, x3, x4, x5, x6, x7, x8, x9, x10 : std_logic_vector (7 downto 0);
begin
  x1 <= not a;
  x2 <= a and b;
  x3 <= a nand b;
  x4 <= a or b;
  x5 <= a nor b;
  x6 <= a xor b;
  x7 <= a xnor b;
  x8 <= a + b;
  x9 <= a - b;
  x10 <= "+" (a, b);
end try;

## Slide 37: Data Types
DATA TYPES
A Data Type defines a set of values & a set of operations.
VHDL is a strongly-typed Language. Types cannot be mixed in Expressions or in assigning values to Objects in general
COMPOSITES
Arrays
Records
SCALARS
Numeric (Integer, Real)
Enumerations
Physical
File Type &
Access Type
Not Used for H/W Modeling

## Slide 38: Scalar Data Types
SYNTAX
  TYPE Identifier IS Type-Definition
Numeric Data Type
  Type-Definition is a Range_Constraint as follows:
  Type-Definition := Range Initial-Value < To | DownTo> Final-Value
Examples
  TYPE address IS RANGE 0 To 127;
  TYPE index IS RANGE 7 DownTo 0;
  TYPE voltage IS RANGE -0.5 To 5.5;

## Slide 39: Number Formats
Integers have no Decimal Point.
Integers may be Signed or Unsigned (e.g. -5, 356 )
A Real number must have either a Decimal Point, a -ive Exponent Term (Scientific Notation), or both.
Real numbers may be Signed or Unsigned (e.g. -3.75, 1E-9, 1.5E-12 )
Based Numbers:
  Numbers Default to Base 10 (Decimal)
  VHDL Allows Expressing Numbers Using Other Bases
  Syntax
    B#nnnn# -- Number nnnn is in Base B
  Examples
    16#DF2# -- Base 16 Integer (HEX)
    8#7134# -- Base 8 Integer (OCTAL)
    2#10011# -- Base 2 Integer (Binary)
    16#65_3EB.37# -- Base 16 REAL (HEX)

## Slide 40: Predefined Numeric Data Types
INTEGER -- Range is Machine limited but At Least -(231 - 1) To (231 - 1)
POSITIVE -- INTEGERS > 0
NATURAL -- INTEGERS >= 0
REAL -- Range is Machine limited

## Slide 41: Enumeration Data Type
Parenthesized ordered list of literals.
  Each may be an identifier or a character literal.
  The list elements are separated by commas
A Position # is associated with each element in the List
Position #`s begin with 0 for the Leftmost Element
Variables & Signals of type ENUMERATION will have the leftmost element as their Default (Initial) value unless, otherwise explicitly assigned.
Examples
  TYPE Color IS (Red, Orange, Yellow, Green, Blue, Indigo, Violet);
  TYPE Tri_Level IS (`0`, `1`, `Z`);
  TYPE Bus_Kind IS (Data, Address, Control);
  TYPE state IS (Init, Xmit, Receive, Wait, Terminal);

## Slide 42: Predefined Enumerated Data Types
TYPE BIT IS ( `0` , `1`) ;
TYPE BOOLEAN IS ( False, True) ;
TYPE CHARACTER IS (128 ASCII Chars......) ;
TYPE Severity_Level IS (Note, Warning, Error, Failure) ;
TYPE Std_U_Logic IS (
`U` , -- Uninitialized
`X` , -- Forcing Unknown
`0` , -- Forcing 0
`1` , -- Forcing 1
`Z` , -- High Impedance
`W` , -- Weak Unknown
`L` , -- Weak 0
`H` , -- Weak 1
`-` , -- Don`t Care
) ;
SUBTYPE Std_Logic IS resolved Std_U_Logic ;

## Slide 43: Physical Data Type
Specifies a Range Constraint , one Base Unit, and 0 or more secondary units.
Base unit is indivisible, i.e. no fractional quantities of the Base Units are allowed.
Secondary units must be integer multiple of the indivisible Base Unit.
Examples
  TYPE Resistance IS Range 1 To Integer’High
  Units
  Ohm; -- Base Unit
  Kohm = 1000 Ohm; -- Secondary Unit
  Mohm = 1000 Kohm; -- Secondary Unit
  end Units ;

## Slide 44: Predefined Physical Data Types
Time is the ONLY predefined Physical data type
  TYPE Time IS Range 0 To 1E20
  Units
  fs; -- Base Unit (Femto Second = 1E-15 Second)
  ps = 1000 fs; -- Pico_Second
  ns = 1000 ps; -- Nano_Second
  us = 1000 ns; -- Micro_Second
  ms = 1000 us; -- Milli_Second
  sec = 1000 ms; -- Second
  min = 60 sec; -- Minuite
  hr = 60 min; -- Hour
  end Units ;

## Slide 45: Composite Data Types: Arrays
Elements of an Array have the same data type
Arrays may be Single/Multi - Dimensional
Array bounds may be either Constrained or Unconstrained.
Constrained Arrays
  Array Bounds Are Specified
  Syntax:
    TYPE id Is Array ( Range_Constraint) of Type;
Examples
  TYPE word Is Array ( 0 To 7) of Bit;
  TYPE pattern Is Array ( 31 DownTo 0) of Bit;
  2-D Arrays
    TYPE col Is Range 0 To 255;
    TYPE row Is Range 0 To 1023;
    TYPE Mem_Array Is Array (row, col) of Bit;
    TYPE Memory Is Array (row) of word;

## Slide 46: Unconstrained Arrays
Array Bounds not specified through using the notation RANGE<>
Type of each Dimension is specified, but the exact Range and Direction are not Specified.
Useful in Interface_Lists  Allows Dynamic Sizing of Entities, e.g. Registers.
Bounds of Unconstrained Arrays in such entities assume the Actual Array Sizes when wired to the Actual Signals.
Example
  TYPE Screen Is Array ( Integer Range<> , Integer Range<>) of BIT;

## Slide 47: Predefined Array Types
Two UNCONSTRAINED Array Types are predefined
BIT_VECTOR
  TYPE Bit_Vector Is Array ( Natural Range<> ) of Bit;
String
  TYPE String Is Array ( Positive Range<> ) of Character;
Example
  SUBTYPE Pixel Is Bit_Vector (7 DownTo 0);

## Slide 48: Use of Unconstrained Arrays
PROCEDURE apply_data (
SIGNAL target : OUT BIT_VECTOR;
CONSTANT values : IN integer_vector; CONSTANT period : IN TIME) IS
VARIABLE buf : BIT_VECTOR (target'RANGE);
BEGIN
FOR i IN values'RANGE LOOP
int2bin (values(i), buf);
target <= TRANSPORT buf AFTER i * period;
END LOOP;
END apply_data;
Example shows use of unconstrained arrays:
  target : BIT_VECTOR
  values : integer_vector
Use 'RANGE to look up passed range
Range will be determined when procedure is called
TYPE integer_vector IS ARRAY (NATURAL RANGE <>) of INTEGER;

## Slide 49: Unconstrained Comparator
ENTITY n_bit_comparator IS PORT (a, b : IN BIT_VECTOR; gt, eq, lt : IN BIT; a_gt_b, a_eq_b, a_lt_b : OUT BIT); END n_bit_comparator; -- ARCHITECTURE structural OF n_bit_comparator IS COMPONENT comp1 PORT (a, b, gt, eq, lt : IN BIT; a_gt_b, a_eq_b, a_lt_b : OUT BIT); END COMPONENT; FOR ALL : comp1 USE ENTITY WORK.bit_comparator (functional); CONSTANT n : INTEGER := a'LENGTH; SIGNAL im : BIT_VECTOR ( 0 TO (n-1)*3-1); BEGIN c_all: FOR i IN 0 TO n-1 GENERATE l: IF i = 0 GENERATE least: comp1 PORT MAP (a(i), b(i), gt, eq, lt, im(0), im(1), im(2) ); END GENERATE; m: IF i = n-1 GENERATE most: comp1 PORT MAP (a(i), b(i), im(i*3-3), im(i*3-2), im(i*3-1), a_gt_b, a_eq_b, a_lt_b); END GENERATE; r: IF i > 0 AND i < n-1 GENERATE rest: comp1 PORT MAP (a(i), b(i), im(i*3-3), im(i*3-2), im(i*3-1), im(i*3+0), im(i*3+1), im(i*3+2) ); END GENERATE; END GENERATE; END structural;
Size of input vectors are not specified
Comparator length is a'LENGTH
Size will be determined when instatntiated

## Slide 50: Unconstrained Comparator Test Bench
  ENTITY n_bit_comparator_test_bench IS
  END n_bit_comparator_test_bench ;
  --
  USE WORK.basic_utilities.ALL;
  -- FROM PACKAGE USE : apply_data which uses integer_vector
  ARCHITECTURE procedural OF n_bit_comparator_test_bench IS
  COMPONENT comp_n
  PORT (a, b : IN bit_vector; gt, eq, lt : IN BIT; a_gt_b, a_eq_b, a_lt_b : OUT BIT);
  END COMPONENT;
  FOR a1 : comp_n USE ENTITY WORK.n_bit_comparator(structural);
  SIGNAL a, b : BIT_VECTOR (5 DOWNTO 0);
  SIGNAL eql, lss, gtr : BIT;
  SIGNAL vdd : BIT := '1';
  SIGNAL gnd : BIT := '0';
  BEGIN
  a1: comp_n PORT MAP (a, b, gnd, vdd, gnd, gtr, eql, lss);
  apply_data (a, 00&15&57&17, 500 NS);
  apply_data (b, 00&43&14&45&11&21&44&11, 500 NS);
  END procedural;
SIGNAL a determines size of comparator
SIGNAL a determines target size of apply_data
SIGNAL b determines target size of apply_data
Concatenated integers form integer_vector

## Slide 51: Referencing Arrays & Array Elements …
VHDL allows referencing an Array in its Entirety or by a SLICE, or Element.
Examples
  TYPE clock_state IS (Low, Rising, High, Falling);
  TYPE Conversion_Array IS Array (Clock_state) of Bit;
  Signal C_A : Conversion_Array := (`0` , `1`, `0`, `1`) ;
  C_A <= (`1`, `1`, `0`, `0`); -- Positional Association List
  C_A <= (Low => `0`, Rising => `1`, High => `1`, Falling => `0`); -- Named Association List
  C_A <= (Low => `0`, High => `0`, OTHERS=> `1`); -- Alternative 3
  C_A(Low) <= `0`;
  TYPE Register4 IS Array (3 Downto 0) of Bit;
  TYPE Reg4 IS Array (0 To 3) of Bit;
  Signal A: Register4 := (`0` , `1`, `0`, `1`) ;--A(0)=`1`, A(3)=`0`
  Signal B: Reg4 := (`0` , `1`, `0`, `1`) ;--B(0)=`0`, B(3)=`1`

## Slide 52: … Referencing Arrays & Array Elements
2-D Arrays
  TYPE Reg32 Is Array (31 DownTo 0) of Bit;
  TYPE ROM Is Array (0 To 3) of Reg32;
  TYPE ROM2 Is Array (0 To 4 , 0 To 2) of Bit;
  Signal A: ROM := (X``2F3C_5456`` , X``FF32_E7B8`` , X``109A_BA15`` , X``FFFF_FFFF`` );
  Signal B: ROM2 := ( (`1`, `0`, `0`),
  (`0` , `1`, `0`),
  (`0` , `1`, `1`,
  (`1` , `0`, `1`),
  (`1` , `1`, `1`) ) ;
  B(1 , 2) <= `0` ; -- Referencing a 2-D Array Element

## Slide 53: File Type & External File I/O …
Specifying files is a two step process of
  File type declaration
  File declaration
Data is associated with an identifier that is defined as a file type.
File Type Declaration Example
  Type logic_data is FILE of Character;
File Declaration Examples
  FILE file1 : logic_data; -- file must be opened to be associated with a physical file
  FILE file2 : logic_data IS “Input.dat”;
  FILE file3 : logic_data OPEN READ_MODE IS “Input.dat”;
    File can be opened in READ_MODE, WRITE_MODE, APPEND_MODE

## Slide 54: … File Type & External File I/O …
  FILE file4 : logic_data OPEN WRITE_MODE IS “output.dat”;
Opening and Closing Files
  FILE_OPEN(file1, “input.dat”, READ_MODE);
  FILE_OPEN(file1, “output.dat”, WRITE_MODE);
  FILE_CLOSE(file1);
File Read and Write Operations
  VHDL provides three operations READ, WRITE and ENDFILE for file types
  READ takes an object of file data type as its argument, reads next data from file to its data argument
  WRITE takes an object of file data type as its argument, write next data from its data argument to file
  ENDFILE takes an object of file data type as its argument and returns TRUE if a subsequent read cannot be done

## Slide 55: …File Type & External File I/O …
Entity try is end try;
Architecture example of try IS
Type cfile is file of character;
File f1i, f1o : cfile;
Begin
process
variable char: character;
begin
-- opening files
FILE_OPEN (f1i, "f1i.txt", READ_MODE);
FILE_OPEN (f1o, "f1o.txt", WRITE_MODE);
while not endfile(f1i) loop
read (f1i, char); write (f1o, char);
end loop;
-- closing files
FILE_CLOSE (f1i); FILE_CLOSE (f1o);
wait;
end process;
End example;

## Slide 56: … File Type & External File I/O
  -- File Type logic_data is Visible
  PROCEDURE assign_bits (
  SIGNAL target : OUT BIT; file_name : IN STRING; period : IN TIME) IS
  VARIABLE char : CHARACTER;
  VARIABLE current : TIME := 0 NS;
  FILE input_value_file : logic_data IS file_name;
  BEGIN
  WHILE NOT ENDFILE (input_value_file) LOOP
  READ (input_value_file, char);
  IF char = '0' OR char = '1' THEN
  current := current + period;
  IF char = '0' THEN
  target <= TRANSPORT '0' AFTER current;
  ELSIF char = '1' THEN
  target <= TRANSPORT '1' AFTER current;
  END IF;
  END IF;
  END LOOP;
  END assign_bits;

## Slide 57: Formatted I/O …
USE STD.TEXTIO.ALL;
l is LINE, f is FILE
The following functions provided:
  READLINE (f, l)
  READ (l, v)
  WRITE (l, v),
  WRITELINE (f, l)
  ENDFILE (f)
READ or WRITE can read values of type:
  BIT, BIT_VECTOR, BOOLEAN, CHARACTER, INTEGER, REAL, STRING, TME

## Slide 58: … Formatted I/O …
USE STD.TEXTIO.ALL;
TYPE state IS (reset, got1, got10, got101);
TYPE state_vector IS ARRAY (NATURAL RANGE <>) OF state;
FUNCTION one_of (sources : state_vector) RETURN state IS
VARIABLE l : LINE;
FILE flush : TEXT IS OUT "/dev/tty";
BEGIN
FOR i IN sources'RANGE LOOP
WRITE (l, state’IMAGE(sources(I), LEFT, 7);
END LOOP;
WRITELINE (flush, l);
RETURN sources (sources'LEFT);
END one_of;
Add screen output to resolution function
The ‘IMAGE type attribute translates a state to its corresponding string
The keyword LEFT specifies left justification
7 specifies the string length

## Slide 59: … Formatted I/O
USE STD.TEXTIO.ALL;
PROCEDURE display (SIGNAL value1, value2 : BIT) IS
FILE flush : TEXT IS OUT "/dev/tty;
VARIABLE filler : STRING (1 TO 3) := " ..";
VARIABLE l : LINE;
BEGIN
WRITE (l, NOW, RIGHT, 8, NS);
IF value1'EVENT THEN
WRITE (l, value1, RIGHT, 3);
WRITE (l, filler, LEFT, 0);
ELSE
WRITE (l, filler, LEFT, 0);
WRITE (l, value2, RIGHT, 3);
END IF;
WRITELINE (flush, l);
END display;
An EVENT on value1 or value2 puts the following in l:
  NOW
An EVENT on value1 puts the following in l:
  v1 ...
An EVENT on value2 puts the following in l:
  ... v2
WRITELINE writes:
  time v1 ...
  time ... v2

## Slide 60: VHDL Synthesis Subset
VHDL is a complex language but only a subset of it is synthesizable.
Primary VDHL constructs used for synthesis:
  Constant definition
  Port map statement
  Signal assignment: A <= B
  Comparisons: = (equal), /= (not equal), > (greater than), < (less than), >= (greater than or equal), <= (less than or equal)
  Logical operators: AND, OR, NAND, NOR, XOR, XNOR, NOT
  'if' statement
    if ( presentstate = CHECK_CAR ) then ....
    end if | elsif ....
  'for' statement (used for looping in creating arrays of elements)
  Other constructs are ‘with’, ’when’, 'when else', 'case' . Also ":=" for variable assignment.

## Slide 61: Constant Definition…
library ieee;
use ieee.std_logic_1164.all;
entity constant_ex is
port (in1 : in std_logic_vector (7 downto 0); out1 : out std_logic_vector (7 downto 0));
end constant_ex;
architecture constant_ex_a of constant_ex is
constant A : std_logic_vector (7 downto 0) := "00000000";
constant B : std_logic_vector (7 downto 0) := "11111111";
constant C : std_logic_vector (7 downto 0) := "00001111";
begin
out1 <= A when in1 = B else C;
end constant_ex_a;

## Slide 62: …Constant Definition

## Slide 63: Port Map Statement…
library ieee;
use ieee.std_logic_1164.all;
entity sub is
port (a, b : in std_logic; c : out std_logic);
end sub;
architecture sub_a of sub is
begin
c <= a and b;
end sub_a;

## Slide 64: …Port Map Statement…
library ieee;
use ieee.std_logic_1164.all;
entity portmap_ex is
port (in1, in2, in3 : in std_logic; out1 : out std_logic);
end portmap_ex;
architecture portmap_ex_a of portmap_ex is
component sub
port (a, b : in std_logic; c : out std_logic);
end component;
signal temp : std_logic;
begin
u0 : sub port map (in1, in2, temp);
u1 : sub port map (temp, in3, out1);
end portmap_ex_a;

## Slide 65: When Statement
library ieee;
use ieee.std_logic_1164.all;
entity when_ex is
port (in1, in2 : in std_logic; out1 : out std_logic);
end when_ex;
architecture when_ex_a of when_ex is
begin
out1 <= '1' when in1 = '1' and in2 = '1' else '0';
end when_ex_a;

## Slide 66: With Statement
library ieee;
use ieee.std_logic_1164.all;
entity with_ex is
port (in1, in2 : in std_logic; out1 : out std_logic);
end with_ex;
architecture with_ex_a of with_ex is
begin
with in1 select out1 <= in2 when '1',
'0' when others;
end with_ex_a;

## Slide 67: Case Statement…
library ieee;
use ieee.std_logic_1164.all;
entity case_ex is
port (in1, in2 : in std_logic; out1,out2 : out std_logic);
end case_ex;
architecture case_ex_a of case_ex is
signal b : std_logic_vector (1 downto 0);
begin
process (b)
begin
case b is
when "00"|"11" => out1 <= '0'; out2 <= '1';
when others => out1 <= '1'; out2 <= '0';
end case;
end process;
b <= in1 & in2;
end case_ex_a;

## Slide 68: For Statement…
library ieee;
use ieee.std_logic_1164.all;
entity for_ex is
port (in1 : in std_logic_vector (3 downto 0); out1 : out std_logic_vector (3 downto 0));
end for_ex;
architecture for_ex_a of for_ex is
begin
process (in1)
begin
for0 : for i in 0 to 3 loop
out1 (i) <= not in1(i);
end loop;
end process;
end for_ex_a;

## Slide 69: Generate Statement
signal A, B : BIT_VECTOR (3 downto 0);
signal C : BIT_VECTOR (7 downto 0);
signal X : BIT;
. . .
GEN_LABEL:
for I in 3 downto 0 generate
C(2*I+1) <= A(I) nor X;
C(2*I) <= B(I) nor X;
end generate GEN_LABEL

## Slide 70: If Statement
library ieee;
use ieee.std_logic_1164.all;
entity if_ex is
port (in1, in2 : in std_logic; out1 : out std_logic);
end if_ex;
architecture if_ex_a of if_ex is
begin
process (in1, in2)
begin
if in1 = '1' and in2 = '1' then out1 <= '1';
else out1 <= '0';
end if;
end process;
end if_ex_a;

## Slide 71: Variable Definition…
library ieee;
use ieee.std_logic_1164.all;
entity variable_ex is
port ( a : in std_logic_vector (3 downto 0); b : in std_logic_vector (3 downto 0); c : out std_logic_vector (3 downto 0));
end variable_ex;
architecture variable_ex_a of variable_ex is
begin
process (a,b)
variable carry : std_logic_vector (4 downto 0);
variable sum : std_logic_vector (3 downto 0);

## Slide 72: …Variable Definition…
begin
carry (0) := '0';
for i in 0 to 3 loop
sum (i) := a(i) xor b(i) xor carry(i);
carry (i+1) := (a(i) and b(i)) or (b(i) and carry (i))
or (carry (i) and a(i));
end loop;
c <= sum;
end process;
end variable_ex_a;

## Slide 73: Ripple Carry Adder…
library ieee;
use ieee.std_logic_1164.all;
entity adder4 is
port (Signal a, b: in std_logic_vector (3 downto 0);
Signal cin : in std_logic_vector;
Signal sum: out std_logic_vector (3 downto 0);
Signal cout : in std_logic_vector);
end adder4;
architecture behavior of adder4 is
Signal c: std_logic_vector (4 downto 0);
begin
C is a temporary signal to hold the carries.

## Slide 74: …Ripple Carry Adder…
process (a, b, cin, c)
begin
c(0) <= cin;
for I in 0 to 3 loop
sum(I) <= a(I) xor b(I) xor c(I);
c(I+1) <= (a(I) and b(I)) or (c(I) and (a(I) or b(I)));
end loop;
end process;
cout <= c(4);
End behavior;

## Slide 75: Unsigned Division
library ieee;
use ieee.std_logic_1164.all;
use ieee.std_logic_signed.all;
entity DIV is
generic (N: integer :=4);
port (Q, R: out std_logic_vector (N-1 downto 0);
dividend, diviser: in std_logic_vector (N-1 downto 0));
end DIV;
architecture iterative of DIV is
begin
process (dividend, diviser)
variable i: integer;
variable diff: std_logic_vector (N-1 downto 0);

## Slide 76: Unsigned Division
variable HI: std_logic_vector (N-1 downto 0);
variable LO: std_logic_vector (N-1 downto 0);
begin
LO := dividend; HI := (others=>'0');
for i in 0 to N-1 loop
HI := HI(N-2 downto 0) & LO(N-1); LO := LO(N-2 downto 0) & '0';
diff := HI - diviser;
if( diff(N-1)='0' ) then
HI := diff; LO(0):= '1';
end if;
end loop;
Q <= LO;
R<=HI;
end process;
end iterative;

## Slide 77: Multiplexor Synthesis…
library ieee;
use ieee.std_logic_1164.all;
entity mux is
port (in1, in2, ctrl : in std_logic; out1 : out std_logic);
end mux;
architecture mux_a of mux is
begin
process (in1, in2, ctrl)
begin
if ctrl = '0' then out1 <= in1;
else out1 <= in2;
end if;
end process;
end mux_a;

## Slide 78: …Multiplexor Synthesis
entity mux2to1_8 is
port ( signal s: in std_logic; signal zero,one: in std_logic_vector(7 downto 0); signal y: out std_logic_vector(7 downto 0) );
end mux2to1_8;
architecture behavior of mux2to1 is
begin
y <= one when (s = '1') else zero;
end behavior;

## Slide 79: 2x1 Multiplexor using Booleans
architecture boolean_mux of mux2to1_8 is
signal temp: std_logic_vector(7 downto 0);
begin
temp <= (others => s);
y <= (temp and one) or (not temp and zero);
end boolean_mux;
The s signal cannot be used in a Boolean operation with the one or zero signals because of type mismatch (s is a std_logic type, one/zero are std_logic_vector types)
An internal signal of type std_logic_vector called temp is declared. The temp signal will be used in the Boolean operation against the zero/one signals.
Every bit of temp is set equal to the s signal value.

## Slide 80: 2x1 Multiplexor using a Process
architecture process_mux of mux2to1_8 is
begin
comb: process (s, zero, one)
begin
y <= zero;
if (s = '1') then
y <= one;
end if;
end process comb;
end process_mux ;

## Slide 81: Decoder Synthesis…
library ieee;
use ieee.std_logic_1164.all;
entity decoder is
port (in1, in2 : in std_logic; out00, out01, out10, out11 : out std_logic);
end decoder;
architecture decoder_a of decoder is
begin
process (in1, in2)
begin
if in1 = '0' and in2 = '0' then out00 <= '1';
else out00 <= '0';
end if;
if in1 = '0' and in2 = '1' then out01 <= '1';
else out01 <= '0';
end if;

## Slide 82: …Decoder Synthesis
if in1 = '1' and in2 = '0' then out10 <= '1';
else out10 <= '0';
end if;
if in1 = '1' and in2 = '1' then out11 <= '1';
else out11 <= '0';
end if;
end process;
end decoder_a;

## Slide 83: 3-to-8 Decoder Example…
entity dec3to8 is
port (signal sel: in std_logic_vector(2 downto 0); signal en: in std_logic; signal y: out std_logic_vector(7 downto 0))
end dec3to8;
architecture behavior of dec3to8 is
begin
process (sel, en)
y <= “00000000”;
if (en = ‘1’) then
case sel is
when “000” => y(0) <= ‘1’; when “001” => y(1) <= ‘1’;
when “010” => y(2) <= ‘1’; when “011” => y(3) <= ‘1’;
when “100” => y(4) <= ‘1’; when “101” => y(5) <= ‘1’;
when “110” => y(6) <= ‘1’; when “111” => y(7) <= ‘1’;
end case;
end if;
end process;
end behavior;

## Slide 84: Architecture of Generic Decoder
architecture behavior of generic_decoder is
begin
process (sel, en)
begin
y <= (others => ‘0') ;
for i in y'range loop
if ( en = '1' and bvtoi(To_Bitvector(sel)) = i ) then
y(i ) <= ‘1' ;
end if ;
end loop;
end process;
end behavior;
bvtoi is a function to convert from bit_vector to integer

## Slide 85: A Common Error in Process Statements…
When using processes, a common error is to forget to assign an output a default value.
  ALL outputs should have DEFAULT values
If there is a logical path in the model such that an output is not assigned any value
  the synthesizer will assume that the output must retain its current value
  a latch will be generated.
Example: In dec3to8.vhd do not assign 'y' the default value of "00000000"
  If en is 0, then 'y' will not be assigned a value
  In the new synthesized logic, all 'y' outputs are latched

## Slide 86: …A Common Error in Process Statements…
entity dec3to8 is
port (signal sel: in std_logic_vector(3 downto 0); signal en: in std_logic; signal y: out std_logic_vector(7 downto 0))
end dec3to8;
architecture behavior of dec3to8 is
begin
process (sel, en)
-- y <= “00000000”;
if (en = ‘1’) then
case sel is
when “000” => y(0) <= ‘1’; when “001” => y(1) <= ‘1’;
when “010” => y(2) <= ‘1’; when “011” => y(3) <= ‘1’;
when “100” => y(4) <= ‘1’; when “101” => y(5) <= ‘1’;
when “110” => y(6) <= ‘1’; when “111” => y(7) <= ‘01;
end case;
end if;
end process;
end behavior;
No default value assigned to y!!

## Slide 87: Another Incorrect Latch Insertion Example…
entity case_example is
port (in1, in2 : in std_logic; out1, out2 : out std_logic);
end case_example;
architecture case_latch of case_example is
signal b : std_logic_vector (1 downto 0);
begin
process (b)
begin
case b is
when "01" => out1 <= '0'; out2 <= '1';
when "10" => out1 <= '1'; out2 <= '0';
when others => out1 <= '1';
end case;
end process;
b <= in1 & in2;
end case_latch;
out2 has not been assigned a value for others condition!!

## Slide 88: …Another Incorrect Latch Insertion Example

## Slide 89: Avoiding Incorrect Latch Insertion
architecture case_nolatch of case_example is
signal b : std_logic_vector (1 downto 0);
begin
process (b)
begin
case b is
when "01" => out1 <= '0'; out2 <= '1';
when "10" => out1 <= '1'; out2 <= '0';
when others => out1 <= '1'; out2 <= '0';
end case;
end process;
b <= in1 & in2;
end case_nolatch;

## Slide 90: Eight-Level Priority Encoder…
Entity priority is
Port (Signal y1, y2, y3, y4, y5, y6, y7: in std_logic;
Signal vec: out std_logic_vector(2 downto 0));
End priority;
Architecture behavior of priority is
Begin
Process(y1, y2, y3, y4, y5, y6, y7)
begin
if (y7 = ‘1’) then vec <= “111”; elsif (y6 = ‘1’) then vec <= “110”;
elsif (y5 = ‘1’) then vec <= “101”; elsif (y4 = ‘1’) then vec <= “100”;
elsif (y3 = ‘1’) then vec <= “011”; elsif (y2 = ‘1’) then vec <= “010”;
elsif (y1= ‘1’) then vec <= “001”; else vec <= “000”;
end if;
end process;
End behavior;

## Slide 91: Eight-Level Priority Encoder…
Architecture behavior2 of priority is
Begin
Process(y1, y2, y3, y4, y5, y6, y7)
begin
vec <= “000”;
if (y1 = ‘1’) then vec <= “001”; end if;
if (y2 = ‘1’) then vec <= “010”; end if;
if (y3 = ‘1’) then vec <= “011”; end if;
if (y4 = ‘1’) then vec <= “100”; end if;
if (y5 = ‘1’) then vec <= “101”; end if;
if (y6 = ‘1’) then vec <= “110”; end if;
if (y7= ‘1’) then vec <= “111”; end if;
end process;
End behavior2;
Equivalent 8-level priority encoder.

## Slide 92: Tri-State Buffer Synthesis
library ieee;
use ieee.std_logic_1164.all;
entity tri_ex is
port (in1, control : in std_logic; out1 : out std_logic);
end tri_ex;
architecture tri_ex_a of tri_ex is
begin
out1 <= in1 when control = '1' else 'Z';
end tri_ex_a;

## Slide 93: Bi-directional Buffer Synthesis
library ieee;
use ieee.std_logic_1164.all;
entity inout_ex is
port (io1, io2 : inout std_logic; ctrl : in std_logic);
end inout_ex;
architecture inout_ex_a of inout_ex is
begin
io1 <= io2 when ctrl = '1' else 'Z';
io2 <= io1 when ctrl = '0' else 'Z';
end inout_ex_a;

## Slide 94: Latch Synthesis…
library ieee;
use ieee.std_logic_1164.all;
entity latch_ex is
port (clock, in1 : in std_logic; out1 : out std_logic);
end latch_ex;
architecture latch_ex_a of latch_ex is
begin
process (clock, in1)
begin
if (clock = '1') then
out1 <= in1;
end if;
end process;
end latch_ex_a;

## Slide 95: Flip-Flop Synthesis with Asynchronous Reset…
library ieee;
use ieee.std_logic_1164.all;
entity dff_asyn is
port( reset, clock, d: in std_logic; q: out std_logic);
end dff_asyn;
architecture dff_asyn_a of dff_asyn is
begin
process
begin
if (reset = '1') then
q <= '0';
elsif clock = '1' and clock'event then
q <= d;
end if;
end process;
end dff_asyn_a;
Note that the reset input has precedence over the clock in order to define the asynchronous operation.

## Slide 96: Flip-Flop Synthesis with Synchronous Reset…
library ieee;
use ieee.std_logic_1164.all;
entity dff_syn is
port( reset, clock, d: in std_logic; q: out std_logic);
end dff_syn;
architecture dff_syn_a of dff_syn is
begin
process
begin
if clock = '1' and clock'event then
if (reset = '1') then q <= '0';
else q <= d;
end if;
end if;
end process;
end dff_syn_a;

## Slide 97: 8-bit Loadable Register with Asynchronous Clear…
library ieee;
use ieee.std_logic_1164.all;
entity reg8bit is
port( reset, clock, load: in std_logic;
din: in std_logic_vector(7 downto 0);
dout: out std_logic_vector(7 downto 0));
end reg8bit;
architecture behavior of reg8bit is
signal n_state, p_state: std_logic_vector(7 downto 0);
begin
dout <= p_state;
comb: process (p_state, load, din)
begin
n_state <= p_state;
if (load = '1') then n_state <= din end if;
end process comb;

## Slide 98: …8-bit Loadable Register with Asynchronous Clear…
state: process (clk, reset)
begin
if (reset = ‘0') then p_state <= (others => '0‘);
elsif (clock = '1' and clock'event) then
p_state <= n_state;
end if;
end process state;
End behavior;
The state process defines a storage element which is 8-bits wide, rising edge triggered, and had a low true asynchronous reset.
Note that the reset input has precedence over the clock in order to define the asynchronous operation.

## Slide 99: 4-bit Shift Register…
library ieee;
use ieee.std_logic_1164.all;
entity shift4 is
port( reset, clock: in std_logic; din: in std_logic;
dout: out std_logic_vector(3 downto 0));
end shift4;
architecture behavior of shift4 is
signal n_state, p_state: std_logic_vector(3 downto 0);
begin
dout <= p_state;
state: process (clock, reset)
begin
if (reset = ‘0') then p_state <= (others => '0‘);
elsif (clock = '1' and clock'event) then
p_stateq <= n_state;
end if;
end process state;

## Slide 100: …4-bit Shift Register…
comb: process (p_state, din)
begin
n_state(0) <= din;
for I in 3 downto 1 loop
n_state(I) <= p_state(I-1);
end loop;
end process comb;
End behavior;
Serial input din is assigned to the D-input of the first D-FF.
For loop is used to connect the output of previous flip-flop to the input of current flip-flop.

## Slide 101: 4-bit Shift Register – Version 2
architecture behavior2 of shift4 is
signal p_state: std_logic_vector(3 downto 0);
begin
dout <= p_state;
state: process (clock, reset)
begin
if (reset = '0') then p_state <= (others => '0');
elsif (clock = '1' and clock'event) then
p_state(0) <= din;
for I in 3 downto 1 loop
p_state(I) <= p_state(I-1);
end loop;
end if;
end process state;
end behavior2;

## Slide 102: Register with Tri-State Output…
library ieee;
use ieee.std_logic_1164.all;
entity tsreg8bit is
port( reset, clock, load, en: in std_logic;
signal din: in std_logic_vector(7 downto 0);
signal dout: out std_logic_vector(7 downto 0));
end tsreg8bit;
architecture behavior of tsreg8bit is
signal n_state, p_state: std_logic_vector(7 downto 0);
begin
dout <= p_state when (en=‘1’) else “ZZZZZZZZ”;
comb: process (p_state, load, din)
begin
n_state <= p_state;
if (load = '1') then n_state <= din end if;
end process comb;
Z assignment used to specify tri-state capability.

## Slide 103: …Register with Tri-State Output…
state: process (clk, reset)
begin
if (reset = ‘0') then p_state <= (others => '0‘);
elsif (clock = '1' and clock'event) then
p_state <= n_state;
end if;
end process state;
End behavior;

## Slide 104: Sequential Circuits
Sequential circuits consist of both combinational logic and storage elements.
Sequential circuits can be
    Moore-type: outputs are a combinatorial function of Present State signals.
    Mealy-type: outputs are a combinatorial function of both Present State signals and primary inputs.
Combinational
Logic
FFs
^
Primary
Inputs
Primary
Outputs
CLK
Present State
Next State

## Slide 105: Template Model for a Sequential Circuit
entity model_name is
port ( list of inputs and outputs );
end model_name;
architecture behavior of model_name is
internal signal declarations
begin
-- the state process defines the storage elements
state: process ( sensitivity list -- clock, reset)
begin
vhdl statements for state elements
end process state;
-- the comb process defines the combinational logic
comb: process ( sensitivity list -- usually includes all inputs, current state)
begin
vhdl statements which specify combinational logic
end process comb;
end behavior;

## Slide 106: Finite State Machine Synthesis…
00
01
10
11
1/10
0/00
0/01
1/10
-/10
-/10
Reset=0
Mealy model
Single input, two outputs
Synchronous reset

## Slide 107: …Finite State Machine Synthesis…
library ieee;
use ieee.std_logic_1164.all;
entity state_ex is
port (in1, clock, reset : in std_logic; out1 :
out std_logic_vector (1 downto 0));
end state_ex;
architecture state_ex_a of state_ex is
signal cur_state, next_state : std_logic_vector (1 downto 0);
begin
process (clock)
begin
if clock = '1' and clock'event then
if reset = '0' then cur_state <= "00";
else cur_state <= next_state;
end if;
end if;
end process;

## Slide 108: …Finite State Machine Synthesis…
process (in1, cur_state)
begin
case cur_state is
when "00" => if in1 = '0' then next_state <= "10"; out1 <= "00";
else next_state <= "01"; out1 <= "10";
end if;
when "01" => if in1 = '0' then next_state <= cur_state;
out1 <= "01";
else next_state <= "10“; out1 <= "10";
end if;
when "10" => next_state <= "11"; out1 <= "10";
when "11" => next_state <= "00"; out1 <= "10";
when others => null;
end case;
end process;
end state_ex_a;

## Slide 109: Key Synthesis Facts
Synthesis ignores the after clause in signal assignment
  C <= A AND B after 10ns
  May cause mismatch between pre-synthesis and post-synthesis simulation if a non-zero value used
  The preferred coding style is to write signal assignments without the after clause.
If the process has a static sensitivity list, it is ignored by the synthesis tool.
Sensitivity list must contain all read signals
  Synthesis tool will generate a warning if this condition is not satisfied
  Results in mismatch between pre-synthesis and post-synthesis simulation

## Slide 110: Synthesis Static Sensitivity Rule
Original VHDL Code
Process(A, B)
Begin
D <= (A AND B) OR C;
End process;
Synthesis View of Original VHDL Code
Process(A, B, C)
Begin
D <= (A AND B) OR C;
End process;
A
B
C
D
A
B
C
D
Pre-Synthesis Simulation
Post-Synthesis Simulation

## Slide 111: Latch Inference & Synthesis Rules…
A latch is inferred to satisfy the VHDL fact that signals and process declared variables maintain their values until assigned new ones.
Latches are synthesized from if statements if all the following conditions are satisfied
  Conditional expressions are not completely specified
    An else clause is omitted
  Objects conditionally assigned in an if statement are not assigned a value before entering this if statement
  The VHDL attribute `EVENT is not present in the conditional if expression
If latches are not desired, then a value must be assigned to the target object under all conditions of an if statement (without the `EVENT attribute).

## Slide 112: …Latch Inference & Synthesis Rules
For a case statement, latches are synthesized when it satisfies all of the following conditions:
  An expression is not assigned to a VHDL object in every branch of a case statement
  VHDL objects assigned an expression in any case branch are not assigned a value before the case statement is entered.
Latches are synthesized whenever a for…loop statement satisfies all of the following conditions
  for…loop contains a next statement
  Objects assigned inside the for…loop are not assigned a value before entering the enclosing for…loop

## Slide 113: For…Loop Statement Latch Example
Process(Data_In, Copy_Enable)
Begin
for k in 7 downto 0 loop
next when Copy_Enable(k)=‘0’
Data_Out(k) <= Data_in(k);
end loop;
End process;
Data_In(k)
Copy_Enable(k)
Data_Out(k)
LATCH
Seven latches will be synthesized

## Slide 114: Flip-Flop Inference & Synthesis Rules…
Flip-flops are inferred by either
  Wait until….
    Wait on… is not supported by synthesis
    Wait for… is not supported by synthesis
  If statement containing `EVENT
Synthesis accepts any of the following functionally equivalent statements for inferring a FF
  Wait until Clock=‘1’;
  Wait until Clock`Event and Clock=‘1’;
  Wait until (not Clock`Stable) and Clock=‘1’;

## Slide 115: …Flip-Flop Inference & Synthesis Rules
Synthesis does not support the following Asynchronous description of set and reset signals
  Wait until (clock=‘1’) or (Reset=‘1’)
  Wait on Clock, Reset
When using a synthesizable wait statement only synchronous set and reset can be used.
If statement containing the VHDL attribute `EVENT cannot have an else or an elsif clause.