## Slide 1: COE 561 Digital System Design & Synthesis Architectural Synthesis
Dr. Aiman H. El-Maleh
Computer Engineering Department
King Fahd University of Petroleum & Minerals
[Adapted from slides of Prof. G. De Micheli: Synthesis & Optimization of Digital Circuits]

## Slide 2: Outline
Motivation
Dataflow graphs & Sequencing graphs
Resources
Synthesis in temporal domain: Scheduling
Synthesis in spatial domain: Binding
Scheduling Models
  Unconstrained scheduling
  Scheduling with timing constraints
  Scheduling with resource constraints
Algorithmic Solution to the Optimum Binding Problem
Register Binding Problem

## Slide 3: Synthesis
Transform behavioral into structural view.
Architectural-level synthesis
  Architectural abstraction level.
  Determine macroscopic structure.
  Example: major building blocks like adder, register, mux.
Logic-level synthesis
  Logic abstraction level.
  Determine microscopic structure.
  Example: logic gate interconnection.

## Slide 4: Synthesis and Optimization

## Slide 5: Architectural-Level Synthesis Motivation
Raise input abstraction level.
  Reduce specification of details.
  Extend designer base.
  Self-documenting design specifications.
  Ease modifications and extensions.
Reduce design time.
Explore and optimize macroscopic structure
  Series/parallel execution of operations.

## Slide 6: Architectural-Level Synthesis
Translate HDL models into sequencing graphs.
Behavioral-level optimization
  Optimize abstract models independently from the implementation parameters.
Architectural synthesis and optimization
  Create macroscopic structure
    data-path and control-unit.
  Consider area and delay information of the implementation.

## Slide 7: Dataflow Graphs …
Behavioral views of architectural models.
Useful to represent data-paths.
Graph
  Vertices = operations.
  Edges = dependencies.
Dependencies arise due
  Input to an operation is result of another operation.
  Serialization constraints in specification.
  Two tasks share the same resource.

## Slide 8: … Dataflow Graphs
Assumes the existence of variables who store information required and generated by operations.
Each variable has a lifetime which is the interval from birth to death.
Variable birth is the time at which the value is generated.
Variable death is the latest time at which the value is referenced as input to an operation.
Values must be preserved during life-time.

## Slide 9: Sequencing Graphs
Useful to represent data-path and control.
Extended dataflow graphs
  Control Data Flow Graphs (CDFGs).
  Polar: source and sink.
  Operation serialization.
  Hierarchy.
  Control-flow commands
    branching and iteration.
Paths in the graph represent concurrent streams of operations.

## Slide 10: Behavioral-Level Optimization
Tree-height reduction using commutativity and associativity
x = a + b * c + d => x = (a + d) + b * c
Tree-height reduction using distributivity
x = a * (b * c * d + e) => x = a * b * c * d + a * e

## Slide 11: Architectural Synthesis and Optimization
Synthesize macroscopic structure in terms of building-blocks.
Explore area/performance trade-offs
  maximum performance implementations subject to area constraints.
  minimum area implementations subject to performance constraints.
Determine an optimal implementation.
Create logic model for data-path and control.

## Slide 12: Circuit Specification for Architectural Synthesis
Circuit behavior
  Sequencing graphs.
Building blocks
  Resources.
    Functional resources: process data (e.g. ALU).
    Memory resources: store data (e.g. Register).
    Interface resources: support data transfer (e.g. MUX and Buses).
Constraints
  Interface constraints
    Format and timing of I/O data transfers.
  Implementation constraints
    Timing and resource usage.
      Area
      Cycle-time and latency

## Slide 13: Resources
Functional resources: perform operations on data.
  Example: arithmetic and logic blocks.
  Standard resources
    Existing macro-cells.
    Well characterized (area/delay).
    Example: adders, multipliers, ALUs, Shifters, ...
  Application-specific resources
    Circuits for specific tasks.
    Yet to be synthesized.
    Example: instruction decoder.
Memory resources: store data.
  Example: memory and registers.
Interface resources
  Example: busses and ports.

## Slide 14: Resources and Circuit Families
Resource-dominated circuits
  Area and performance depend on few, well-characterized blocks.
  Example: DSP circuits.
Non resource-dominated circuits
  Area and performance are strongly influenced by sparse logic, control and wiring.
  Example: some ASIC circuits.

## Slide 15: Synthesis in the Temporal Domain: Scheduling
Scheduling
  Associate a start-time with each operation.
  Satisfying all the sequencing (timing and resource) constraints.
Goal
  Determine area/latency trade-off.
  Determine latency and parallelism of the implementation.
Scheduled sequencing graph
  Sequencing graph with start-time annotation.
Unconstrained scheduling.
Scheduling with timing constraints.
Scheduling with resource constraints.

## Slide 16: Scheduling …
4 Multipliers, 2 ALUs
1 Multiplier , 1 ALU

## Slide 17: … Scheduling
2 Multipliers, 3 ALUs
2 Multipliers, 2 ALUs

## Slide 18: Synthesis in the Spatial Domain: Binding
Binding
  Associate a resource with each operation with the same type.
  Determine area of the implementation.
Sharing
  Bind a resource to more than one operation.
  Operations must not execute concurrently.
Bound sequencing graph
  Sequencing graph with resource annotation.

## Slide 19: Example: Bound Sequencing Graph

## Slide 20: Performance and Area Estimation
Resource-dominated circuits
  Area = sum of the area of the resources bound to the operations.
    Determined by binding.
  Latency = start time of the sink operation (minus start time of the source operation).
    Determined by scheduling
Non resource-dominated circuits
  Area also affected by
    registers, steering logic, wiring and control.
  Cycle-time also affected by
    steering logic, wiring and (possibly) control.

## Slide 21: Scheduling
Circuit model
  Sequencing graph.
  Cycle-time is given.
  Operation delays expressed in cycles.
Scheduling
  Determine the start times for the operations.
  Satisfying all sequencing (timing and resource) constraints.
Goal
  Determine area/latency trade-off.
Scheduling affects
  Area: maximum number of concurrent operations of same type is a lower bound on required hardware resources.
  Performance: concurrency of resulting implementation.

## Slide 22: Scheduling Models
Unconstrained scheduling.
Scheduling with timing constraints
  Latency.
  Detailed timing constraints.
Scheduling with resource constraints.
Simplest scheduling model
  All operations have bounded delays.
  All delays are in cycles.
    Cycle-time is given.
  No constraints - no bounds on area.
  Goal
    Minimize latency.

## Slide 23: Minimum-Latency Unconstrained Scheduling Problem
Given a set of operations V with integer delays D and a partial order on the operations E
Find an integer labeling of the operations  : V  Z+, such that
  ti = (vi),
  ti  tj + dj  i, j s.t. (vj, vi)  E
  and tn is minimum.
Unconstrained scheduling used when
  Dedicated resources are used.
  Operations differ in type.
  Operations cost is marginal when compared to that of steering logic, registers, wiring, and control logic.
  Binding is done before scheduling: resource conflicts solved by serializing operations sharing same resource.
  Deriving bounds on latency for constrained problems.

## Slide 24: ASAP Scheduling Algorithm
Denote by ts the start times computed by the as soon as possible (ASAP) algorithm.
Yields minimum values of start times.

## Slide 25: ALAP Scheduling Algorithm
Denote by tL the start times computed by the as late as possible (ALAP) algorithm.
Yields maximum values of start times.
Latency upper bound 

## Slide 26: Latency-Constrained Scheduling
ALAP solves a latency-constrained problem.
Latency bound can be set to latency computed by ASAP algorithm.
Mobility
  Defined for each operation.
  Difference between ALAP and ASAP schedule.
  Zero mobility implies that an operation can be started only at one given time step.
  Mobility greater than 0 measures span of time interval in which an operation may start.
Slack on the start time.

## Slide 27: Example
Operations with zero mobility
  {v1, v2, v3, v4, v5}.
  Critical path.
Operations with mobility one
  {v6, v7}.
Operations with mobility two
  {v8, v9, v10, v11}

## Slide 28: Scheduling under Resource Constraints
Classical scheduling problem.
  Fix area bound - minimize latency.
The amount of available resources affects the achievable latency.
Dual problem
  Fix latency bound - minimize resources.
Assumption
  All delays bounded and known.

## Slide 29: Minimum Latency Resource-Constrained Scheduling Problem
Given a set of ops V with integer delays D, a partial order on the operations E, and upper bounds {ak; k = 1, 2, … , nres}
Find an integer labeling of the operations  : V  Z+, such that
  ti = (vi),
  ti  tj + dj  i, j s.t. (vj, vi)  E
  and tn is minimum.
Number of operations of any given type in any schedule step does not exceed bound.
:V{1,2, …nres}

## Slide 30: Scheduling under Resource Constraints
Intractable problem.
Algorithms
  Exact
    Integer linear program.
    Hu (restrictive assumptions).
  Approximate
    List scheduling.
    Force-directed scheduling.

## Slide 31: ILP Formulation …
Binary decision variables
  X = { xil ; i = 1, 2, … , n; l = 1, 2, … , +1}.
  xil, is TRUE only when operation vi starts in step l of the schedule (i.e. l = ti).
   is an upper bound on latency.
Start time of operation vi
Operations start only once
ti =

## Slide 32: … ILP Formulation …
Sequencing relations must be satisfied
Resource bounds must be satisfied

## Slide 33: … ILP Formulation
Minimize cT t such that
cT=[0,0,…,0,1]T corresponds to minimizing the latency of the schedule.
cT=[1,1,…,1,1]T corresponds to finding the earliest start times of all operations under the given constraints.

## Slide 34: Example …
Resource constraints
  2 ALUs; 2 Multipliers.
  a1 = 2; a2 = 2.
Single-cycle operation.
  di = 1 i.
Operations start only once
  x0,1=1; x1,1=1; x2,1=1; x3,2=1
  x4,3=1; x5,4=1
  x6,1+ x6,2=1
  x7,2+ x7,3=1
  x8,1+ x8,2+x8,3=1
  x9,2+ x9,3+x9,4=1
  x10,1+ x10,2+x10,3=1
  x11,2+ x11,3+x11,4=1
  xn,5=1

## Slide 35: … Example …
Sequencing relations must be satisfied
  2x3,2-x1,1 1
  2x3,2-x2,1 1
  2x7,2+3x7,3-x6,1-2x6,2 1
  2x9,2+3x9,3+4x9,4-x8,1-2x8,2-3x8,3 1
  2x11,2+3x11,3+4x11,4-x10,1-2x10,2 -3x10,3 1
  4x5,4-2x7,2-3x7,3 1
  4x5,4-3x4,3 1
  5xn,5-2x9,2-3x9,3-4x9,4 1
  5xn,5-2x11,2-3x11,3-4x11,4 1
  5xn,5-4x5,4 1

## Slide 36: … Example
Resource bounds must be satisfied:
Any set of start times satisfying constraints provides a feasible solution.
Any feasible solution is optimum since sink (xn,5=1) mobility is 0.

## Slide 37: Dual ILP Formulation
Minimize resource usage under latency constraint.
Same constraints as previous formulation.
Additional constraint
  Latency bound must be satisfied.
Resource usage is unknown in the constraints.
Resource usage is the objective to minimize.
  Minimize cT a
    a vector represents resource usage
    cT vector represents resource costs

## Slide 38: Example
Multiplier area = 5; ALU area = 1.
Objective function: 5a1 +a2.  = 4
Start time constraints same.
Sequencing dependency constraints same.
Resource constraints
  x1,1+x2,1+x6,1+x8,1 – a1  0
  x3,2+x6,2+x7,2+x8,2 – a1  0
  x7,3+x8,3 – a1  0
  x10,1 – a2  0
  x9,2+x10,2+x11,2 – a2  0
  x4,3+x9,3+x10,3+x11,3– a2  0
  x5,4+x9,4+x11,4– a2  0

## Slide 39: ILP Solution
Use standard ILP packages.
Transform into LP problem [Gebotys].
Advantages
  Exact method.
  Other constraints can be incorporated easily
    Maximum and minimum timing constraints
Disadvantages
  Works well up to few thousand variables.

## Slide 40: List Scheduling Algorithms
Heuristic method for
  Minimum latency subject to resource bound.
  Minimum resource subject to latency bound.
Greedy strategy.
Priority list heuristics.
  Assign a weight to each vertex indicating its scheduling priority
    Longest path to sink.
    Longest path to timing constraint.

## Slide 41: List Scheduling Algorithm for Minimum Latency …

## Slide 42: … List Scheduling Algorithm for Minimum Latency
Candidate Operations Ul,k
  Operations of type k whose predecessors are scheduled and completed at time step before l
Unfinished operations Tl,k are operations of type k that started at earlier cycles and whose execution is not finished at time l
  Note that when execution delays are 1, Tl,k is empty.

## Slide 43: Example
Assumptions
  a1 = 2 multipliers with delay 1.
  a2 = 2 ALUs with delay 1.
First Step
  U1,1 = {v1, v2, v6, v8}
  Select {v1, v2}
  U1,2 = {v10}; selected
Second step
  U2,1 = {v3, v6, v8}
  select {v3, v6}
  U2,2 = {v11}; selected
Third step
  U3,1 = {v7, v8}
  Select {v7, v8}
  U3,2 = {v4}; selected
Fourth step
  U4,2 = {v5, v9}; selected

## Slide 44: Example
Assumptions
  a1 = 3 multipliers with delay 2.
  a2 = 1 ALU with delay 1.

## Slide 45: List Scheduling Algorithm for Minimum Resource Usage

## Slide 46: Example
Assume =4
Let a = [1, 1]T
First Step
  U1,1 = {v1, v2, v6, v8}
  Operations with zero slack {v1, v2}
  a = [2, 1]T
  U1,2 = {v10}
Second step
  U2,1 = {v3, v6, v8}
  Operations with zero slack {v3, v6}
  U2,2 = {v11}
Third step
  U3,1 = {v7, v8}
  Operations with zero slack {v7, v8}
  U3,2 = {v4}
Fourth step
  U4,2 = {v5, v9}
  Both have zero slack; a = [2, 2]T

## Slide 47: Allocation and Binding
Allocation
  Determine number of resources needed
Binding
  Mapping between operations and resources.
Sharing
  Assignment of a resource to more than one operation.
Optimum binding/sharing
  Minimize the resource usage.

## Slide 48: Optimum Sharing Problem
Scheduled sequencing graphs.
  Operation concurrency well defined.
Consider operation types independently.
  Problem decomposition.
  Perform analysis for each resource type.
Minimize resource usage.

## Slide 49: Compatibility and Conflicts
Operation compatibility
  Same resource type.
  Non concurrent.
Compatibility graph
  Vertices: operations.
  Edges: compatibility relation.
Conflict graph
  Complement of compatibility graph.
Multiplier
ALU
Compatibility
graphs

## Slide 50: Algorithmic Solution to the Optimum Binding Problem
Compatibility graph.
  Partition the graph into a minimum number of cliques.
  Find clique cover number.
Conflict graph.
  Color the vertices by a minimum number of colors.
  Find chromatic number.
NP-complete problems - Heuristic algorithms.

## Slide 51: Example
ALU1: 1, 3, 5
ALU2: 2, 4
1
2
3
4
5
1
3
5
2
4

## Slide 52: ILP Formulation of Binding
Boolean variables bir
  Operation i bound to resource r.
Boolean variables xil
  Operation i scheduled to start at step l.
Each operation vi should be assigned to one resource
At most, one operation can be executing, among those assigned to resource r, at any time step

## Slide 53: Example…
Operation types: Multiplier, ALU
Unit execution delay
A feasible binding satisfies constraints

## Slide 54: … Example
Constants in X are 0 except x1,1, x2,1, x3,2, x4,3, x5,4, x6,2, x7,3, x8,3, x9,4, x10,1, x11,2.
An implementation with a1=2 multipliers:
Solutions
  b1,1=1, b2,2=1, b3,1=1, b6,2=1, b7,1=1, b8,2=1.

## Slide 55: Register Binding Problem
Given a schedule
  Lifetime intervals for variables.
  Lifetime overlaps.
Conflict graph (interval graph).
  Vertices  variables.
  Edges  overlaps.
Find minimum number of registers storing all the variables.
Compatibility graph.

## Slide 56: Example
Six intermediate variables that need to be stored in registers {z1, z2, z3, z4, z5, z6}
Six variables can be stored in two registers

## Slide 57: Example
7 intermediate variables, 3 loop variables, 3 loop invariants
5 registers suffice to store 10 intermediate loop variables

## Slide 58: Sharing and Binding for General Circuits
Area and delay influenced by
  Steering logic, wiring, registers and control circuit.
  E.g. multiplexers area and propagation delays depend on number of inputs.
  Wire lengths can be derived from statistical models.
Binding affects the cycle-time
  It may invalidate a schedule.
Control unit is affected marginally by resource binding.

## Slide 59: Left-Edge Algorithm
Input
  Set of intervals with left and right edge.
Rationale
  Sort intervals by left edge.
  Assign non-overlapping intervals to first color using the sorted list.
  When possible intervals are exhausted increase color counter and repeat.

## Slide 60: Example

## Slide 61: Example
It is required to design a circuit to compute the equation Y=A+B+C+D+E+F, where A, B, C, D, E and F are 4-bit inputs representing unsigned numbers. Assume that inputs are available only during the first cycle when a Start signal is asserted. Assume that a Done signal will be set when the result is ready and the result will remain held until the next Start operation. Assume that the clock cycle delay is constrained by the delay of the adder.
Show a schedule of the operations with minimum latency (i.e., clock cycles) satisfying the area constraint of using a maximum of two adders. Store the output Y in a register.

## Slide 62: Example

## Slide 63: Example
Show the DataPath design of your circuit indicating all the control signals and the used adder sizes.

## Slide 64: Example
Show the ASMD diagram of your control unit.

## Slide 65: Example
Consider the network given below with inputs {a, b, c, d} and output {y}:
[1]=b+c; [2]=a+b; [3]=b+d; [4]=a+[3];
[5]=[1]+[3]; [6]=[2]+[4]; y=[5]+[6];
Assume that the delay of an Adder fits within one clock cycle.

## Slide 66: Example
Schedule the sequencing graph into the minimum number of cycles under the resource constraints of two Adders

## Slide 67: Example
Datapath