Jan. 6, 2006

COMPUTER ENGINEERING DEPARTMENT

COE 561

Digital System Design and Synthesis

MAJOR EXAM II

(Open Book Exam)

First Semester (061)

Time: 7:30-9:30 PM

Student Name : ______________________________________________

Student ID.     : ______________________________________________

| Question | Max Points | Score |
| --- | --- | --- |
| Q1 | 30 |  |
| Q2 | 25 |  |
| Q3 | 20 |  |
| Q4 | 25 |  |
| Total | 100 |  |

# [30 Points]

# (Q1) Consider the function F(A, B, C, D) with ON-SET=(m(0, 2, 3, 7, 10) and DC-SET=(m(1, 6, 8, 14). Note that you do not need to use the positional-cube notation in your solution.

## Expand the minterm AB’CD’ using ESPRESSO heuristics.

## A cover of the function is given by F = A’C + B’ D’. Reduce the cube A’C using Theorem 7.4.1.

## Use Corollary 7.4.1 to check if the implicant A’C is an essential prime implicant.

# [25 Points]

# (Q2)  Consider the logic network defined by the following expressions:

# x = a b d + b' c d + c e + d e

# y = a' b d' + b’ c’ d’ + a’ c’ d' +  c’ d’ e

## (i) Using the procedure KERNELS, compute all the kernels and co-kernels of x. Show all the steps of the algorithm. Assume the following lexicographic order: {a, b, b’, c, d, e}.

## (ii) Compute the double-cube divisors of x and y and compute the weight of each double-cube divisor taking into account the combination of all divisors of x and y. Extract the best double-cube divisor and show the resulting network.

# [20 Points]

# (Q3)  Consider the logic network defined by the following expressions:

# c=a’

# x=a . b

# y =a (  b

# w = x +  y’ +  c’

# Inputs are {a, b} and output is w.

# (i) Compute the CDC set for the cut {x, y, c}. Simplify the equation of w to the minimum number of literals possible.

## (ii) Compute ODC set for node x. Based on the ODC set of node x, decide if the fault x stuck-at-0 is testable or not. If it is testable, find all tests detecting the fault. If it is untestable, optimize the network by eliminating redundancy.

[25 Points]

# (Q4) Consider the logic network defined by the following expressions:

# k=a . b

# l =a . c

# h = a + c

# e = a’ + b

# g = k + l

# f =d’ . g

# i = f (  d

# x= e (  i

# j =f + d

# y =j + h

# Inputs are {a, b, c, d} and outputs are {x, y}.  Assume that the delay of each inverter, AND and OR gates is 1 and that the delay of each XOR gate is 2. Also, assume that the input data-ready times are zero except for input a, which is equal to 2.

# (i) Draw the logic network graph and compute the data ready times and slacks for all vertices in the network.

## (ii) Determine the maximum propagation delay and the topological critical path.

## (iii) Suggest an implementation of the function g in terms of the Inputs {a, b, c} to reduce the delay of the circuit. What is the maximum propagation delay after the modified implementation?