Jan. 15, 2008

COMPUTER ENGINEERING DEPARTMENT

COE 561

Digital System Design and Synthesis

MAJOR EXAM II

(Open Book Exam)

First Semester (081)

Time: 12:00-2:30 PM

Student Name : __KEY________________________________________

Student ID.     : ______________________________________________

| Question | Max Points | Score |
| --- | --- | --- |
| Q1 | 30 |  |
| Q2 | 15 |  |
| Q3 | 15 |  |
| Q4 | 20 |  |
| Q5 | 20 |  |
| Total | 100 |  |

# [30 Points]

# (Q1) Consider the function F(A, B, C, D) with ON-SET=(m(3, 4, 5, 7) and OFF-SET=(m(1, 9, 10, 14). Note that you do not need to use the positional-cube notation in your solution.

## Expand the minterm A'BC'D’ using ESPRESSO heuristics.

## A cover of the function is given by F = A’B + A’C. Reduce the cube A’C using Theorem 7.4.1.

## Use Corollary 7.4.1 to check if the implicant A’C is an essential prime implicant.

# [15 Points]

# (Q2)  Consider the logic network defined by the following expression:

# x = a b d e f + a c d e f + a b d e g + a c d e g

## Using the recursive procedure KERNELS, compute all the kernels and co-kernels of x. Show all the steps of the algorithm. Assume the following lexicographic order: {a, b, c, d, e, f, g}

# [15 Points]

# (Q3)  Consider the logic network defined by the following expression:

# x = a b d' e'  + a' c' d' e' + a b' d  + a b' e + a' c d + a' c e

## Compute the weight of the double cube divisors d1 = a b + a' c' and d2 = d + e. Extract the double cube divisor with the highest weight and show the resulting network after extraction and the number of literals saved.

# [20 Points]

# (Q4)  Consider the logic network defined by the following expressions with inputs {a, b, c} and output {y}:

# w = b' c a' + b c'

# x = w (  c

# y = w b + w a + x

## Simplify the function x based on the utilization of don't care conditions.

## Based on perturbation analysis, determine if it is possible to change the implementation of w to w=b + c.

[20 Points]

# (Q5) Consider the logic network below with inputs {a, b, c, d, e} and output {k}:

# Assume that the delay of the inverter gate is 1 and that the delay of the 2-input NAND gate is 2.  Also, assume that the input data-ready times are zero except for input a, which is equal to 2.

## Compute the data ready times and slacks for all vertices in the network.

## Determine the topological critical path.

## Suggest an implementation of the function k using only inverters and 2-input NAND gates to reduce the delay of the circuit to the minimum possible and determine the maximum propagation delay in the optimized circuit. Has the area been affected?