## Slide 1: COE 202: Digital Logic Design Number Systems Part 2
Courtesy of Dr. Ahmad Almulhem

## Slide 2: Objectives
Base Conversion
  Decimal to other bases
  Binary to Octal and Hexadecimal
  Any base to any base
Arithmetic operations:
  Binary number system
  Other number systems

## Slide 3: Objectives
Base Conversion
  Decimal to other bases
  Binary to Octal and Hexadecimal
  Any base to any base
Arithmetic operations:
  Binary number system
  Other number systems

## Slide 4: Converting Decimal Integers to Binary
Divide the decimal number by ‘2’
Repeat division until a quotient of ‘0’ is received
The sequence of remainders in reverse order constitute the binary conversion
Example:
(41)10 = (101001)2
Remainder = 1
Remainder = 0
Remainder = 0
Remainder = 1
Remainder = 0
Remainder = 1
Verify: 1 x 25 + 0 x 24 + 1 x 23 + 0 x 22 + 0 x 21 + 1 x 20 = (41)10
LSB
MSB

## Slide 5: Decimal to binary conversion chart

## Slide 6: Converting Decimal Integer to Octal
Divide the decimal number by ‘8’
Repeat division until a quotient of ‘0’ is received
The sequence of remainders in reverse order constitute the binary conversion
Example:
(153)10 = (231)8
Remainder = 1
Remainder = 3
Remainder = 2
Verify: 2x82 + 3 x 81 + 1 x 80 = (153)10
LSB
MSB

## Slide 7: Converting Decimal Integer to Hexadecimal
Divide the decimal number by ‘16’
Repeat division until a quotient of ‘0’ is received
The sequence of remainders in reverse order constitute the binary conversion
Example:
(156)10 = (9C)16
Remainder = (12)10
 (C)16
Remainder = 9
Verify: 9 x 161 + 12 x 160 = (156)10
LSB
MSB

## Slide 8: Converting Decimal Fraction to Binary
Multiply the decimal number by ‘2’
Repeat multiplication until a fraction value of ‘0.0’ is reached or until the desired level of accuracy is reached
The sequence of integers before the decimal point constitute the binary number
Example:
(0.6875)10 = (0.1011)2
Verify: 1x2-1 + 0 x 2-2 + 1 x 2-3 + 1 x 2-4 = (0.6875)10
MSB
LSB
0.6875 x 2 = 1.3750
0.3750 x 2 = 0.7500
0.7500 x 2 = 1.5000
0.5000 x 2 = 1.0000
0.0000

## Slide 9: Converting Decimal Fraction to Octal
Multiply the decimal number by ‘8’
Repeat multiplication until a fraction value of ‘0.0’ is reached or until the desired level of accuracy is reached
The sequence of integers before the decimal point constitute the octal number
Example:
(0.513)10 = (0.4065…)8
Verify: 4x8-1 + 0 x 8-2 + 6 x 8-3 + 5 x 8-4 = (0.513)10
MSB
LSB
0.513 x 8 = 4.104
0.104 x 8 = 0.832
0.832 x 8 = 6.656
0.656 x 8 = 5.248
. . . .

## Slide 10: Converting Decimal Fraction to Hexadecimal
Multiply the decimal number by ‘16’
Repeat multiplication until a fraction value of ‘0.0’ is reached or until the desired level of accuracy is reached
The sequence of integers before the decimal point constitute the octal number
Example:
(0.513)10 = (0.8353…)16
Verify: 8x16-1 + 3 x 16-2 + 5 x 16-3 + 3 x 16-4 = (0.51299)10
MSB
LSB
0.513 x 16 = 8.208
0.208 x 16 = 3.328
0.328 x 16 = 5.248
0.248 x 16 = 3.968
. . . .

## Slide 11: Converting Integer & Fraction
Q. How to convert a decimal number that has both integral and fractional parts?
A. Convert each part separately, combine the two results with a point in between.
Example: Consider the “decimal -> octal” examples
in previous slides
(153.513)10 = (231.407)8

## Slide 12: Example
Convert (211.6250)10 to binary?
Steps:
  Split the number into integer and fraction
  Perform the conversions for the integer and fraction part separately
  Rejoin the results after the individual conversions

## Slide 13: Example (cont.)
Remainder = 1
Remainder = 1
Remainder = 0
Remainder = 0
Remainder = 1
Remainder = 0
Remainder = 1
Remainder = 1
MSB
LSB
(211.6250)10 = (11010011.101)2
Combining the results gives us:
Integer part
fraction part

## Slide 14: Converting Binary to Octal
Group 3 bits at a time
Pad with 0s if needed
Example: (11001.11)2 = (011 001.110)2 = (31.6)8
3 1 6

## Slide 15: Converting Binary to Hexadecimal
Group 4 bits at a time
Pad with 0s if needed
Example: (11001.11)2 = (0001 1001.1100)2 = (19.C)16
1 9 C

## Slide 16: Converting between other bases
Exercise: (13)4 = ( ? )6 ?
Q. How to convert between bases other than decimal; e.g from base-4 to base-6?
Two steps:
  1. convert source base to decimal
  2. convert decimal to destination base.

## Slide 17: Converting between other bases
Exercise: (13)4 = ( ? )6 ? Answer: (13)4 = (11)6
Q. How to convert between bases other than decimal; e.g from base-4 to base-6?
Two steps:
  1. convert source base to decimal
  2. convert decimal to destination base.

## Slide 18: Converting Hexadecimal to Octal (special case)
In this case, we can use binary as an intermediate step instead of decimal
Example:
  (3A)16 = (0011-1010)2 = (000-111-010)2 = (072)8
re-group by 3
0 added

## Slide 19: Converting Octal to Hexadecimal (special case)
In this case, we can use binary as an intermediate step instead of decimal
Example:
  (72)8 = (111-010)2 = (0011-1010)2 = (3A)16
re-group by 4
2 0s added

## Slide 20: Objectives
Base Conversion
  Decimal to other bases
  Binary to Octal and Hexadecimal
  Any base to any base
Arithmetic operations:
  Binary number system
  Other number systems

## Slide 21: Arithmetic Operation in base-r
Arithmetic operations with numbers in base-r follow the same rules as for decimal numbers
Be careful !
  Only r allowed digits

## Slide 22: Binary Addition
One bit addition:
0 0 1 1
+ 0 + 1 + 0 + 1
----- ------ ------ ------
0 1 1 2
1 0
2 doesn’t exist in binary!
carry
augend /aw-jend/
addend
sum

## Slide 23: Binary Addition (cont.)
Example:
1 1 1 1
1 1 0 0 0 0 1 1 1 1
+ 0 1 1 1 1 0 1 0 1 0
--------------------------
1 0 0 1 1 1 1 1 0 0 1
carries
sum
Q: How to verify?
A: Convert to decimal
783
+ 490
-----------
1273

## Slide 24: Binary Subtraction
In binary addition, there is a sum and a carry.
In binary subtraction, there is a difference and a borrow
Note: 0 – 1 = 1 borrow 1
One bit subtraction:
0 0 1 1
- 0 - 1 - 0 - 1
----- ------ ------ ------
0 1 1 0
borrow 1
minuend /men-u-end/
subtrahend /sub-tra-hend/
difference

## Slide 25: Binary Subtraction (cont.)
Subtract 101 - 011
1
0 1 0 1
- 0 1 1
--------------------------
0 1 0
borrow
difference
Larger binary numbers
1 1 1 1
1 1 0 0 0 0 1 1 1 1
- 0 1 1 1 1 0 1 0 1 0
--------------------------
0 1 0 0 1 0 0 1 0 1
borrow
In Decimal subtraction, the borrow is equal to 10.
In Binary, the borrow is equal to 2. Therefore, a ‘1’ borrowed in binary will generate a (10)2, which equals to (2)10 in decimal
Verify In decimal,
783
- 490
---------
293
difference

## Slide 26: Binary Subtraction (cont.)
Subtract (11110)2 from (10011)2
00110  borrow
10011 11110
- 11110 - 10011
----------- -----------
- 01011 01011
Note that
  (10011)2 is smaller than (11110)2  result is negative
negative sign

## Slide 27: Binary Multiplication
Multiply 1011 with 101:
1 0 1 1
x 1 0 1
-----------------
1 0 1 1
0 0 0 0
1 0 1 1
------------------------
1 1 0 1 1 1
product
Rules (short cut):
A ‘1’ digit in the multiplier implies a simple copy of the multiplicand
A ‘0’ digit in the multiplier implies a shift left operation with all 0’s
multiplier
multiplicand

## Slide 28: Hexadecimal addition
Add (59F)16 and (E46)16
5 9 F F + 6 = (21)10 = (16 x 1) + 5 = (15)16
+ E 4 6 5 + E = (19)10 = (16 x 1) + 3 = (13)16
---------
1 3 E 5
Carry
1 1
Rules:
For adding individual digits of a Hexadecimal number, a mental addition of the decimal equivalent digits makes the process easier.
After adding up the decimal digits, you must convert the result back to Hexadecimal, as shown in the above example.
Carry

## Slide 29: Octal Multiplication
Multiply (762)8 with (45)8
Octal Octal Decimal Octal
7 6 2 5 x 2 = (10)10 = (8 x 1) + 2 = 12
x 4 5 5 x 6 + 1 = (31)10 = (8 x 3) + 7 = 37
-------------- 5 x 7 + 3 = (38)10 = (8 x 4) + 6 = 46
4 6 7 2 4 x 2 = (8)10 = (8 x 1) + 0 = 10
3 7 1 0 4 x 6 + 1 = (25)10 = (8 x 3) + 1 = 31
--------------- 4 x 7 + 3 = (31)10 = (8 x 3) + 7 = 37
4 3 7 7 2
We use decimal representation for ease of calculation
Carry

## Slide 30: Conclusions
To convert from decimal to base-r, divide by r for the integral part, multiply by r for the fractional part, then combine.
To convert from binary to octal (hexadecimal) group bits into 3 (4).
To convert between bases other than decimal, first convert source base to decimal, then convert decimal to the destination base.
When performing arithmetic operations in base-r, remember allowed digits {0,..r-1}.