## Slide 1: COE 202: Digital Logic Design Combinational Logic Part 1
Courtesy of Dr. Ahmad Almulhem

## Slide 2: Objectives
Logic Operations and Gates
Boolean Algebra
Boolean Expressions
Boolean Identities
Algebraic manipulation (simplification)
Complement of a Function

## Slide 3: Logical Operations
Three basic logical operations can be applied to binary variables:
  AND: Z = X.Y or Z = XY
    The AND operation works as follows: If both X and Y have a value of 1, the output Z will be 1 else Z will be 0
  OR: Z = X + Y
    The OR operation implies: If either X or Y have a value of 1, the output Z will be 1
  NOT: Z = X
  If the value of X is a 0, Z is a 1, and if X = 1, Z= 0
Don’t confuse binary logic and binary arithmetic !

## Slide 4: AND Operation
AND |  | 
X | Y | Z = X.Y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
A truth table of a logical operation is a table of all possible combinations of input variable values, and the corresponding value of the output
The truth table for the AND logical operation:
Similar to
multiplication

## Slide 5: AND Gate
The electronic device that performs the AND operation is called the AND gate
X
Y
Z
An AND gate with two input variables X, Y and one output Z
Note: The output of the AND gate Z is a 1 if and only if all the inputs are 1 else it is 0

## Slide 6: 3-input AND gate
W
X
Y
Z
W | X | Y | Z
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1
Truth Table for a 3 input AND gate
Note: For an n-input logic gate, the size of the truth table is 2n

## Slide 7: OR Operation
OR |  | 
X | Y | Z = X +Y
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
Similar to
addition
The truth table for the OR logical operation

## Slide 8: OR Gate
The electronic device that performs the AND operation is called the AND gate
X
Y
Z
An OR gate with two input variables X, Y and one output Z
Note: The output of the OR gate Z is a 1 if either of the two inputs X, Y are 1

## Slide 9: OR Gate – 3 Input
W
X
Y
Z
W | X | Y | Z = W + X + Y
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
Truth Table for a 3 input OR gate
Note: For an n-input logic gate, the size of the truth table is 2n

## Slide 10: NOT Operation
NOT is a unary operator, meaning there can only be 1 input
The NOT operation can be represented as follows: Z= X’ or
Z = X
X is also referred to as the complement of Z.
The NOT gate is also known as the Inverter
Z
X
NOT | 
X | Z = X
0 | 1
1 | 0

## Slide 11: Timing Diagram
time
time
time
time
time
A graphical
representation
Of the truth table!

## Slide 12: Logical Operations and Gates (Summary)
src: Mano’s Textbook

## Slide 13: Boolean Algebra
Digital circuits are hardware components for processing (manipulation) of binary input
They are built of transistors and interconnections in semiconductor devices called integrated circuits
A basic circuit is called a logic gate; its function can be represented mathematically.
What is inside the gate is not of concern to the system/computer designer (Only its function)
Binary logic (Boolean Algebra) is a mathematical system to analyze and design digital circuits
  George Boole (introduced mathematical theory of logic in1854)

## Slide 14: Boolean Algebra
Regular Algebra
Numbers
Integers
Real numbers
Complex Numbers
+, -, x, /, … etc
Boolean Algebra
1 (True, High)
0 (False, Low)
AND ( . )
OR (+)
NOT ( ‘, )
Values
Operators
Variables may be given any name such as A, B, X etc..

## Slide 15: Boolean Expression
A Boolean expression is made of Boolean variables and constants combined with logical operators: AND, OR and NOT
A literal is each instance of a variable or constant.
Boolean expressions are fully defined by their truth tables
A Boolean expression can be represented using interconnected logic gates
  Literals correspond to the input signals to the gates
  Constants (1 or 0) can also be input signals
  Operators of the expression are converted to logic gates
Example: a’bd + bcd + ac’ + a’d’ (4 variables, 10 literals, ?? gates)
F (X, Y) = XY + Y’
variable
operator
literals

## Slide 16: Operator Precedence
Given a Boolean expression, the order of operations depends on the precedence rules given by:
  Parenthesis Highest Priority
  NOT
  AND
  OR Lowest Priority
Example: XY + WZ will be evaluated as:
1. XY
2. WZ
3. XY + WZ

## Slide 17: Example
F = X . ( Y’ + Z)
  This function has three inputs X, Y, Z and the output is given by F
  As can be seen, the gates needed to construct this circuit are: 2 input AND, 2 input OR and NOT
Y’
Y
Z
X
F

## Slide 18: Example (Cont.)
F = X . ( Y’ + Z) |  |  |  |  | 
X | Y | Z | Y’ | Y’ + Z | F=X.(Y’+Z)
0 | 0 | 0 | 1 | 1 | 0
0 | 0 | 1 | 1 | 1 | 0
0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 1 | 0
1 | 0 | 0 | 1 | 1 | 1
1 | 0 | 1 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0 | 0
1 | 1 | 1 | 0 | 1 | 1
A Boolean function can be represented with a truth table

## Slide 19: Identities of Boolean Algebra
src: Mano’s Textbook

## Slide 20: Duality Principle
The principle of duality states that: given a Boolean Algebra identity, its dual is obtained by replacing all 1’s with 0’s and 0’s with 1’s, all AND operators with OR, and all OR operators with AND
The dual of an identity is also an identity
AND Identities:
X.1 = X
X.0 = 0
X.X = X
X.X = 0
OR Identities (Dual):
X + 0 = X
X + 1 = 1
X + X = X
X + X = 1
Replacing
1 with 0
0 with 1
+ with .
. with +
Another Important Identity: X = X

## Slide 21: DeMorgan’s Theorem
use truth tables to prove that two Boolean expressions are equal !
Extended DeMorgan’s Theorem: X1 + X2 + …. +Xn = X1.X2…..Xn
X1 X2 …. Xn = X1 + X2+….+Xn

## Slide 22: Why Boolean Algebra?
Boolean algebra identities and properties help reduce the size of expressions
In effect, smaller sized expressions will require fewer logic gates for building the circuit
As a result, less cost will be incurred for building simpler circuits
The speed of simpler circuits is also high

## Slide 23: Algebraic Manipulation
Ability to use the Boolean identities and properties to reduce complex equations
Example 1: Prove that X + XY = X
X + XY = X.(1+Y) = X.1 = X
distributive property
Example 2: Reduce X+X’Y
= (X+X’).(X+Y) = 1.(X+Y) = X+Y
This is called absorption
Y has been absorbed

## Slide 24: Algebraic Manipulation (Example)
F = X’YZ + X’YZ’ + XZ
= X’Y(Z+Z’) + XZ (id 14)
= X’Y.1 + XZ (id 7)
= X’Y + XZ (id 2)

## Slide 25: Algebraic Manipulation (Example)
F = X’YZ + X’YZ’ + XZ
= X’Y(Z+Z’) + XZ (id 14)
= X’Y.1 + XZ (id 7)
= X’Y + XZ (id 2)

## Slide 26: Algebraic Manipulation (Example)
F = X’YZ + X’YZ’ + XZ
= X’Y(Z+Z’) + XZ (id 14)
= X’Y.1 + XZ (id 7)
= X’Y + XZ (id 2)
Verify !

## Slide 27: Example (Consensus Theorem)
XY + X’Z + YZ = XY + X’Z
Prove:
XY+X’Z+YZ = XY+X’Z+YZ.1
= XY+X’Z+YZ(X+X’)
= XY+X’Z+XYZ+X’YZ
= XY+XYZ+X’Z+X’YZ
= XY(1+Z)+X’Z(1+Y)
= XY.1 + X’Z.1
= XY + X’Z
Adding an extra step to acquire the desired output
Y and Z are associated
with X and X’ in the
first two terms and
appear together in the third.
YZ is redundant and can be
eliminated.

## Slide 28: Example
Reduce F1=(A + B + AB) (AB + AC + BC)
Using DeMorgan’s Theorem,
F1 = (A’.B.(A’+B’)).(A’+B’).(A+C’).(B’+C’)
= (A’.B.A’ + A’.B.B’).(A’+B’)(A+C’) .(B’+C’)
= (A’B + 0).(A’+B’)(A+C’) .(B’+C’)
= (A’BA’ + A’BB’) (A+C’) .(B’+C’)
= (A’B) (A+C’) .(B’+C’)
= (A’BA+A’BC’)(B’+C’)
= (0+A’BC’)(B’+C’)
= (A’BC’B’ + A’BC’C’)
= (0 + A’BC’) = A’BC’

## Slide 29: Example
Simplify G = ((A+B+C).(AB+CD)+(ACD))
= ((A+B+C)+(AB.(C+D))).ACD
= (A+B+C).ACD + (AB.(C+D)).ACD
= (ACD+ABCD) + (ABCD+ABCD)
= (ACD +ACD(B+B) + ABCD)
= (ACD + ACD + ABCD)
= (ACD + ABCD)
= (ACD(1+B))
= ACD

## Slide 30: Complement of a Function
The complement of a function F, F, is obtained in two ways:
  1. Truth Table: Change 1s to 0s and 0s to 1s
  2. Boolean Expression: Apply DeMorgan’s Theorem
  * Be Careful !! Before you begin, surround all AND terms with parentheses (easy to make a mistake!).
A | B | F | F’
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
Truth table
F = A’B + AB’
F’ = (A+B’).(A’+B)
= AB + A’B’
Short cut: Take the dual and complement the literals.

## Slide 31: Conclusion
Boolean Algebra is a mathematical system to study logic circuits
Boolean identities and algebraic manipulation can be used to simplify Boolean expressions.
Simplified Boolean expressions result in simpler circuits.