## Slide 1: COE 202: Digital Logic Design Combinational Logic Part 2
Courtesy of Dr. Ahmad Almulhem

## Slide 2: Objectives
Minterms and Maxterms
From truth table to Boolean expression
  Sum of minterms
  Product of Maxterms
Standard and Canonical Forms
Implementation of Standard Forms
Practical Aspects of Logic Gates

## Slide 3: Minterms
A product term is a term where literals are ANDed.
  Example: x’y’, xz, xyz, …
A minterm is a product term in which all variables appear exactly once, in normal or complemented form
  Example: F(x,y,z) has 8 minterms: x’y’z’, x’y’z, x’yz’, ...
In general, a function with n variables has 2n minterms
A minterm equals 1 at exactly one input combination and is equal to 0 otherwise
  Example: x’y’z’ = 1 only when x=0, y=0, z=0
A minterm is denoted as mi where i corresponds the input combination at which this minterm is equal to 1

## Slide 4: Minterms
Variable complemented if 0
Variable uncomplemented if 1
mi indicated the ith minterm
i indicates the binary combination
mi is equal to 1 for ONLY THAT combination
Src: Mano’s book

## Slide 5: Maxterms
A sum term is a term where literals are ORed.
  Example: x’+y’, x+z, x+y+z, …
A maxterm is a sum term in which all variables appear exactly once, in normal or complemented form
  Example: F(x,y,z) has 8 maxterms: (x+y+z), (x+y+z’), (x+y’+z), ...
In general, a function with n variables has 2n maxterms
A maxterm equals 0 at exactly one input combination and is equal to 1 otherwise
  Example: (x+y+z) = 0 only when x=0, y=0, z=0
A maxterm is denoted as Mi where i corresponds the input combination at which this maxterm is equal to 0

## Slide 6: Maxterms
Src: Mano’s book
Variable complemented if 1
Variable not complemented if 0
Mi indicated the ith maxterm
i indicates the binary combination
Mi is equal to 0 for ONLY THAT combination

## Slide 7: Minterms and Maxterms
In general, a function of n variables has
  2n minterms: m0, m1, …, m2n-1
  2n maxterms: M0, M1, …, M2n-1
Minterms and maxterms are the complement of each other!
  Example: F(X,Y):
  m2 = XY’  m2’ = X’+Y = M2

## Slide 8: Expressing Functions with Minterms
A Boolean function can be expressed algebraically from a give truth table by forming the logical sum (OR) of ALL the minterms that produce 1 in the function
Example:
X | Y | Z | m | F
0 | 0 | 0 | m0 | 1
0 | 0 | 1 | m1 | 0
0 | 1 | 0 | m2 | 1
0 | 1 | 1 | m3 | 0
1 | 0 | 0 | m4 | 0
1 | 0 | 1 | m5 | 1
1 | 1 | 0 | m6 | 0
1 | 1 | 1 | m7 | 1
Consider the function defined by the truth table
F(X,Y,Z) = X’Y’Z’ + X’YZ’ + XY’Z + XYZ
= m0 + m2 + m5 + m7
= Sm(0,2,5,7)

## Slide 9: Expressing Functions with Maxterms
A Boolean function can be expressed algebraically from a give truth table by forming the logical product (AND) of ALL the maxterms that produce 0 in the function
X | Y | Z | M | F | F’
0 | 0 | 0 | M0 | 1 | 0
0 | 0 | 1 | M1 | 0 | 1
0 | 1 | 0 | M2 | 1 | 0
0 | 1 | 1 | M3 | 0 | 1
1 | 0 | 0 | M4 | 0 | 1
1 | 0 | 1 | M5 | 1 | 0
1 | 1 | 0 | M6 | 0 | 1
1 | 1 | 1 | M7 | 1 | 0
Example:
Consider the function defined by the truth table
F(X,Y,Z) =  M(1,3,4,6)
Applying DeMorgan
F’ = m1 + m3 + m4 + m6
= Sm(1,3,4,6)
F = F’’ = [m1 + m3 + m4 + m6]’
= m1’.m3’.m4’.m6’
= M1.M3.M4.M6
=  M(1,3,4,6)
Note the indices in this list are those that are
missing from the previous list in Sm(0,2,5,7)

## Slide 10: Sum of Minterms vs Product of Maxterms
A Boolean function can be expressed algebraically as:
  The sum of minterms
  The product of maxterms
Given the truth table, writing F as
  ∑mi – for all minterms that produce 1 in the table, or
  Mi – for all maxterms that produce 0 in the table
Minterms and Maxterms are complement of each other.

## Slide 11: Example
Write E = Y’ + X’Z’ in the form of Smi and Mi?
Solution: Method1
First construct the Truth Table as shown
Second:
E = Sm(0,1,2,4,5), and
E = M(3,6,7)
X | Y | Z | m | M | E
0 | 0 | 0 | m0 | M0 | 1
0 | 0 | 1 | m1 | M1 | 1
0 | 1 | 0 | m2 | M2 | 1
0 | 1 | 1 | m3 | M3 | 0
1 | 0 | 0 | m4 | M4 | 1
1 | 0 | 1 | m5 | M5 | 1
1 | 1 | 0 | m6 | M6 | 0
1 | 1 | 1 | m7 | M7 | 0

## Slide 12: Example (Cont.)
Solution: Method2_a
E = Y’ + X’Z’
= Y’(X+X’)(Z+Z’) + X’Z’(Y+Y’)
= (XY’+X’Y’)(Z+Z’) + X’YZ’+X’Z’Y’
= XY’Z+X’Y’Z+XY’Z’+X’Y’Z’+ X’YZ’+X’Z’Y’
= m5 + m1 + m4 + m0 + m2 + m0
= m0 + m1 + m2 + m4 + m5
= Sm(0,1,2,4,5)
To find the form Mi, consider the remaining indices
E = M(3,6,7)
Solution: Method2_b
E = Y’ + X’Z’
E’ = Y(X+Z)
= YX + YZ
= YX(Z+Z’) + YZ(X+X’)
= XYZ+XYZ’+X’YZ
E = (X’+Y’+Z’)(X’+Y’+Z)(X+Y’+Z’)
= M7 . M6 . M3
= M(3,6,7)
To find the form Smi, consider the remaining indices
E = Sm(0,1,2,4,5)

## Slide 13: Example
Question: F (a,b,c,d) = ∑m(0,1,2,4,5,7), What are the minterms and maxterms of F and and its complement F?
Solution:
F has 4 variables; 24 possible minterms/maxterms
F (a,b,c,d) = ∑m(0,1,2,4,5,7)
= Π M(3,6,8,9,10,11,12,13,14,15)
F (a,b,c,d) = ∑m(3,6,8,9,10,11,12,13,14,15)
= Π M(0,1,2,4,5,7)

## Slide 14: Example
Question: F (a,b,c,d) = ∑m(0,1,2,4,5,7), What are the minterms and maxterms of F and and its complement F?
Solution:
F has 4 variables; 24 = 16 possible minterms/maxterms
F (a,b,c,d) = ∑m(0,1,2,4,5,7)
= Π M(3,6,8,9,10,11,12,13,14,15)
F (a,b,c,d) = ∑m(3,6,8,9,10,11,12,13,14,15)
= Π M(0,1,2,4,5,7)

## Slide 15: Canonical Forms
The sum of minterms and the product of maxterms forms are known as the canonical forms (الصيغ القانونية) of a function.

## Slide 16: Standard Forms
Sum of Products (SOP) and Product of Sums (POS) are also standard forms
  AB+CD = (A+C)(B+C)(A+D)(B+D)
The sum of minterms is a special case of the SOP form, where all product terms are minterms
The product of maxterms is a special case of the POS form, where all sum terms are maxterms

## Slide 17: SOP and POS Conversion
SOP  POS
F = AB + CD
= (AB+C)(AB+D)
= (A+C)(B+C)(AB+D)
= (A+C)(B+C)(A+D)(B+D)
Hint 1: Use id15: X+YZ=(X+Y)(X+Z)
Hint 2: Factor
POS  SOP
F = (A’+B)(A’+C)(C+D)
= (A’+BC)(C+D)
= A’C+A’D+BCC+BCD
= A’C+A’D+BC+BCD
= A’C+A’D+BC
Hint 1: Use id15 (X+Y)(X+Z)=X+YZ
Hint 2: Multiply

## Slide 18: SOP and POS Conversion
SOP  POS
F = AB + CD
= (AB+C)(AB+D)
= (A+C)(B+C)(AB+D)
= (A+C)(B+C)(A+D)(B+D)
Hint 1: Use id15: X+YZ=(X+Y)(X+Z)
Hint 2: Factor
POS  SOP
F = (A’+B)(A’+C)(C+D)
= (A’+BC)(C+D)
= A’C+A’D+BCC+BCD
= A’C+A’D+BC+BCD
= A’C+A’D+BC
Hint 1: Use id15 (X+Y)(X+Z)=X+YZ
Hint 2: Multiply
Question1: How to convert SOP to sum of minterms?
Question2: How to convert POS to product of maxterms?

## Slide 19: Implementation of SOP
Any SOP expression can be implemented using 2-levels of gates
The 1st level consists of AND gates, and the 2nd level consists of a single OR gate
Also called 2-level Circuit

## Slide 20: Implementation of POS
Any POS expression can be implemented using 2-levels of gates
The 1st level consists of OR gates, and the 2nd level consists of a single AND gate
Also called 2-level Circuit

## Slide 21: Implementation of SOP
Consider F = AB + C(D+E)
  This expression is NOT in the sum-of-products form
  Use the identities/algebraic manipulation to convert to a standard form (sum of products), as in F = AB + CD + CE
Logic Diagrams:
F
E
C
D
C
B
A
F
C
B
A
E
D
3-level circuit
2-level circuit

## Slide 22: Practical Aspects of Logic Gates
Logic gates are built with transistors as integrated circuits (IC) or chips.
ICs are digital devices built using various technologies.
  Complementary metal oxide semiconductor (CMOS) technology
Levels of Integration:
  Small Scale Integrated (SSI) < 10 gates
  Medium Scale Integrated (MSI) < 100 gates
  Large Scale Integrated (LSI) < 1000 gates
  Very Large Scale Integrated (VLSI) < 106 gates
NOT gate

## Slide 23: Propagation Delay
Propagation delay (tpd) is the time for a change in the input of a gate to propagate to the output
  High-to-low (tphl) and low-to-high (tplh) output signal changes may have different propagation delays
  tpd = max {tphl, tphl)
A circuit is considered to be fast, if its propagation delay is less (ideally as close to 0 as possible)
Delay is usually measured
between the 50% levels
of the signal

## Slide 24: Timing Diagram
The timing diagram shows the input and output signals in the form of a waveform
It also shows delays
X
Y
Z
Propagation Delay of the Circuit = τ
Inputs
Output
Timing Diagram for an AND gate
Time

## Slide 25: Tristate Gates
Gates with 3 output values 0, 1, Hi-Z
  Hi-Z behaves like an open circuit.
E | X | Z
1 | 0 | 1
1 | 1 | 0
0 | 0 | High Z
0 | 1 | High Z

## Slide 26: Tristate Gates
Q: Can we connect the outputs
of two gates?

## Slide 27: Tristate Gates
Q: Can we connect the outputs
of two gates?

## Slide 28: Tristate Gates
Q: Can we connect the outputs
of two gates?
Two or more tri-state outputs may be
connected provided that only one
of these outputs is enabled while all
others are in the Hi-Z state.