## Slide 1: COE 202: Digital Logic Design Sequential Circuits Part 2
Courtesy of Dr. Ahmad Almulhem

## Slide 2: Objectives
Analysis of Synchronous Sequential Circuits
  Procedure
  Examples

## Slide 3: Analysis of Sequential Circuits
Analysis is describing what a given circuit will do
The behavior of a clocked (synchronous) sequential circuit is determined from the inputs, the output, and the states of FF
Steps:
  Obtain state equations
    FF input equations
    Output equations
  Fill the state table
    Put all combinations of inputs and current states
    Fill the next state and output
  Draw the state diagram

## Slide 4: Analysis of Combinational vs Sequential Circuits
Combinational :
Boolean Equations
Truth Table
Output as a function of inputs
Sequential :
State Equations
State Table
State Diagram
Output as a function of input and current state
Next state as a function of inputs and current state.

## Slide 5: State Equations
A state equation is a Boolean expression which specifies the next state and output as a function of the present state and inputs.
Example:
The shown circuit has two D-FFs (A,B), an input x and output y.
The D input of a FF determines the next state
  A(t+1) = A(t)x+B(t)x = Ax+Bx
  B(t+1) = A’(t)x = A’x
Output:
  y = (A+B)x’

## Slide 6: State Table
A state table is a table enumerating all present states, inputs, next states and outputs.
Present state, inputs: list all combinations
Next states, outputs: derived from state equations
4 sections

## Slide 7: State Table
2-D Form
A state table is a table enumerating all present states, inputs, next states and outputs.
Present state, inputs: list all combinations
Next states, outputs: derived from state equations

## Slide 8: State Diagram
The state diagram is a graphical representation of a state table (provides same information)
Circles are states (FFs), Arrows are transitions between states
Labels of arrows represent inputs and outputs

## Slide 9: Analysis of Sequential Circuits
Analysis is describing what a given circuit will do
The behavior of a clocked (synchronous) sequential circuit is determined from the inputs, the output, and the states of FF
Steps:
  Obtain state equations
    FF input equations
    Output equations
  Fill the state table
    Put all combinations of inputs and current states
    Fill the next state and output
  Draw the state diagram

## Slide 10: Example 1
Analyze this circuit?
Is this a sequential circuit? Why?
How many inputs?
How many outputs?
How many states?
What type of memory?

## Slide 11: Example 1 (cont.)
Q(t) | D | Q(t+1)
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
D | Q(t+1)
0 | 0
1 | 1
Q(t+1) = D
Characteristic Tables and Equations
D Flip Flop (review)

## Slide 12: Example 1 (cont.)

## Slide 13: Example 1 (cont.)
State equations:
DA = AX + BX
DB = A’ X
Y = (A + B) X’

## Slide 14: Example 1 (cont.)
State equations:
DA = AX + BX
DB = A’ X
Y = (A + B) X’
State table:

## Slide 15: Example 1 (cont.)
State equations:
DA = AX + BX
DB = A’ X
Y = (A + B) X’
State table (2D):

## Slide 16: Example 1 (cont.)
State equations:
DA = AX + BX
DB = A’ X
Y = (A + B) X’
State table:
State diagram:

## Slide 17: Example 2
Analyze this circuit.
What about the output?
This circuit is an example of a Moore machine (output depends only on current state)
Mealy machines is the other type (output depends on inputs and current states)

## Slide 18: Example 2 (cont.)
Equation:
DA = A  X  Y

## Slide 19: Example 2 (cont.)
Equation:
DA = A  X  Y
0/0
1/1

## Slide 20: Mealy vs Moore Finite State Machine (FSM)
Mealy FSM:
Output depends on current state and input
Output is not synchronized with the clock
Moore FSM:
Output depends on current state only

## Slide 21: Summary
To analyze a sequential circuit:
  Obtain state equations
    FF input equations
    Output equations
  Fill the state table
    Put all combinations of inputs and current states
    Fill the next state and output
    For the next state use characteristic table/equation
  Draw the state diagram
Two types of synchronous sequential circuits (Mealy and Moore)