## Slide 1: COE 202: Digital Logic Design Sequential Circuits Part 3
Courtesy of Dr. Ahmad Almulhem

## Slide 2: Objectives
Design of Synchronous Sequential Circuits
  Procedure
  Examples
Important Design Concepts
  State Reduction and Assignment

## Slide 3: Design of Synchronous Sequential Circuits
The design of a clocked sequential circuit starts from a set of specifications and ends with a logic diagram (Analysis reversed!)
Building blocks: flip-flops, combinational logic
Need to choose type and number of flip-flops
Need to design combinational logic together with flip-flops to produce the required behavior
The combinational part is
  flip-flop input equations
  output equations

## Slide 4: Design of Synchronous Sequential Circuits
Design Procedure:
  Obtain a state diagram from the word description
    State reduction if necessary
  Obtain State Table
    State Assignment
    Choose type of flip-flops
    Use FF’s excitation table to complete the table
  Derive state equations
    Obtain the FF input equations and the output equations
    Use K-Maps
  Draw the circuit diagram

## Slide 5: Step1: Obtaining the State Diagram
A very important step in the design procedure.
Requires experience!
Example: Design a circuit that detects a sequence of three consecutive 1’s in a string of bits coming through an input line (serial bit stream)

## Slide 6: Step1: Obtaining the State Diagram
A very important step in the design procedure.
Requires experience!
Example: Design a circuit that detects a sequence of three consecutive 1’s in a string of bits coming through an input line (serial bit stream)

## Slide 7: Step2: Obtaining the State Table
Assign binary codes for the states
We choose 2 D-FF
  Next state specifies what should be the input to each FF
Example: Design a circuit that detects a sequence of three consecutive 1’s in a string of bits coming through an input line (serial bit stream)

## Slide 8: Step3: Obtaining the State Equations
Using K-Maps
A(t + 1) = DA = ∑(3,5,7) = A x + B x
B(t + 1) = DB = ∑(1,5,7) = A x + B’ x
y = ∑(6,7) = A B
Example: Design a circuit that detects a sequence of three consecutive 1’s in a string of bits coming through an input line (serial bit stream)

## Slide 9: Step4: Draw Circuits
Using K-Maps
A(t + 1) = DA = ∑(3,5,7) = A x + B x
B(t + 1) = DB = ∑(1,5,7) = A x + B’ x
y = ∑(6,7) = A B
Example: Design a circuit that detects a sequence of three consecutive 1’s in a string of bits coming through an input line (serial bit stream)

## Slide 10: Timing Diagram (Verification)
Question: Does it detect 111 ?

## Slide 11: Example 2
Problem: Design of A Sequence Recognizer
Design a circuit that reads as inputs continuous bits, and generates an output of ‘1’ if the sequence (1011) is detected
Input 1 1 1 0 0 1 0 0 1 0 0 1 1 0 1 1 0 1 0 1 1 0 1 1 1 1 1 1
Output 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 1 0 0 0 0 1 0 0 1 0 0 0 0
X
Y

## Slide 12: Example 2 (cont.)
Step1: State Diagram
Sequence to be detected:1011

## Slide 13: Example 2 (cont.)
Step 2: State Table
OR

## Slide 14: Example 2 (cont.)
Step 2: State Table
state assignment
Q: How many FF?
log2(no. of states)

## Slide 15: Example 2 (cont.)
Step 2: State Table
choose FF
In this example, lets use JK–FF for A and D-FF for B

## Slide 16: Example 2 (cont.)
Step 2: State Table
complete state table
use excitation tables for JK–FF and D-FF
D–FF excitation table
JK–FF excitation table
Next
State
output

## Slide 17: Example 2 (cont.)
Step 3: State Equations
use k-map
JA = BX’
KA = BX + B’X’
DB = X
Y = ABX’

## Slide 18: Example 2 (cont.)
Step 4: Draw Circuit
JA = BX’
KA = BX + B’X’
DB = X
Y = ABX’

## Slide 19: Example 3
Problem: Design of A 3-bit Counter
Design a circuit that counts in binary form as follows 000, 001, 010, … 111, 000, 001, …

## Slide 20: Example 3 (cont.)
Step1: State Diagram
The outputs = the states
Where is the input?
What is the type of this sequential circuit?

## Slide 21: Example 3 (cont.)
Step2: State Table
No need for state assignment here

## Slide 22: Example 3 (cont.)
Step2: State Table
We choose T-FF
T–FF excitation table
0

## Slide 23: Example 3 (cont.)
Step3: State Equations

## Slide 24: Example 3 (cont.)
Step4: Draw Circuit
TA0 = 1
TA1 = A0
TA2 = A1A0

## Slide 25: Example 4
N
S
E
W
Traffic | Action
EW only | EW Signal green NS Signal red
NS only | NS Signal green EW Signal red
EW & NS | Alternate
No traffic | Previous state
Problem: Design a traffic light controller for a 2-way intersection. In each way, there is a sensor and a light

## Slide 26: Example 4 (cont.)
EW / 10
NS / 01
INPUTS
Sensors X1, X0
X0: car coming on NS
X1 : car coming on EW
11, 10
00, 01
00, 10
11, 01
  OUTPUTS
Light S1, S0
S0 : NS is green
S1 : EW is green
  STATES
NS: NS is green
EW: EW is green
Step1: State Diagram

## Slide 27: Example 4 (cont.)
Exercise: Complete the design using:
  D-FF
  JK-FF
  T-FF

## Slide 28: Example 5
Problem: Design Up/Down counter with Enable
Design a sequential circuit with two JK flip-flops A and B and two inputs X and E. If E = 0, the circuit remains in the same state, regardless of the input X. When E = 1 and X = 1, the circuit goes through the state transitions from 00 to 01 to 10 to 11, back to 00, and then repeats. When E = 1 and X = 0, the circuit goes through the state transitions from 00 to 11 to 10 to 01, back to 00 and then repeats.

## Slide 29: Example 5 (cont.)
00
01
10
11
00
01
10
11
10
11
10
11
11
00
01
00
01
10
00
01
Present State |  |  | Inputs |  |  | Next State |  |  | FF Inputs |  |  |  | 
A | B |  | E | X |  | A | B |  | JA | KA |  | JB | KB
0 | 0 |  | 0 | 0 |  | 0 | 0 |  | 0 | X |  | 0 | X
0 | 0 |  | 0 | 1 |  | 0 | 0 |  | 0 | X |  | 0 | X
0 | 0 |  | 1 | 0 |  | 1 | 1 |  | 1 | X |  | 1 | X
0 | 0 |  | 1 | 1 |  | 0 | 1 |  | 0 | X |  | 1 | X
0 | 1 |  | 0 | 0 |  | 0 | 1 |  | 0 | X |  | X | 0
0 | 1 |  | 0 | 1 |  | 0 | 1 |  | 0 | X |  | X | 0
0 | 1 |  | 1 | 0 |  | 0 | 0 |  | 0 | X |  | X | 1
0 | 1 |  | 1 | 1 |  | 1 | 0 |  | 1 | X |  | X | 1
1 | 0 |  | 0 | 0 |  | 1 | 0 |  | X | 0 |  | 0 | X
1 | 0 |  | 0 | 1 |  | 1 | 0 |  | X | 0 |  | 0 | X
1 | 0 |  | 1 | 0 |  | 0 | 1 |  | X | 1 |  | 1 | X
1 | 0 |  | 1 | 1 |  | 1 | 1 |  | X | 0 |  | 1 | X
1 | 1 |  | 0 | 0 |  | 1 | 1 |  | X | 0 |  | X | 0
1 | 1 |  | 0 | 1 |  | 1 | 1 |  | X | 0 |  | X | 0
1 | 1 |  | 1 | 0 |  | 1 | 0 |  | X | 0 |  | X | 1
1 | 1 |  | 1 | 1 |  | 0 | 0 |  | X | 1 |  | X | 1

## Slide 30: Example 5 (cont.)
JA = BEX + B’EX’
EX AB | 00 | 01 | 11 | 10
00 | x | x | x | x
01 | x | x | x | x
11 | 0 | 0 | 1 | 0
10 | 0 | 0 | 0 | 1
KA = BEX + B’EX’
EX AB | 00 | 01 | 11 | 10
00 | 0 | 0 | 0 | 1
01 | 0 | 0 | 1 | 0
11 | x | x | x | x
10 | x | x | x | x
JB = E
EX AB | 00 | 01 | 11 | 10
00 | x | x | x | x
01 | 0 | 0 | 1 | 1
11 | 0 | 0 | 1 | 1
10 | x | x | x | X
KB = E
EX AB | 00 | 01 | 11 | 10
00 | 0 | 0 | 1 | 1
01 | x | x | x | x
11 | x | x | x | x
10 | 0 | 0 | 1 | 1
Y
X
JA
C
A
A’
KA
E
clock
JB
C
B
B’
KB

## Slide 31: More Design Examples
More design examples can be found at
  Homework 5
  Textbook
  Course CD
  Google

## Slide 32: Summary
To design a synchronous sequential circuit:
  Obtain a state diagram
    State reduction if necessary
  Obtain State Table
    State Assignment
    Choose type of flip-flops
    Use FF’s excitation table to complete the table
  Derive state equations
    Use K-Maps
    Obtain the FF input equations and the output equations
  Draw the circuit diagram