## Slide 1: COE 202: Digital Logic Design Memory
Courtesy of Dr. Ahmad Almulhem

## Slide 2: Objectives
Memory

## Slide 3: Memory
Memory: A collection of cells capable of storing binary information (1s or 0s) – in addition to electronic circuit for storing (writing) and retrieving (reading) information.
n data lines (input/output)
k address lines
2k words (data unit)
Read/Write Control
Memory size = 2k X n
Word: group of bits stored in one location

## Slide 4: Memory (cont.)
Two Types of Memory:
Random Access Memory (RAM):
  Write/Read operations
  Volatile: Data is lost when power is turned off
Read Only Memory (ROM):
  Read operation (no write)
  Non-Volatile: Data is permanent.
  PROM is programmable (allow special write)

## Slide 5: Read-Only Memory (ROM)
ROM: A device in which “permanent” binary information is stored using a special device (programmer)
k inputs (address)  2k words each of size n bits (data)
ROM DOES NOT have a write operation  ROM DOES NOT have data inputs
2k x n ROM
k inputs
(address)
n outputs
(data)
Word: group of bits stored in one location

## Slide 6: ROM Internal Logic
The decoder stage produces ALL possible minterms
32 words of 8 bits each
5 input lines (address)
Each OR gate has a 32 input
A contact can be made using fuse/anti-fuse
0
1
2
3
.
.
.
28
29
30
31
I0
I1
I2
I3
I4
A7 A6 A5 A4 A3 A2 A1 A0
5-to-32
decoder
Internal Logic of a 32x8 ROM

## Slide 7: Programming a ROM
Every ONE in truth table specifies a closed circuit
Every ZERO in truth table specifies an OPEN circuit
Example: At address 00011  The word 10110010 is stored
Inputs |  |  |  |  |  | Outputs |  |  |  |  |  |  | 
I4 | I3 | I2 | I1 | I0 |  | A7 | A6 | A5 | A4 | A3 | A2 | A1 | A0
0 | 0 | 0 | 0 | 0 |  | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 0
0 | 0 | 0 | 0 | 1 |  | 0 | 0 | 0 | 1 | 1 | 1 | 0 | 1
0 | 0 | 0 | 1 | 0 |  | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 1
0 | 0 | 0 | 1 | 1 |  | 1 | 0 | 1 | 1 | 0 | 0 | 1 | 0
 |  | . |  |  |  |  |  |  | . |  |  |  | 
 |  | . |  |  |  |  |  |  | . |  |  |  | 
 |  | . |  |  |  |  |  |  | . |  |  |  | 
1 | 1 | 1 | 0 | 0 |  | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1
1 | 1 | 1 | 0 | 1 |  | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 1 | 0 |  | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1 |  | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
0
1
2
3
.
.
.
28
29
30
31
I0
I1
I2
I3
I4
A7 A6 A5 A4 A3 A2 A1 A0
5-to-32
decoder
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x

## Slide 8: Combinational Circuit Implementation with ROM
ROM = Decoder + OR gates
Implementation of a combinational circuit is easy
  Store the truth table by programming the ROM
Only need to provide the truth table

## Slide 9: Example 1
Example: Design a combinational circuit using ROM. The circuit accepts a 3-bit number and generates an output binary number equal to the square of the number.
Solution: Derive truth table:
Inputs |  |  |  | Outputs |  |  |  |  |  | 
A2 | A1 | A0 |  | B5 | B4 | B3 | B2 | B1 | B0 | SQ
0 | 0 | 0 |  | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 |  | 0 | 0 | 0 | 0 | 0 | 1 | 1
0 | 1 | 0 |  | 0 | 0 | 0 | 1 | 0 | 0 | 4
0 | 1 | 1 |  | 0 | 0 | 1 | 0 | 0 | 1 | 9
1 | 0 | 0 |  | 0 | 1 | 0 | 0 | 0 | 0 | 16
1 | 0 | 1 |  | 0 | 1 | 1 | 0 | 0 | 1 | 25
1 | 1 | 0 |  | 1 | 0 | 0 | 1 | 0 | 0 | 36
1 | 1 | 1 |  | 1 | 1 | 0 | 0 | 0 | 1 | 49

## Slide 10: Example 1 (cont.)
B1 is ALWAYS 0  no need to generate it using the ROM
B0 is equal to A0  no need to generate it using the ROM
Therefore: The minimum size of ROM needed is 23X4 or 8X4
8 X 4 ROM
A0
A1
A2
B5
B4
B3
B2
B1
B0
0
ROM truth table – specifies the required connections
Inputs |  |  |  | Outputs |  |  |  |  |  | 
A2 | A1 | A0 |  | B5 | B4 | B3 | B2 | B1 | B0 | SQ
0 | 0 | 0 |  | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 |  | 0 | 0 | 0 | 0 | 0 | 1 | 1
0 | 1 | 0 |  | 0 | 0 | 0 | 1 | 0 | 0 | 4
0 | 1 | 1 |  | 0 | 0 | 1 | 0 | 0 | 1 | 9
1 | 0 | 0 |  | 0 | 1 | 0 | 0 | 0 | 0 | 16
1 | 0 | 1 |  | 0 | 1 | 1 | 0 | 0 | 1 | 25
1 | 1 | 0 |  | 1 | 0 | 0 | 1 | 0 | 0 | 36
1 | 1 | 1 |  | 1 | 1 | 0 | 0 | 0 | 1 | 49

## Slide 11: Example 2
Inputs |  |  |  | Outputs |  |  | 
X | Y | Z |  | A | B | C | D
0 | 0 | 0 |  | 0 | 1 | 0 | 0
0 | 0 | 1 |  | 0 | 1 | 0 | 0
0 | 1 | 0 |  | 0 | 0 | 1 | 1
0 | 1 | 1 |  | 1 | 0 | 1 | 1
1 | 0 | 0 |  | 0 | 1 | 1 | 1
1 | 0 | 1 |  | 0 | 1 | 0 | 0
1 | 1 | 0 |  | 1 | 1 | 0 | 0
1 | 1 | 1 |  | 1 | 0 | 0 | 1
Problem: Tabulate the truth for an 8 X 4 ROM that implements the following four Boolean functions:
A(X,Y,Z) = Sm(3,6,7); B(X,Y,Z) = Sm(0,1,4,5,6)
C(X,Y,Z) = Sm(2,3,4); D(X,Y,Z) = Sm(2,3,4,7)
Solution:
8 X 4 ROM
X
Y
Z
D
C
B
A

## Slide 12: Example 3 (Size of a ROM)
Problem: Specify the size of a ROM (number of words and number of bits per word) that will accommodate the truth table for the following combinational circuit: An 8-bit adder/subtractor with Cin and Cout.
Solution:
Inputs to the ROM (address lines) = 8 (first number) + (8 second number) + 1 (Cin) + 1 (Add/Subtract)  18 lines
Hence number of words in ROM is 218 = 256K
Size of each word = number of possible functions/outputs
= 16 (addition/subtraction) + 1 (Cout)
= 17
Hence ROM size = 256K X 17

## Slide 13: Sequential Circuit Implementation with ROM
sequential circuit = combinational circuit + memory
Combinational part can be built with a ROM as shown previously
  Number of address lines = No. of FF + No. of inputs
  Number of outputs = No. of FF + No. of outputs
Combinational
Circuits
inputs X
outputs Z
FFs
next state
present state

## Slide 14: Example
Example: Design a sequential circuit whose state table is given, using a ROM and a register.
State Table
We need a 8x3 ROM (why?)
3 address lines and 3 data lines
Exercise: Compare design with ROMs with the traditional design procedure.

## Slide 15: Types of ROMs
A ROM programmed in four different ways:
ROM: Mask Programming
  By a semiconductor company
PROM (Programmable ROM)
  User can blow/connect fuses with a special programming device (PROM programmer)
  Only programmed once!
EPROM (Erasable PROM)
  Can be erased using Ultraviolet Light
Electrically Erasable PROM (EEPROM or E2PROM)
  Like an EPROM, but erased with electrical signal