## Slide 1: Modeling Sequential Circuits in Verilog
COE 202
Digital Logic Design
Dr. Muhamed Mudawar
King Fahd University of Petroleum and Minerals

## Slide 2: Presentation Outline
Blocking versus Non-Blocking Assignments
Modeling Latches and Flip-Flops
Modeling Sequential Circuit Diagrams
Modeling Mealy and Moore State Diagrams
Writing Test Benches for Sequential Circuits
Modeling Registers and Counters

## Slide 3: Procedural Assignment
Procedural assignment is used inside a procedural block only
Two types of procedural assignments:
Blocking assignment:
variable = expression; // = operator
Variable is updated before executing next statement
Similar to an assignment statement in programming languages
Non-Blocking assignment:
variable <= expression; // <= operator
Variable is updated at the end of the procedural block
Does not block the execution of next statements

## Slide 4: Blocking versus Non-Blocking Assignment
Read: in, q2, q1
Parallel Assignment at the end
module nonblocking
(input in, clk, output reg out);
reg q1, q2;
always @ (posedge clk) begin
q2 <= in;
q1 <= q2;
out <= q1;
end
endmodule
Guideline: Use Non-Blocking Assignment for Sequential Logic
D
Q
D
Q
D
Q
in
q2
q1
out
clk
module blocking
(input in, clk, output reg out);
reg q1, q2;
always @ (posedge clk) begin
q2 = in;
q1 = q2; // q1 = in
out = q1; // out = in
end
endmodule
D
Q
in
q2
q1
out
clk

## Slide 5: Blocking versus Non-Blocking Assignment
Parallel Assignment at the end
Evaluate all expressions
module nonblocking
(input a,b,c, output reg x,y);
always @ (a, b, c) begin
x <= a & b;
y <= x | c;
end
endmodule
module blocking
(input a,b,c, output reg x,y);
always @ (a, b, c) begin
x = a & b; // update x
y = x | c; // y = a&b | c;
end
endmodule
Guideline: Use Blocking Assignment for Combinational Logic
a
b
c
x
y
a
b
c
x
y
Old x
Old x is
Latched

## Slide 6: Verilog Coding Guidelines
When modeling combinational logic, use blocking assignments
When modeling sequential logic, use non-blocking assignments
When modeling both sequential and combinational logic within the same always block, use non-blocking assignments
Do NOT mix blocking with non-blocking assignments in the same always block
Do NOT make assignments to the same variable from more than one always block

## Slide 7: Recall: Sensitivity List of always block
Syntax:
always @(sensitivity list) begin
procedural statements
end
Sensitivity list is a list of signals: @(signal1, signal2, …)
The sensitivity list triggers the execution of the always block
When there is a change of value in any listed signal
Otherwise, the always block does nothing until another change occurs on a signal in the sensitivity list

## Slide 8: Guidelines for Sensitivity List
For combinational logic, the sensitivity list must include ALL the signals that are read inside the always block
Combinational logic can also use: @(*) or @*
For sequential logic, the sensitivity list may not include all the signals that are read inside the always block
For edge-triggered sequential logic use:
always @(posedge signal1, negedge signal2, …)
The positive edge or negative edge of each signal can be specified in the sensitivity list

## Slide 9: Modeling a D Latch with Enable
// Modeling a D Latch with Enable and output Q
// Output Q must be of type reg
// Notice that the if statement does NOT have else
// If Enable is 0, then value of Q does not change
// The D_latch stores the old value of Q
module D_latch (input D, Enable, output reg Q);
always @(D, Enable)
if (Enable) Q <= D; // Non-blocking assignment
endmodule

## Slide 10: Modeling a D-type Flip-Flop
// Modeling a D Flip-Flop with outputs Q and Qbar
module D_FF (input D, Clk, output reg Q, Qbar);
// Q and Qbar change at the positive edge of Clk
// Notice that always is NOT sensitive to D
always @(posedge Clk)
begin
Q <= D; // Non-blocking assignment
Qbar <= ~D; // Non-blocking assignment
end
endmodule

## Slide 11: Negative-Edge Triggered D-type Flip-Flop
// Modeling a Negative-Edge Triggered D Flip-Flop
// The only difference is the negative edge of Clk
module D_FF2 (input D, Clk, output reg Q, Qbar);
// Q and Qbar change at the negative edge of Clk
always @(negedge Clk)
begin
Q <= D; // Non-blocking assignment
Qbar <= ~D; // Non-blocking assignment
end
endmodule

## Slide 12: D-type Flip-Flop with Synchronous Reset
// Modeling a D Flip-Flop with Synchronous Reset input
module D_FF3 (input D, Clk, Reset, output reg Q, Qbar);
// always block is NOT sensitive to Reset or D
// Updates happen only at positive edge of Clk
// Reset is Synchronized with Clk
always @(posedge Clk)
if (Reset)
{Q, Qbar} <= 2'b01;
else
{Q, Qbar} <= {D, ~D};
endmodule

## Slide 13: D-type Flip-Flop with Asynchronous Reset
// Modeling a D Flip-Flop with Asynchronous Reset input
module D_FF (input D, Clk, Reset, output reg Q, Qbar);
// Q and Qbar change at the positive edge of Clk
// Or, at the positive edge of Reset
// Reset is NOT synchronized with Clk
always @(posedge Clk, posedge Reset)
if (Reset)
{Q, Qbar} <= 2'b01;
else
{Q, Qbar} <= {D, ~D};
endmodule

## Slide 14: Structural Modeling of Sequential Circuits
// Mixed Structural and Dataflow
module Seq_Circuit_Structure
(input x, Clock, output y);
wire DA, DB, A, Ab, B, Bb;
// Instantiate two D Flip-Flops
D_FF FFA(DA, Clock, A, Ab);
D_FF FFB(DB, Clock, B, Bb);
// Modeling logic
assign DA = (A & x) | (B & x);
assign DB = Ab & x;
assign y = (A | B) & ~x;
endmodule
Modeling the Circuit Structure

## Slide 15: Behavioral Modeling of Sequential Circuits
module Seq_Circuit_Behavior
(input x, Clock, output y);
// reg A, B for the Flip-Flops
reg A, B;
// Modeling using always block
// Update A, B at positive edge
// Non-Blocking assignment
always @(posedge Clock) begin
A <= (A & x) | (B & x);
B <= ~A & x;
end
// Output y: assign statement
assign y = (A | B) & ~x;
endmodule
Modeling the Circuit Behavior

## Slide 16: Verifying Structural and Behavioral Models
module Seq_Circuit_TB; // Test Bench
reg x, clk;
wire y, z;
// Instantiate structural and behavioral sequential circuits
// Same inputs x and clk, but different outputs y and z
Seq_Circuit_Structure test1 (x, clk, y);
Seq_Circuit_Behavior test2 (x, clk, z);
// Generate a clock with period = 10 ns
initial clk = 1;
always #5 clk = ~clk;
// Test sequence: x = 0, 1, 0, 1, 1, 0, 1, 1, 1, 1, 0, . . .
initial begin
x=0; #12 x=1; #10 x=0; #10 x=1; #20 x=0; #10 x=1; #40 x=0;
end
endmodule

## Slide 17: Simulation Waveforms
Structural and behavioral descriptions have identical waveforms

## Slide 18: Modeling a State Diagram
A state diagram can be modeled directly in Verilog
Without the need of having the circuit implementation
An example of a Mealy state diagram is shown below
This is the state diagram of the 111 sequence detector
State assignment: S0 = 00, S1 = 01, and S2 = 10
0 / 0
0 / 0
00
0 / 0
reset
1 / 0
01
1 / 0
10
1 / 1

## Slide 19: Modeling a Mealy State Diagram
module Mealy_111_detector (input x, clock, reset, output z);
reg [1:0] state; // present state
always @(posedge clock, posedge reset)
if (reset) state <= 'b00;
else case(state)
'b00: if (x) state <= 'b01; else state <= 'b00;
'b01: if (x) state <= 'b10; else state <= 'b00;
'b10: if (x) state <= 'b10; else state <= 'b00;
endcase
// output depends on present state and input x
assign z = (state == 'b10) & x;
endmodule
0 / 0
0 / 0
00
0 / 0
reset
1 / 0
01
1 / 0
10
1 / 1

## Slide 20: Modeling a Moore State Diagram
module Moore_Comparator (input A, B, clk, rst, output GT, LT, EQ);
reg [1:0] state; // present state
assign GT = state[1];
assign LT = state[0];
assign EQ = ~(GT | LT);
always @(posedge clk, posedge rst)
if (rst) state <= 'b00;
else case (state)
'b00: state <= ({A,B}=='b01)?'b01:
({A,B}=='b10)?'b10:'b00;
'b01: state <= ({A,B}=='b10)?'b10:'b01;
'b10: state <= ({A,B}=='b01)?'b01:'b10;
endcase
endmodule
01
10
00
11
01
00
11
10
10
100
10
01
01
010
00
001
rst
00, 11

## Slide 21: Test Bench for the Moore Comparator
module Moore_Comparator_TB; // Test Bench
reg A, B, clk, rst;
wire GT, LT, EQ;
Moore_Comparator test (A, B, clk, rst, GT, LT, EQ);
// Reset pulse
initial begin #2 rst = 1; #4 rst = 0; end
// Generate clock
initial clk = 1;
always #5 clk = ~clk;
// Generate input test sequence
initial begin
{A,B}='b00; #12 {A,B}='b11; #10 {A,B}='b01; #10 {A,B}='b11;
#10 {A,B}='b10; #10 {A,B}='b00; #10 {A,B}='b01; #20 {A,B}='b10;
end
endmodule

## Slide 22: Moore Comparator Waveforms

## Slide 23: Modeling a Register with Parallel Load
module Register #(parameter n = 4)
(input [n-1:0] Data_in, input clock, reset,
output reg [n-1:0] Data_out);
always @(posedge clock, posedge reset) // Asynchronous reset
if (reset) Q <= 0;
else if (load) Data_out <= Data_in;
endmodule

## Slide 24: Modeling a Shift Register
module Shift_Register #(parameter n = 4)
(input Data_in, clock, reset, output Data_out);
reg [n-1:0] Q;
assign Data_out = Q[0];
always @(posedge clock, negedge reset) // Asynchronous reset
if (!reset) Q <= 0; // Active Low reset
else Q <= {Data_in, Q[n-1:1]}; // Shifts to the right
endmodule

## Slide 25: Modeling a Generic Up-Down Counter
module Up_Down_Counter #(parameter n = 16) // n-bit counter
( input [n-1:0] Data_in,
input [1:0] f, input reset, clock,
output reg [n-1:0] Count );
// Asynchronous reset
always @(posedge clock, posedge reset)
if (reset) Count <= 0;
else if (f == 1) Count <= Count + 1;
else if (f == 2) Count <= Count – 1;
else if (f == 3) Count <= Data_in;
endmodule
Up-Down
Counter
n
n
Data_in
Count
f
clock
2
reset
f = 0  Disable counter
f = 1  Count up
f = 2  Count down
f = 3  Load counter

## Slide 26: Test Bench for the Up-Down Counter
module Up_Down_Counter_TB; // Test Bench
reg [7:0] Data_in; reg [1:0] f; reg rst, clk; wire [7:0] Count;
// Instantiate an 8-bit test counter
Up_Down_Counter #(8) test (Data_in, f, rst, clk, Count);
// Initialize Data_in (in hexadecimal)
initial Data_in = 8'h2A;
// Generate reset pulse
initial begin #2 rst=1; #4 rst=0; end
// Generate clock
initial clk = 1; always #5 clk = ~clk;
// Generate function sequence
initial begin
#2 f=3; #10 f=1; #30 f=2; #10 f=0; #10 f=1;
end
endmodule

## Slide 27: Up-Down Counter Waveforms