## Slide 1: The Karnaugh Map
COE 202
Digital Logic Design
Dr. Muhamed Mudawar
King Fahd University of Petroleum and Minerals

## Slide 2: Presentation Outline
Boolean Function Minimization
The Karnaugh Map (K-Map)
Two, Three, and Four-Variable K-Maps
Prime and Essential Prime Implicants
Minimal Sum-of-Products and Product-of-Sums
Don't Cares
Five and Six-Variable K-Maps
Multiple Outputs

## Slide 3: Boolean Function Minimization
Complexity of a Boolean function is directly related to the complexity of the algebraic expression
The truth table of a function is unique
However, the algebraic expression is not unique
Boolean function can be simplified by algebraic manipulation
However, algebraic manipulation depends on experience
Algebraic manipulation does not guarantee that the simplified Boolean expression is minimal

## Slide 4: Example: Sum of Minterms
Sum-of-Minterms has 15 literals  Can be simplified
Truth Table
x y z | f | Minterm
0 0 0 | 0 | 
0 0 1 | 1 | 
0 1 0 | 1 | 
0 1 1 | 1 | 
1 0 0 | 0 | 
1 0 1 | 1 | 
1 1 0 | 0 | 
1 1 1 | 1 | 
x y z | f | Minterm
0 0 0 | 0 | 
0 0 1 | 1 | 
0 1 0 | 1 | 
0 1 1 | 1 | 
1 0 0 | 0 | 
1 0 1 | 1 | 
1 1 0 | 0 | 
1 1 1 | 1 | 
Focus on the ‘1’ entries

## Slide 5: Algebraic Manipulation
Simplify: (15 literals)
(Sum-of-Minterms)
Reorder
Distributive · over +
Simplify (7 literals)
Reorder
Distributive · over +
Simplify (4 literals)
Distributive + over ·
Simplify (3 literals)

## Slide 6: Drawback of Algebraic Manipulation
No clear steps in the manipulation process
  Not clear which terms should be grouped together
  Not clear which property of Boolean algebra should be used next
Does not always guarantee a minimal expression
  Simplified expression may or may not be minimal
  Different steps might lead to different non-minimal expressions
However, the goal is to minimize a Boolean function
Minimize the number of literals in the Boolean expression
  The literal count is a good measure of the cost of logic implementation
  Proportional to the number of transistors in the circuit implementation

## Slide 7: Karnaugh Map
Called also K-map for short
The Karnaugh map is a diagram made up of squares
It is a reorganized version of the truth table
Each square in the Karnaugh map represents a minterm
Adjacent squares differ in the value of one variable
Simplified expressions can be derived from the Karnaugh map
  By recognizing patterns of squares
Simplified sum-of-products expression (AND-OR circuits)
Simplified product-of-sums expression (OR-AND circuits)

## Slide 8: Next . . .
Boolean Function Minimization
The Karnaugh Map (K-Map)
Two, Three, and Four-Variable K-Maps
Prime and Essential Prime Implicants
Minimal Sum-of-Products and Product-of-Sums
Don't Cares
Five and Six-Variable K-Maps
Multiple Outputs

## Slide 9: Two-Variable Karnaugh Map
Minterms and are adjacent (also, and )
  They differ in the value of variable
Minterms and are adjacent (also, and )
  They differ in the value of variable
m3
m2
1
m1
m0
0
1
0
x
y
x y
x y'
1
x' y
x' y'
0
1
0
x
y
Two-variable K-map

## Slide 10: From a Truth Table to Karnaugh Map
Given a truth table, construct the corresponding K-map
Copy the function values from the truth table into the K-map
Make sure to copy each value into the proper K-map square
x y | f
0 0 | 1
0 1 | 0
1 0 | 1
1 1 | 1
Truth Table
1
1
1
0
1
0
1
0
x
y
K-map

## Slide 11: K-Map Function Minimization
Two adjacent cells containing 1's can be combined
(6 literals)
Therefore, can be simplified as: (2 literals)
1
1
1
0
1
0
1
0
x
y
K-map

## Slide 12: Three-Variable Karnaugh Map
Have eight squares (for the 8 minterms), numbered 0 to 7
The last two columns are not in numeric order: 11, 10
  Remember the numbering of the squares in the K-map
Each square is adjacent to three other squares
Minterms in adjacent squares can always be combined
  This is the key idea that makes the K-map work
Labeling of rows and columns is also useful
00
01
11
10
0
1
00
01
11
10
0
1

## Slide 13: Simplifying a Three-Variable Function
Simplify the Boolean function:
(12 literals)
Mark ‘1’ all the K-map squares that represent function
Find possible adjacent squares
Therefore, (4 literals)
00
01
11
10
0
1
0
0
1
0
1
1
1
0

## Slide 14: Simplifying a Three-Variable Function (2)
Here is a second example:
(12 literals)
Learn the locations of the 8 indices based on the variable order
Corner squares can be combined
Therefore, (4 literals)
00
01
11
10
0
1
0
0
1
0
1
0
1
1

## Slide 15: Combining Squares on a 3-Variable K-Map
By combining squares, we reduce number of literals in a product term, thereby reducing the cost
On a 3-variable K-Map:
  One square represents a minterm with 3 variables
  Two adjacent squares represent a term with 2 variables
  Four adjacent squares represent a term with 1 variable
  Eight adjacent square is the constant ‘1’ (no variables)

## Slide 16: Example of Combining Squares
Consider the Boolean function:
00
01
11
10
0
1
0
0
1
1
0
1
1
1
The four minterms that form the 2×2 red square are reduced to the term
The two minterms that form the blue rectangle are reduced to the term
Therefore:

## Slide 17: Minimal Sum-of-Products Expression
Consider the function:
Find a minimal sum-of-products (SOP) expression
Solution:
Red block: term =
Green block: term =
Blue block: term =
Minimal sum-of-products: (5 literals)
00
01
11
10
0
1
1
1
0
1
1
0
1
1

## Slide 18: Four-Variable Karnaugh Map
4 variables  16 squares
Remember the numbering of the squares in the K-map
Each square is adjacent to four other squares
00
01
11
10
00
01
11
10
Notice the order of Rows 11 and 10
and the order of columns 11 and 10

## Slide 19: Combining Squares on a 4-Variable K-Map
On a 4-variable K-Map:
  One square represents a minterm with 4 variables
  Two adjacent squares represent a term with 3 variables
  Four adjacent squares represent a term with 2 variables
  Eight adjacent squares represent a term with 1 variable
  Combining all 16 squares is the constant ‘1’ (no variables)

## Slide 20: Combining Eight Squares
00
01
11
10
00
01
11
10
Term =
Term =
Term =

## Slide 21: Combining Four Squares
00
01
11
10
00
01
11
10
Term =
Term =
Term =

## Slide 22: Combining Two Squares
00
01
11
10
00
01
11
10
Term =
Term =
Term =
Term =

## Slide 23: Simplifying a 4-Variable Function
Given
Draw the K-map for function
Minimize as sum-of-products
Solution:
00
01
11
10
00
1
0
0
1
1
1
1
1
01
11
10
1
0
0
0
1
0
0
0
Term =
Term =
Term =

## Slide 24: Next . . .
Boolean Function Minimization
The Karnaugh Map (K-Map)
Two, Three, and Four-Variable K-Maps
Prime and Essential Prime Implicants
Minimal Sum-of-Products and Product-of-Sums
Don't Cares
Five and Six-Variable K-Maps
Multiple Outputs

## Slide 25: Prime Implicants
Prime Implicant: a product term obtained by combining the maximum number of adjacent squares in the K-map
The number of combined squares must be a power of 2
Essential Prime Implicant: is a prime implicant that covers at least one minterm not covered by the other prime implicants
The prime implicants and essential prime implicants can be determined by inspecting the K-map

## Slide 26: Example of Prime Implicants
Find all the prime implicants and essential prime implicants for:
Six Prime Implicants
, , , , ,
Only Two Prime Implicants are essential
and
00
01
11
10
00
1
1
1
1
1
01
11
10
1
1
1
1
1
1
K-Map

## Slide 27: Simplification Procedure Using the K-Map
Find all the essential prime implicants
  Covering maximum number (power of 2) of 1's in the K-map
  Mark the minterm(s) that make the prime implicants essential
Add prime implicants to cover the function
  Choose a minimal subset of prime implicants that cover all remaining 1's
  Make sure to cover all 1's not covered by the essential prime implicants
  Minimize the overlap among the additional prime implicants
Sometimes, a function has multiple simplified expressions
  You may be asked to list all the simplified sum-of-product expressions

## Slide 28: Obtaining All Minimal SOP Expressions
Consider again:
Obtain all minimal sum-of-products (SOP) expressions
Two essential Prime Implicants: and
00
01
11
10
00
1
1
1
1
1
01
11
10
1
1
1
1
1
1
K-Map
Four possible solutions:

## Slide 29: Product-of-Sums (POS) Simplification
All previous examples were expressed in Sum-of-Products form
With a minor modification, the Product-of-Sums can be obtained
Example:
00
01
11
10
00
1
1
1
01
11
10
1
1
1
1
1
1
K-Map of
00
01
11
10
00
1
01
11
10
1
1
1
1
1
1
K-Map of
Minimal Sum-of-Products = 8 literals
All prime implicants are essential
Minimal Product-of-Sums = 4 literals

## Slide 30: Product-of-Sums Simplification Procedure
Draw the K-map for the function
  Obtain a minimal Sum-of-Products (SOP) expression for
Draw the K-map for , replacing the 0's of with 1's in
Obtain a minimal Sum-of-Products (SOP) expression for
Use DeMorgan's theorem to obtain
  The result is a minimal Product-of-Sums (POS) expression for
Compare the cost of the minimal SOP and POS expressions
  Count the number of literals to find which expression is minimal

## Slide 31: Next . . .
Boolean Function Minimization
The Karnaugh Map (K-Map)
Two, Three, and Four-Variable K-Maps
Prime and Essential Prime Implicants
Minimal Sum-of-Products and Product-of-Sums
Don't Cares
Five and Six-Variable K-Maps
Multiple Outputs

## Slide 32: Don't Cares
Sometimes, a function table may contain entries for which:
  The input values of the variables will never occur, or
  The output value of the function is never used
In this case, the output value of the function is not defined
The output value of the function is called a don't care
A don't care is an X value that appears in the function table
The X value can be later chosen to be 0 or 1
  To minimize the function implementation

## Slide 33: Example of a Function with Don't Cares
Consider a function defined over BCD inputs
The function input is a BCD digit from 0 to 9
The function output is 0 if the BCD input is 0 to 4
The function output is 1 if the BCD input is 5 to 9
The function output is X (don't care) if the input is 10 to 15 (not BCD)
a b c d | f
0 0 0 0 | 0
0 0 0 1 | 0
0 0 1 0 | 0
0 0 1 1 | 0
0 1 0 0 | 0
0 1 0 1 | 1
0 1 1 0 | 1
0 1 1 1 | 1
1 0 0 0 | 1
1 0 0 1 | 1
1 0 1 0 | X
1 0 1 1 | X
1 1 0 0 | X
1 1 0 1 | X
1 1 1 0 | X
1 1 1 1 | X
Truth Table
Minterms
Don't Cares

## Slide 34: Minimizing Functions with Don't Cares
Consider:
If the don't cares were treated as 0's we get:
(9 literals)
If the don't cares were treated as 1's we get:
(5 literals)
00
01
11
10
00
01
11
10
K-Map of
0
0
0
0
1
1
1
0
X
X
X
X
1
X
X
1
The don't care values can be selected to be either 0 or 1, to produce a minimal expression

## Slide 35: Simplification Procedure with Don't Cares
Find all the essential prime implicants
  Covering maximum number (power of 2) of 1's and X's (don't cares)
  Mark the 1's that make the prime implicants essential
Add prime implicants to cover the function
  Choose a minimal subset of prime implicants that cover all remaining 1's
  Make sure to cover all 1's not covered by the essential prime implicants
  Minimize the overlap among the additional prime implicants
  You need not cover all the don't cares (some can remain uncovered)
Sometimes, a function has multiple simplified expressions

## Slide 36: Minimizing Functions with Don't Cares (2)
Simplify:
Solution 1: (4 literals)
Solution 2: (4 literals)
00
01
11
10
00
01
11
10
K-Map of
1
1
X
X
X
1
0
0
0
1
0
0
0
1
0
0
00
01
11
10
00
01
11
10
K-Map of
1
1
X
X
X
1
0
0
0
1
0
0
0
1
0
0
Not all don't cares need be covered
Prime Implicant is essential

## Slide 37: Minimal Product-of-Sums with Don't Cares
Simplify:
Obtain a product-of-sums minimal expression
Solution:
Minimal (3 literals)
Minimal product-of-sums:
(3 literals)
00
01
11
10
00
01
11
10
K-Map of
0
0
X
X
X
0
1
1
1
0
1
1
1
0
1
1
The minimal sum-of-products expression for had 4 literals

## Slide 38: Next . . .
Boolean Function Minimization
The Karnaugh Map (K-Map)
Two, Three, and Four-Variable K-Maps
Prime and Essential Prime Implicants
Minimal Sum-of-Products and Product-of-Sums
Don't Cares
Five and Six-Variable K-Maps
Multiple Outputs

## Slide 39: Five-Variable Karnaugh Map
Consists of 25 = 32 squares, numbered 0 to 31
  Remember the numbering of squares in the K-map
Can be visualized as two layers of 16 squares each
Top layer contains the squares of the first 16 minterms ()
Bottom layer contains the squares of the last 16 minterms ()
00
01
11
10
00
01
11
10
00
01
11
10
00
01
11
10
Each square is adjacent to 5 other squares:
4 in the same layer and
1 in the other layer:
is adjacent to
is adjacent to
is adjacent to …

## Slide 40: Example of a Five-Variable K-Map
Given:
Draw the 5-Variable K-Map
Obtain a minimal Sum-of-Products expression for
Solution: (6 literals)
00
01
11
10
00
01
11
10
00
01
11
10
00
01
11
10
5-Variable K-Map
1
1
1
1
1
1
1
1
1
1

## Slide 41: Five-Variable K-Map with Don't Cares
Draw the 5-Variable K-Map
Obtain a minimal Sum-of-Products expression for
Solution: (8 literals)
00
01
11
10
00
01
11
10
00
01
11
10
00
01
11
10
5-Variable K-Map
1
X
X
1
1
X
X
1
1
1
1
X
X
1
1
All prime implicants are essential
Not covered

## Slide 42: Six-Variable Karnaugh Map
Consists of 26 = 64 squares, numbered 0 to 63
Can be visualized as four layers of 16 squares each
  Four layers: (Notice that layer 11 comes before 10)
Each square is adjacent to 6 other squares:
  4 squares in the same layer and 2 squares in the above and below layers
00
01
11
10
00
01
11
10
00
01
11
10
00
01
11
10
00
01
11
10

## Slide 43: Example of a Six-Variable K-Map
Draw the 6-Variable K-Map
Obtain a minimal Sum-of-Products expression for
Solution: (18 literals)
00
01
11
10
00
01
11
10
00
01
11
10
00
01
11
10
00
01
11
10
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1

## Slide 44: Next . . .
Boolean Function Minimization
The Karnaugh Map (K-Map)
Two, Three, and Four-Variable K-Maps
Prime and Essential Prime Implicants
Minimal Sum-of-Products and Product-of-Sums
Don't Cares
Five and Six-Variable K-Maps
Multiple Outputs

## Slide 45: Multiple Outputs
Suppose we have two functions: and
Same inputs: , but two outputs: and
We can minimize each function separately, or
Minimize and as one circuit with two outputs
The idea is to share terms (gates) among and
One circuit with
Two Outputs
Two separate circuits

## Slide 46: Multiple Outputs: Example 1
Given: and
Minimize each function separately
Minimize both functions as one circuit
00
01
11
10
0
1
1
0
0
1
0
0
1
1
K-Map of
00
01
11
10
0
1
0
1
1
0
0
0
1
1
K-Map of
Common
Term =
One circuit with
two Outputs
One circuit per function

## Slide 47: Multiple Outputs: Example 2
,
Draw the K-map and write minimal SOP expressions of and
Extract the common terms of and
1
1
00
01
11
10
00
01
11
10
K-Map of
1
1
1
1
1
00
01
11
10
00
01
11
10
K-Map of
1
1
1
1
1
1
Common Terms
and
Minimal and

## Slide 48: Common Terms  Shared Gates
Minimal Minimal
Let and (shared by and )
Minimal , Minimal
One Circuit
Two Shared Gates
NO Shared Gates