## Slide 1: Additional Gates
COE 202
Digital Logic Design
Dr. Muhamed Mudawar
King Fahd University of Petroleum and Minerals

## Slide 2: Presentation Outline
Additional Gates and Symbols
Universality of NAND and NOR gates
NAND-NAND and NOR-NOR implementations
Exclusive OR (XOR) and Exclusive NOR (XNOR) gates
Odd and Even functions

## Slide 3: Additional Logic Gates and Symbols
Why?
  Low cost implementation
  Useful in implementing Boolean functions
AND gate
OR gate
NOT gate (inverter)
NAND gate
NOR gate
XOR gate
XNOR gate
Buffer
3-state gate

## Slide 4: NAND Gate
The NAND gate has the following symbol and truth table
NAND represents NOT AND
The small bubble circle represents the invert function
NAND gate is implemented efficiently in CMOS technology
  In terms of chip area and speed
x y | NAND
0 0 | 1
0 1 | 1
1 0 | 1
1 1 | 0
NAND gate
Another symbol for NAND

## Slide 5: NOR Gate
The NOR gate has the following symbol and truth table
NOR represents NOT OR
The small bubble circle represents the invert function
NOR gate is implemented efficiently in CMOS technology
  In terms of chip area and speed
x y | NOR
0 0 | 1
0 1 | 0
1 0 | 0
1 1 | 0
NOR gate
Another symbol for NOR

## Slide 6: The NAND Gate is Universal
NAND gates can implement any Boolean function
NAND gates can be used as inverters, or to implement AND/OR
A single-input NAND gate is an inverter
NAND = =
AND is equivalent to NAND with inverted output
( NAND ) = = (AND)
OR is equivalent to NAND with inverted inputs
( NAND ) = = (OR)

## Slide 7: The NOR Gate is also Universal
NOR gates can implement any Boolean function
NOR gates can be used as inverters, or to implement AND/OR
A single-input NOR gate is an inverter
NOR = =
OR is equivalent to NOR with inverted output
( NOR ) = = (OR)
AND is equivalent to NOR with inverted inputs
( NOR ) = = (AND)

## Slide 8: Non-Associative NAND / NOR Operations
Unlike AND, NAND operation is NOT associative
( NAND ) NAND ≠ NAND ( NAND )
( NAND ) NAND =
NAND ( NAND ) =
Unlike OR, NOR operation is NOT associative
( NOR ) NOR ≠ NOR ( NOR )
( NOR ) NOR =
NOR ( NOR ) =

## Slide 9: Multiple-Input NAND / NOR Gates
NAND/NOR gates can have multiple inputs, similar to AND/OR gates
2-input NAND gate
3-input NAND gate
4-input NAND gate
2-input NOR gate
3-input NOR gate
4-input NOR gate
Note: a 3-input NAND is a single gate, NOT a combination of two 2-input gates. The same can be said about other multiple-input NAND/NOR gates.

## Slide 10: NAND – NAND Implementation
Consider the following sum-of-products expression:
A 2-level AND-OR circuit can be converted easily to a 2-level NAND-NAND implementation
2-Level AND-OR
Inserting Bubbles
Two successive bubbles on same line cancel each other
2-Level NAND-NAND
3-input
NAND gate
3-input
AND gate

## Slide 11: NOR – NOR Implementation
Consider the following product-of-sums expression:
A 2-level OR-AND circuit can be converted easily to a 2-level NOR-NOR implementation
Two successive bubbles on same line cancel each other
2-Level OR-AND
Inserting Bubbles
2-Level NOR-NOR
3-input
NOR gate
3-input
OR gate

## Slide 12: Exclusive OR / Exclusive NOR
Exclusive OR (XOR) is an important Boolean operation used extensively in logic circuits
Exclusive NOR (XNOR) is the complement of XOR
XOR gate
XNOR gate
x y | XOR
0 0 | 0
0 1 | 1
1 0 | 1
1 1 | 0
x y | XNOR
0 0 | 1
0 1 | 0
1 0 | 0
1 1 | 1
XNOR is also known as equivalence

## Slide 13: XOR / XNOR Functions
The XOR function is:
The XNOR function is:
XOR and XNOR gates are complex
  Can be implemented as a true gate, or by
  Interconnecting other gate types
XOR and XNOR gates do not exist for more than two inputs
  For 3 inputs, use two XOR gates
  The cost of a 3-input XOR gate is greater than the cost of two XOR gates
Uses for XOR and XNOR gates include:
  Adders, subtractors, multipliers, counters, incrementers, decrementers
  Parity generators and checkers

## Slide 14: XOR and XNOR Properties
XOR and XNOR are associative operations

## Slide 15: Odd Function
Output is 1 if the number of 1's is odd in the inputs
Output is the XOR operation on all input variables
x y z | fodd
0 0 0 | 0
0 0 1 | 1
0 1 0 | 1
0 1 1 | 0
1 0 0 | 1
1 0 1 | 0
1 1 0 | 0
1 1 1 | 1
Odd Function with 3 inputs
Implementation using two XOR gates

## Slide 16: Even Function
Output is 1 if the number of 1's is even in the inputs (complement of odd function)
Output is the XNOR operation on all inputs
w x y z | feven
0 0 0 0 | 1
0 0 0 1 | 0
0 0 1 0 | 0
0 0 1 1 | 1
0 1 0 0 | 0
0 1 0 1 | 1
0 1 1 0 | 1
0 1 1 1 | 0
1 0 0 0 | 0
1 0 0 1 | 1
1 0 1 0 | 1
1 0 1 1 | 0
1 1 0 0 | 1
1 1 0 1 | 0
1 1 1 0 | 0
1 1 1 1 | 1
Even Function with 4 inputs
Implementation using two XOR gates and one XNOR

## Slide 17: Parity Generators and Checkers
A parity bit is added to the n-bit code
  Produces (n+1)-bit code with an odd (or even) count of 1's
Odd parity: count of 1's in the (n+1)-bit code is odd
  Use an even function to generate the odd parity bit
  Use an even function to check the (n+1)-bit code
Even parity: count of 1's in the (n+1)-bit code is even
  Use an odd function to generate the even parity bit
  Use an odd function to check the (n+1)-bit code
Sender
Receiver
n-bit code
Parity
Generator
(n+1)-bit code
Parity
Checker
Error

## Slide 18: Example of Parity Generator and Checker
Design even parity generator & checker for 3-bit codes
Solution:
  Use 3-bit odd function to generate even parity bit .
  Use 4-bit odd function to check if there is an error in even parity.
  Given that: = 001 then = 1. The sender transmits = 1001.
  If changes from 0 to 1 between generator and checker, the parity checker receives = 1011 and produces = 1, indicating an error.
Parity Generator
Parity Checker