## Slide 1: Combinational Circuit Design
COE 202
Digital Logic Design
Dr. Muhamed Mudawar
King Fahd University of Petroleum and Minerals

## Slide 2: Presentation Outline
How to Design a Combinational Circuit
Designing a BCD to Excess-3 Code Converter
Designing a BCD to 7-Segment Decoder
Hierarchical Design
Iterative Design

## Slide 3: Combinational Circuit
A combinational circuit is a block of logic gates having:
inputs:
outputs:
Each output is a function of the input variables
Each output is determined from present combination of inputs
Combination circuit performs operation specified by logic gates

Combinational
Circuit

inputs
outputs

## Slide 4: How to Design a Combinational Circuit
Specification
  Specify the inputs, outputs, and what the circuit should do
Formulation
  Convert the specification into truth tables or logic expressions for outputs
Logic Minimization
  Minimize the output functions using K-map or Boolean algebra
Technology Mapping
  Draw a logic diagram using ANDs, ORs, and inverters
  Map the logic diagram into the selected technology
  Considerations: cost, delays, fan-in, fan-out
Verification
  Verify the correctness of the design, either manually or using simulation

## Slide 5: Designing a BCD to Excess-3 Code Converter
Specification
  Convert BCD code to Excess-3 code
  Input: BCD code for decimal digits 0 to 9
  Output: Excess-3 code for digits 0 to 9
Formulation
  Done easily with a truth table
  BCD input:
  Excess-3 output:
  Output is don't care for 1010 to 1111
BCD a b c d | Excess-3 w x y z
0 0 0 0 | 0 0 1 1
0 0 0 1 | 0 1 0 0
0 0 1 0 | 0 1 0 1
0 0 1 1 | 0 1 1 0
0 1 0 0 | 0 1 1 1
0 1 0 1 | 1 0 0 0
0 1 1 0 | 1 0 0 1
0 1 1 1 | 1 0 1 0
1 0 0 0 | 1 0 1 1
1 0 0 1 | 1 1 0 0
1010 to 1111 | X X X X

## Slide 6: Designing a BCD to Excess-3 Code Converter
Logic Minimization using K-maps
00
01
11
10
00
K-map for
01
11
10
K-map for
K-map for
K-map for
00
01
11
10
00
01
11
10
00
01
11
10
1
1
1
1
1
1
1
X
X
X
X
X
X
1
1
1
1
1
X
X
X
X
X
X
1
1
X
X
X
X
X
X
1
1
X
X
X
X
X
X
1
1
1
1
Minimal Sum-of-Product expressions:
, , ,
Additional 3-Level Optimizations: extract common term
, ,

## Slide 7: Designing a BCD to Excess-3 Code Converter
Technology Mapping
Draw a logic diagram using ANDs, ORs, and inverters
Other gates can be used, such as NAND, NOR, and XOR
a
b
c
d
w
x
y
z
Using XOR gates
a
b
c
d
w
x
y
z

## Slide 8: Designing a BCD to Excess-3 Code Converter
Verification
  Can be done manually
  Extract output functions from circuit diagram
  Find the truth table of the circuit diagram
  Match it against the specification truth table
  Verification process can be automated
  Using a simulator for complex designs
a
b
c
d
w = a + b(c + d)
x = b  (c + d)
y = c  d'
z = d'
BCD a b c d | c+d | b(c+d) | Excess-3 w x y z
0 0 0 0 | 0 | 0 | 0 0 1 1
0 0 0 1 | 1 | 0 | 0 1 0 0
0 0 1 0 | 1 | 0 | 0 1 0 1
0 0 1 1 | 1 | 0 | 0 1 1 0
0 1 0 0 | 0 | 0 | 0 1 1 1
0 1 0 1 | 1 | 1 | 1 0 0 0
0 1 1 0 | 1 | 1 | 1 0 0 1
0 1 1 1 | 1 | 1 | 1 0 1 0
1 0 0 0 | 0 | 0 | 1 0 1 1
1 0 0 1 | 1 | 0 | 1 1 0 0
Truth Table of the
Circuit Diagram

## Slide 9: BCD to 7-Segment Decoder
Seven-Segment Display:
  Made of Seven segments: light-emitting diodes (LED)
  Found in electronic devices: such as clocks, calculators, etc.
BCD to 7-Segment Decoder
  Accepts as input a BCD decimal digit (0 to 9)
  Generates output to the seven LED segments to display the BCD digit
  Each segment can be turned on or off separately
BCD to
7-Segment
Decoder
A
B
C
D
a
b
c
d
e
f
g

## Slide 10: Designing a BCD to 7-Segment Decoder
Specification:
  Input: 4-bit BCD (A, B, C, D)
  Output: 7-bit (a, b, c, d, e, f, g)
  Display should be OFF for
  Non-BCD input codes
Formulation
  Done with a truth table
  Output is zero for 1010 to 1111
BCD input A B C D | 7-Segment decoder a b c d e f g
0 0 0 0 | 1 1 1 1 1 1 0
0 0 0 1 | 0 1 1 0 0 0 0
0 0 1 0 | 1 1 0 1 1 0 1
0 0 1 1 | 1 1 1 1 0 0 1
0 1 0 0 | 0 1 1 0 0 1 1
0 1 0 1 | 1 0 1 1 0 1 1
0 1 1 0 | 1 0 1 1 1 1 1
0 1 1 1 | 1 1 1 0 0 0 0
1 0 0 0 | 1 1 1 1 1 1 1
1 0 0 1 | 1 1 1 1 0 1 1
1010 to 1111 | 0 0 0 0 0 0 0
Truth Table

## Slide 11: Designing a BCD to 7-Segment Decoder
Logic Minimization Using K-Maps
1
00
01
11
10
00
K-map for
01
11
10
1
1
1
1
1
1
1
00
01
11
10
00
K-map for
01
11
10
1
1
1
1
1
1
1
1
00
01
11
10
00
K-map for
01
11
10
1
1
1
1
1
1
1
1
1
Extracting common terms
Let
Optimized Logic Expressions
are shared gates

## Slide 12: Designing a BCD to 7-Segment Decoder
Logic Minimization Using K-Maps
00
01
11
10
00
K-map for
01
11
10
1
1
1
1
1
1
1
00
01
11
10
00
K-map for
01
11
10
1
1
1
1
00
01
11
10
00
K-map for
01
11
10
1
1
1
1
1
1
00
01
11
10
00
K-map for
01
11
10
1
1
1
1
1
1
1
Optimized Logic Expressions
Common AND Terms
 Shared Gates

## Slide 13: Designing a BCD to 7-Segment Decoder
Technology Mapping
Many Common AND terms: thru
Optimized Logic Expressions
Showing only
Outputs e, f, g
T4
T2
T5
A
B'
C'
D'
T0
T6
T7
B'
A'
C
D'
T8
T1
T9
C'
A'
B
D'
e
f
g

## Slide 14: Verification Methods
Manual Logic Analysis
  Find the logic expressions and truth table of the final circuit
  Compare the final circuit truth table against the specified truth table
  Compare the circuit output expressions against the specified expressions
  Tedious for large designs + Human Errors
Simulation
  Simulate the final circuit, possibly written in HDL (such as Verilog)
  Write a test bench that automates the verification process
  Generate test cases for ALL possible inputs (exhaustive testing)
  Verify the output correctness for ALL input test cases
  Exhaustive testing can be very time consuming for many inputs

## Slide 15: Modeling the 7-Segment Decoder
// Module BCD_to_7Segment: Modeled using continuous assignment
module BCD_to_7Segment (input A,B,C,D, output a,b,c,d,e,f,g);
wire T0, T1, T2, T3, T4, T5, T6, T7, T8, T9;
assign T0=~A&C; assign T1=~A&B; assign T2=~B&~C;
assign T3=~A&D; assign T4=T2&A; assign T5=T2&~D;
assign T6=T0&~B; assign T7=T0&~D; assign T8=T1&~C;
assign T9=T1&~D;
assign a = T0 | T1&D | T4 | T5;
assign b = ~A&~B | T2 | ~A&~C&~D | T3&C;
assign c = T1 | T2 | T3;
assign d = T4 | T5 | T6 | T7 | T8&D;
assign e = T5 | T7;
assign f = T4 | T5 | T8 | T9;
assign g = T4 | T6 | T8 | T9;
endmodule
assign statements can appear in any order

## Slide 16: Testing the BCD to 7-Segment Decoder
module Test_BCD_to_7Segment; // No need for Ports
reg A, B, C, D; // variable inputs
wire a, b, c, d, e, f, g; // wire outputs
// Instantiate the module to be tested
BCD_to_7Segment BCD_7Seg (A, B, C, D, a, b, c, d, e, f, g);
initial begin // initial block
A=0; B=0; C=0; D=0; // at t=0
#200 $finish; // at t=200 finish simulation
end // end of initial block
always #10 D=~D; // invert D every 10 time units
always #20 C=~C; // invert C every 20 time units
always #40 B=~B; // invert B every 40 time units
always #80 A=~A; // invert A every 80 time units
endmodule

## Slide 17: The initial and always Blocks
There are two types of procedural blocks in Verilog
The initial block
  Executes the enclosed statement(s) once
The always block
  Executes the enclosed statement(s) repeatedly until simulation terminates
The body of the initial and always blocks is procedural
  Can enclose one or more procedural statements
  Procedural statements surrounded by begin … end execute sequentially
  #delay is used to delay the execution of the procedural statement
Procedural blocks can appear in any order inside a module
Multiple procedural blocks run in parallel inside the simulator

## Slide 18: Simulator Waveforms
All sixteen input test cases of A, B, C, D are generated between t=0 and t=160ns. Verify that outputs a to g match the truth table.

## Slide 19: Hierarchical Design
Why Hierarchical Design?
To simplify the implementation of a complex circuit
What is Hierarchical Design?
Decompose a complex circuit into smaller pieces called blocks
Decompose each block into even smaller blocks
Repeat as necessary until the blocks are small enough
Any block not decomposed is called a primitive block
The hierarchy is a tree of blocks at different levels
The blocks are verified and well-document
They are placed in a library for future use

## Slide 20: Example of Hierarchical Design
Top Level: 16-input odd function: 16 inputs, one output
  Implemented using Five 4-input odd functions
Second Level: 4-input odd function that uses three XOR gates
16-Input
Odd
Function
x0
x1
x2
x3
x4
x5
x6
x7
x8
x9
x10
x11
x12
x13
x14
x15
z
4-Input
Odd
Function
z
x0
x1
x2
x3
4-Input
Odd
Function
z
x0
x1
x2
x3
4-Input
Odd
Function
z
x0
x1
x2
x3
x0
x1
x2
x3
4-Input
Odd
Function
z
x0
x1
x2
x3
4-Input
Odd
Function
z
x0
x1
x2
x3
x4
x5
x6
x7
x8
x9
x10
x11
x12
x13
x14
x15
z
x0
x1
x2
x3
z
Hierarchical Design typically includes blocks of different functions and sizes

## Slide 21: Top-Down versus Bottom-Up Design
A top-down design proceeds from a high-level specification to a more and more detailed design by decomposition and successive refinement
A bottom-up design starts with detailed primitive blocks and combines them into larger and more complex functional blocks
Design usually proceeds top-down to a known set of building blocks, ranging from complete processors to primitive logic gates

## Slide 22: Hierarchical Design in Verilog
// Module Odd_4: 4-input Odd function uses three xor gates
module Odd_4 (input [0:3] x, output z);
wire [0:1] w;
xor g1(w[0], x[0], x[1]);
xor g2(w[1], x[2], x[3]);
xor g3(z, w[0], w[1]);
endmodule
// Module Odd_16: 16-input Odd function
module Odd_16 (input [0:15] x, output z);
wire [0:3] w;
Odd_4 block0 (x[0:3], w[0]);
Odd_4 block1 (x[4:7], w[1]);
Odd_4 block2 (x[8:11], w[2]);
Odd_4 block3 (x[12:15], w[3]);
Odd_4 block4 (w[0:3], z);
endmodule
Five instances of the Odd_4 module

## Slide 23: Bit Vectors in Verilog
A Bit Vector is multi-bit declaration that uses a single name
A Bit Vector is specified as a Range [msb:lsb]
msb is most-significant bit and lsb is least-significant bit
Examples:
input [0:15] x; // x is a 16-bit input vector
wire [0:3] w; // Bit 0 is most-significant bit
reg [7:0] a; // Bit 7 is most-significant bit
Bit select: w[1] is bit 1 of vector w
Part select: x[8:11] is a 4-bit select of x with range [8:11]
The part select range must be consistent with vector declaration

## Slide 24: Testing Hierarchical Design
Exhaustive testing can be very time consuming (or impossible)
  For a 16-bit input, there are 216 = 65,536 test cases (combinations)
  For a 32-bit input, there are 232 = 4,294,967,296 test cases
  For a 64-bit input, there are 264 = 18,446,744,073,709,551,616 test cases!
Testing a hierarchical design requires a different strategy
Test each block in the hierarchy separately
  For smaller blocks, exhaustive testing can be done
  It is easier to detect errors in smaller blocks before testing complete circuit
Test the top-level design by applying selected test inputs
Make sure that the test inputs exercise all parts of the circuit

## Slide 25: Iterative Design
Using identical copies of a smaller circuit to build a large circuit
Example: Building a 4-bit adder using 4 copies of a full-adder
The cell (iterative block) is a full adder
Adds 3 bits: ai, bi, ci, Computes: Sum si and Carry-out ci+1
Carry-out of cell i becomes carry-in to cell (i +1)
c0
Full
Adder
a0
b0
s0
c1
Full
Adder
a1
b1
s1
c2
Full
Adder
a2
b2
s2
c3
Full
Adder
a3
b3
s3
c4
ci
Full
Adder
ai
bi
si
ci+1

## Slide 26: Full Adder
Full adder adds 3 bits: a, b, and c
Two output bits:
Carry bit: cout
Sum bit: sum
Sum bit is 1 if the number of 1's in the input is odd (odd function)
sum = (a  b)  c
Carry bit is 1 if the number of 1's in the input is 2 or 3
cout = a·b + (a  b)·c
a b c | cout | sum
0 0 0 | 0 | 0
0 0 1 | 0 | 1
0 1 0 | 0 | 1
0 1 1 | 1 | 0
1 0 0 | 0 | 1
1 0 1 | 1 | 0
1 1 0 | 1 | 0
1 1 1 | 1 | 1
Truth Table

## Slide 27: Full Adder Module (Gate-Level Description)
module Full_Adder(input a, b, c, output cout, sum);
wire w1, w2, w3;
and (w1, a, b);
xor (w2, a, b);
and (w3, w2, c);
xor (sum, w2, c);
or (cout, w1, w3);
endmodule
a
b
c
sum
cout
w1
w2
w3
Full_Adder

## Slide 28: 16-Bit Adder with Array Instantiation
// Input ports: 16-bit a and b, 1-bit cin (carry input)
// Output ports: 16-bit sum, 1-bit cout (carry output)
module Adder_16 (input [15:0] a, b, input cin,
output [15:0] sum, output cout);
wire [16:0] c; // carry bits
assign c[0] = cin; // carry input
assign cout = c[16]; // carry output
// Instantiate an array of 16 Full Adders
// Each instance [i] is connected to bit select [i]
Full_Adder adder [15:0] (a[15:0], b[15:0], c[15:0],
c[16:1], sum[15:0]);
endmodule
Array Instantiation of identical modules by a single statement

## Slide 29: 16-Bit Adder with Continuous Assignment
// Input ports: 16-bit a and b, 1-bit cin (carry input)
// Output ports: 16-bit sum, 1-bit cout (carry output)
module Adder_16b (input [15:0] a, b, input cin,
output [15:0] sum, output cout);
wire [16:0] c; // carry bits
assign c[0] = cin; // carry input
assign cout = c[16]; // carry output
// assignment of 16-bit vectors
assign sum[15:0] = (a[15:0] ^ b[15:0]) ^ c[15:0];
assign c[16:1] = (a[15:0] & b[15:0]) |
(a[15:0] ^ b[15:0]) & c[15:0];
endmodule

## Slide 30: Testing the 16-bit Adder
Exhaustive testing: 216 × 216 × 2 = 8,589,934,592 test cases
Let us choose only: 3 × 3 × 2 = 18 test cases
Input test cases for a[15:0] = 'h158A, 'h52AF, 'hB903
Chosen randomly with values shown in hexadecimal
'h158A (hexadecimal) = 'b0001_0101_1000_1010 (binary)
Underscores are ignored (used to enhance readability)
Input test cases for b[15:0] = 'h7095, 'h9A4E, 'hC6BD
Also chosen randomly with values shown in hexadecimal
Radix symbol: 'b (binary), 'o (octal), 'd (decimal), 'h (hex)
Input test cases for cin = 0, 1

## Slide 31: Writing a Test bench for the 16-bit Adder
module Test_Adder_16; // Test bench for Adder_16
reg [15:0] A, B; reg Cin; // Data and Carry inputs
wire [15:0] Sum; wire Cout; // Sum and Carry outputs
Adder_16 Test (A, B, Cin, Sum, Cout); // Instantiate 16-bit adder
initial begin
A='h158A; B='h7095; Cin=0; // Initialize A, B, Cin
#10 Cin=1; // t=10, Change Cin
#10 B='h9A4E; Cin=0; // t=20, Change B and Cin
#10 Cin=1; // t=30, Change Cin
#10 B='hC6BD; Cin=0; // t=40, Change B and Cin
#10 Cin=1; // t=50, Change Cin
#10 A='h52AF; B='h7095; Cin=0; // t=60, Change A, B and Cin
#10 Cin=1; // t=70, Change Cin
#10 B='h9A4E; Cin=0; // t=80, Change B and Cin
. . . // more test cases
#10 $finish; // End simulation
end
endmodule

## Slide 32: Generating Test Cases in parallel with always
module Test_Adder_16; // Test bench for Adder_16
reg [15:0] A, B; reg Cin; // Data and Carry inputs
wire [15:0] Sum; wire Cout; // Sum and Carry outputs
Adder_16 Test (A, B, Cin, Sum, Cout); // Instantiate 16-bit adder
initial begin
A='h158A; B='h7095; Cin=0; // Initialize A, B, Cin
#200 $finish; // At t=200 end simulation
end
always begin // Change A every 60 ns
#60 A='h52AF; #60 A='hB903; #60 A='h158A;
end
always begin // Change B every 20 ns
#20 B='h9A4E; #20 B='hC6BD; #20 B='h7095;
end
always #10 Cin = ~Cin; // Invert Cin every 10 ns
endmodule

## Slide 33: Simulator Waveforms
The values of A, B, and Sum are shown in hexadecimal
Can change the radix to binary, octal, and decimal
The values of Sum and Cout can be verified easily
All 18 test cases of A, B, and Cin are generated (t=0 to 180 ns)