## Slide 1: Arithmetic Circuits 3
COE 202
Digital Logic Design
Dr. Muhamed Mudawar
King Fahd University of Petroleum and Minerals

## Slide 2: Presentation Outline
Carry Lookahead Adder
BCD Adder
Binary Multiplier
Carry-Save Adders in Multipliers

## Slide 3: Carry Lookahead Adder
Is it possible to eliminate carry propagation?
Observation:
If both inputs and are 1s then
will be 1 regardless of input
Therefore, define
is called carry generate: generates regardless of
In addition, define or is 1, not both
is called carry propagate: propagates value of to
Equation of output carry becomes:
If both inputs and are 0s then and
ci
Full
Adder
ai
bi
si
ci+1

## Slide 4: Carry Bits
Carry bits are generated by a Lookahead Carry Unit as follows:
input carry
Define Group Generate:
Define Group Propagate:
Carry does not ripple anymore
Reduced delay when generating to in parallel

## Slide 5: 4-Bit Carry Lookahead Adder
All generate and propagate signals (gi, pi) are generated in parallel
All carry bits (c1 to c4) are generated in parallel
The sum bits are generated faster than ripple-carry adder
ai
ci
si
bi
gi
pi
c4
c0
1-bit
Adder
a0
b0
1-bit
Adder
a1
b1
1-bit
Adder
a2
b2
1-bit
Adder
a3
b3
Lookahead Carry Unit
s0
g0 p0
GG GP
c1
c1
c2
c2
c3
c3
s1
g1 p1
s2
g2 p2
s3
g3 p3

## Slide 6: Lookahead Carry Unit
Lookahead Carry Unit
GG GP
g3 p3
c3
g2 p2
c2
g1 p1
g0 p0
c1
c4
c0
c0
p0
g0
c1
p1
g1
c2
p2
g2
c3
p3
g3
c4
GG
GP
Two-Level AND-OR Logic

## Slide 7: Longest Delay of the 4-bit CLA
All generate and propagate signals are produced in parallel
Delay of all gi and pi = 1 (Delay of XOR > Delay of AND)
Carry bits c1, c2, and c3 are generated in parallel (Delay = 2)
  Carry-out bit c4 is not needed to compute the sum bits
Longest Delay of the 4-bit CLA = 1 + 2 + 1 = 2 1 + 2
ai
ci
si
bi
gi
pi
1
1
c0
p0
g0
c1
p1
g1
c2
p2
g2
c3
p3
g3
c4
GG
GP
Delay = 2

## Slide 8: Hierarchical 16-Bit Carry Lookahead Adder
Designed with Four 4-bit Carry Lookahead Adders (CLA)
A Second-Level Lookahead Carry Unit is required
Uses Group Generate (GG) and Group Propagate (GP) signals
c16
Lookahead Carry Unit (Level 2)
GG GP
4-bit
CLA Adder
c12
s [15:12]
b [15:12]
4
4
4
a [15:12]
4-bit
CLA Adder
c8
s [11:8]
b [11:8]
4
4
4
a [11:8]
4-bit
CLA Adder
c4
s [7:4]
b [7:4]
4
4
4
a [7:4]
4-bit
CLA Adder
c0
s [3:0]
g0 p0
GP
GG
GP
GG
GP
GG
GP
GG
g1 p1
g2 p2
g3 p3
b [3:0]
4
4
4
a [3:0]
4-bit
input
vectors

## Slide 9: Hierarchical 64-Bit Carry Lookahead Adder
Designed with Four 16-bit Carry Lookahead Adders (CLA)
A Third-Level Lookahead Carry Unit is required
Uses Group Generate (GG) and Group Propagate (GP) signals
c64
Lookahead Carry Unit (Level 3)
GG GP
16-bit
CLA Adder
c48
s [47:32]
b [47:32]
16
16
16
a [47:32]
16-bit
CLA Adder
c32
s [47:32]
b [47:32]
16
16
16
a [47:32]
16-bit
CLA Adder
c16
s [31:16]
b [31:16]
16
16
16
a [31:16]
16-bit
CLA Adder
c0
s [15:0]
g0 p0
GP
GG
GP
GG
GP
GG
GP
GG
g1 p1
g2 p2
g3 p3
b [15:0]
16
16
16
a [15:0]
16-bit
input
vectors

## Slide 10: Next . . .
Carry Lookahead Adder
BCD Adder
Binary Multiplier
Carry-Save Adders in Multipliers

## Slide 11: BCD Addition
We use binary arithmetic to add the BCD digits
If the result is more than 9, it must be corrected to use 2 digits
To correct the digit, add 6 to the digit sum
8
+ 5
13 (>9)
1000
+ 0101
1101
8
+ 5
13 (>9)
+ 6 (add 6)
19 (carry + 3)
1000
+ 0101
1101
+ 0110
0011
Final answer
in BCD

## Slide 12: Multiple Digit BCD Addition
Add: 2905 + 1897 in BCD
Showing carries and digit corrections
+1
0101
0111
1100
0110
0010
0000
1001
1010
0110
0000
+1
1001
1000
10010
0110
1000
+1
0010
0001
0100
0100
+
carry
digit correction
Final answer: 2905 + 1897 = 4802

## Slide 13: BCD Adder
Correction is required if: A+B > 9
Correction circuit adds 0 or 6
4
S [3:0]
BCD Adder
4
A [3:0]
4
B [3:0]
Cin
Cout
S3
4
A [3:0]
4
B [3:0]
Cin
Cout
4-bit binary Adder
HA
FA
S2
S1
S0
z3
z2
z1
z0
HA = Half Adder
FA = Full Adder
Correction
Circuit
Add 0 or 6
Detection
Circuit
00
01
11
10
00
01
11
10
1
1
1
1
1
1

## Slide 14: Ripple-Carry BCD Adder
Inputs are BCD digits: 0 to 9
Sum are BCD digits: ones, tens, hundreds, thousands, etc.
Can be extended to any number of BCD digits
BCD adders are larger in size than binary adders
BCD
Adder
c3
S [15:12]
B [15:12]
4
4
4
A [15:12]
c4
BCD
Adder
c2
S [11:8]
B [11:8]
4
4
4
A [11:8]
BCD
Adder
c1
S [7:4]
B [7:4]
4
4
4
A [7:4]
Tens
BCD
Adder
c0
S [3:0]
B [3:0]
4
4
4
A [3:0]
Ones
Hundreds
Thousands

## Slide 15: Next . . .
Carry Lookahead Adder
BCD Adder
Binary Multiplier
Carry-Save Adders in Multipliers

## Slide 16: Binary Multiplication
Binary Multiplication is simple:
0×0=0, 0×1=0, 1×0=0, 1×1=1
Multiplicand 11002 = 12
Multiplier × 11012 = 13
1100
0000
1100
1100
Product 100111002 = 156
n-bit multiplicand × n-bit multiplier = 2n-bit product
Accomplished via shifting and addition
Binary multiplication
0 × multiplicand = 0
1 × multiplicand = multiplicand

## Slide 17: 4-bit × 4-bit Binary Multiplier
Suppose we want to multiply two numbers A and B
  Example on 4-bit numbers: A = a3 a2 a1 a0 and B = b3 b2 b1 b0
Step 1: AND (multiply) each bit of A with each bit of B
  Requires n2 AND gates and produces n2 product bits
  Position of aibj = (i+j). For example, Position of a2b3 = 2+3 = 5
a0b0
a1b0
a2b0
a3b0
a0b1
a1b1
a2b1
a3b1
a0b2
a1b2
a2b2
a3b2
a0b3
a1b3
a2b3
a3b3
A × B

## Slide 18: Adding the Bits Vertically
ADD the product bits vertically using Carry-Save adders
  Full Adder adds three vertical bits
  Half Adder adds two vertical bits
  Each adder produces a partial sum and a carry
Use Carry-propagate adder for final addition
a0b0
a1b0
a2b0
a3b0
a0b1
a1b1
a2b1
a3b1
a0b2
a1b2
a2b2
a3b2
a0b3
a1b3
a2b3
a3b3
A × B

## Slide 19: Carry Save Adder
A n-bit carry-save adder produces two n-bit outputs
  n-bit partial sum bits and n-bit carry bits
All the n bits of a carry-save adder work in parallel
  The carry does not propagate as in a carry-propagate adder
  This is why a carry-save is faster than a carry-propagate adder
Useful when adding multiple numbers (as in a multiplier)
Carry-Propagate Adder
+
a0
b0
s0
+
a1
b1
s1
+
a31
b31
s31
. . .
cout
cin
Carry-Save Adder
. . .
+
a31
b31
s'31
c'31
c31
+
a1
b1
s'1
c'1
c1
+
a0
b0
s'0
c'0
c0

## Slide 20: Carry-Save Adders in a Multiplier
Step 1: Use carry save adders to add the partial products
  Reduce the partial products to just two numbers
Step 2: Use carry-propagate adder to add last two numbers
P0
FA
a2b0 a1b1
HA
FA
FA
a3b0 a2b1
a0b0
HA
a1b0 a0b1
HA
HA
FA
FA
FA
FA
a3b1 a2b2
FA
a3b2
a2b3
a3b3
a1b3
a0b3
a1b2
a0b2
P1
P2
P3
P4
P5
P6
P7
Carry Save Adder
Carry Propagate Adder
Carry Save