KING FAHD UNIVERSITY OF PETROLEUM & MINERALS

ELECTRICAL ENGINEERING DEPARTMENT

FIRST SEMESTER 2009-2010 (091)

| Course Title: | Fundamentals of Electric Circuits |
| --- | --- |
| Course Number: | EE 204 |

| Exam Type: | MAJOR EXAM II |
| --- | --- |
| Date: | December 23, 2009 |
| Time: | 07:00 pm – 8:30 pm (1 & 1/2 hours) |

| Indicate your lab section number from the list below (lab section/instructor name/lab starting time/day) |
| --- |
| 51/Salim/2:10/S | 52/Al-Saihati/8:00/U | 53/Salhab/11:00/U | 54/Al-Saihati/11:0/U | 55/Alfaouri/2:10/U |
| 56/Ali/2:10/U | 57/Mahmoud/2:10/M | 58/Akber/2:10/M | 59/Al-Saihati/8:00/T | 60/Salhab/11:00/T |
| 61/Ismail/11:00/T | 62/Alfaouri/2:10/T | 63/Akber/2:10/T | 64/Ghani/2:10/W | 65/Al-Safadi/2:10/W |

| Student Name: | ________________________________ |
| --- | --- |
| Student ID: | ________________________________ |
| Section: | ________________________________ |
| Serial Number: | ________________________________ |

| GRADING |
| --- |
| Question 1: | 16 |  |
| Question 2: | 20 |  |
| Question 3: | 24 |  |
| Total: | 60 |  |

Be neat, organized, and show all your work and results.

Question 1:

For the given ‘is’,

- Find the equations for 'VC' for the following intervals.

(i) 0 < t ≤ 1	(ii) 1 < t < ∞

- Plot the result in part a.

- Plot the voltage 'VR'.

Solution:

(a) Find the equivalent capacitance:

Ceq = [4 in series with 4] in parallel with 2 = [(4*4)/(4+4)]+2 = 2+2 = 4 F.

(i) 0 < t ≤ 1

(ii) 1 < t < ∞

(b) and (c)

Question 2:

Using only the superposition principle, determine the following:

- Thevenin's equivalent circuit that is connected to the resistor RL.

- RL that absorbs maximum power.

- The maximum power absorbed by RL.

(a) We need to find RTh and VOC

Rth: Deactivate the two sources

VOC: use superposition

The voltage source circuit

Or using voltage division rule

The current source circuit

Draw the equivalent circuit as shown

(b)

(c) (2 marks for the power calculation)

Question 3:

For the circuit shown below:

- Write the three node equations for node A, B, and C and put them in the standard system of equations.

- Find the node voltages VA, VB, and VC.

- What is the power dissipated in (absorbed by) R1.

- Which method you prefer to use node voltage method or mesh current method? Why?

Solution:

KVL for V1

(1 mark)

- Substitute from 3 into 2

Solve (1) and (4)

| VA | VB | VC |
| --- | --- | --- |
| 24V | 6V | 4V |

- (2 marks)

OR

- Mesh is better. As the current in two meshes are known by using KCL directly (I1, I2). We will have only one equation in one unknown for the third mesh contains R2, R3, and V1. (2 marks)