# University Diploma Programs

# Electronic Equipment Maintenance

EET-029: Introduction to Communications

## Quiz # 1

Name: ________________________________	ID #: ___________

- In a communication system, noise is most likely to affect the signal:

  - At the transmitter

  - In the channel

  - In the information source

  - At the destination

- Indicate the false statement. Modulation is used to:

  - Reduce the bandwidth used

  - Separate differing transmissions

  - Ensure that intelligence may be transmitted over long distances

  - Allow the use of practicable antennas.

- In a low-level AM system, amplifiers following the modulated stage must be:

  - Linear devices

  - Harmonic devices

  - Class C amplifiers

  - Nonlinear devices

- If the carrier of a 100 percent modulated AM wave is suppressed, the percentage power saving will be:

  - 50

  - 150

  - 100

  - 66.66

- To provide two or more voice circuits with the same carrier, it is necessary to use:

  - ISB

  - Carrier reinsertion

  - SSB with pilot carrier

  - Lincompex

- The modulation index of an AM wave is changed from 0 to 1. The transmitted power is:

  - Unchanged

  - Halved

  - Doubled

  - Increased by 50 percent

- A carrier is simultaneously modulated by two sine waves with modulation indices of 0.3 and 0.4; the total modulation index:

  - is 1

  - cannot be calculated unless the phase relations are known

  - is 0.5

  - is 0.7

- Indicate the false statement regarding the advantages of SSB over double sideband, full carrier AM:

  - More channel space is available

  - Transmitter circuits must be more stable, giving better reception

  - The signal is more noise-resistant

  - Much less power is required for the same signal strength