APPENDIX B

UNITS OF OPTICAL POWER

Optical power can be expressed either in linear units [such as watt (W), milliwatt () or microwatt ()] or in dB units [such as dB, dB-milli (dBm) or dB-micro ()]. The unit dBm is dB with respect to milliwatt. The unit  is dB with respect to microwatt. The various units of optical power will be explained in this appendix. The majority of optical power meters give the user an option for displaying the optical power using one of these units.

An optical power  expressed in Watts, can also be expressed in dB using the following expression:

[ is in Watts]                              (1)

An optical power  expressed in  or , may be expressed in  or , respectively, using:

[ is in ]                               (2)

[ is in ]                                (3)

Example 1:

Express  in:   a) Watts and       b)      c)       d)

Solution:

a)

b)

c)

d)

Notice that the difference between  and  is . Also the difference between and is . The reason is that  corresponds to a factor of 1000 in linear units.

Example 2:

Express  in:       a) mW        b) W and      c) and

Solution:

a)

b)

c)       &

In many EE 420 laboratory experiments, we will be required to calculate optical power loss. Consider for instance the situation illustrated in Figure 1, where a given optical beam is incident on a lossy optical element. The input optical power is  and the output optical power is . Since the optical element is lossy, it follows that .

Figure 1: Input and Output Optical Powers through a Lossy Optical Element.

For a linear element, it is well-known that the output optical power is proportional to the input optical power, i.e. , where  is some constant. This constant is larger than unity, simply because .  The parameter  can be used to represent the loss of the element. When  increases, the loss of the optical element also increases. For instance, when , then  and therefore, only one third of the incident optical power is available at the output end of the element.

The element loss can also be expressed using the dB measure, using the expression:

(4)

Where  and  are expressed in the same linear units. For instance, if  is expressed in mW, then   must also be expressed in mW.

The loss in dB can also be expressed as the difference between the power levels in dB, as shown next. Using equation (4), and assuming that and  are expressed in Watt, we have:

(5)

In a similar fashion, it is easy to show that:

(6)

(7)

Notice that in expressions (5), (6) and (7), both the input and output power levels are expressed in the same dB units, such as ,  or . In addition, the  is always expressed in dB, even if the power levels are expressed in  or . It is meaningless to express the power loss in  or . For instance, the difference between  and  is given by:

(i.e. )

Example 3:

With reference to Figure 3 above, assume that and . Calculate:

a)        b) the element loss in dB using two different methods.

Solution:

a)

b) Method 1:

Method 2:

(the same answer as above).

# Text boxes

Lossy

Optical

Element