EE 420 H.W. Set # 1

1. An optical fiber has a numerical aperture of 0.20 and a cladding refractive index of 1.59. Calculate:

a) the acceptance angle of the optical fiber in air.

b) the acceptance angle of the fiber in water (the refractive index of water ).

c) the critical angle at the core-cladding boundary.

2. The velocity of light in the core of an optical fiber is  and the critical angle at the core-cladding interface is . Calculate the numerical aperture and the acceptance angle of the optical fiber in air.

3. The diagram shows a collimated Gaussian beam with a spot size of  and a wavelength of The beam is to be coupled efficiently into an optical fiber having a core diameter of  and a numerical aperture of . Coupling can be achieved using a single thin lens as shown in the diagram. Calculate:

a) the smallest possible focal length  of the lens (this results in a compact system).

b) the largest possible focal length  of the lens.

4. The f-number of a lens is defined as: f-number , where focal length of the lens and  lens diameter. Calculate the f-number of a complete sphere made of glass having a refractive index of 1.50.

5. Given a light source with a very small spectral width (i.e. ). Show that:

where:  center frequency of the source.

center wavelength of the source.

Spectral width of the source.

Bandwidth of the source.

6. Briefly explain why material dispersion limits the maximum data rate in a digital optical fiber communication system.

7. List 10 advantages of the optical fiber in communication systems.