King Fahd Univesity of Petroleum & Minerals

Department of Electrical Engineering

EE200-03&04		(071)

Homework # 5

- Design a combinational circuit that generates the 7's complement of an octal digit using decoders and OR gates,. Use letters a, b, c, for the inputs and x, y,…. For the outputs.

- A combinational circuit is specified by the following three Boolean functions:

Implement the circuit with a decoder constructed with NAND gates, similar to Fig. 4.19 of the textbook, and NAND or AND gates connected to the decoder outputs. Use a block diagram for the decoder. Minimize the number of inputs to the external gates.

- Construct an 8x1 multiplexer using 3 state buffers and any required logic components. Draw the logic diagram indicating the inputs and output of the multiplexer.

- Implement the following 4-variable Boolean function using a 4x1 multiplexer

Connect the variables y and z to the selection lines S1 and S0 respectively.