King Fahd University of Petroleum & Minerals

Electrical Engineering Department

# EE390 Exam-1

1.  For the given values shown in the table  {assume the memory contents of the

addresses in between the given addresses (in the table) contain zero values};

| Register contents | Memory addresses (PA) | Memory contents (Hex) | Memory addresses (PA) | Memory contents (Hex) |
| --- | --- | --- | --- | --- |
| (AX)=0076H | (01100 H )= 20 H | (01201 H )= 01 H |
| (BX)=0032H | (01101 H )= 30 H | (01210 H )= 45 H |
| (CX)=0042H | (01120 H )= FE H | (01211 H )= 02 H |
| (DX)=0052H | (01121 H )= EF H | (01220 H )= 34 H |
| (DS)=0200H | (01130H )= 09 H | (01221 H )= 05 H |
| (SS)=1200H | (01131H )= 10 H | (01230 H )= 43 H |
| (SI)=0200H | (01150 H )= 32 H | (01231 H )= 20 H |
| (DI)=0300H | (01151 H )= 20 H | (01240 H )= 14 H |
| (CF)=1 | (01200 H )= 40 H | (01241 H )= 07 H |

What is the result produced in the destination operand by executing the instructions of each of the following two parts (each part starts from the same conditions above).

| No | INSTRUCTION | Destination after execution (Distination)= contents |
| --- | --- | --- |
| 1 | ADD | AL, 15H | ( )= |
| 2 | DAA |  | ( )= |
| 3 | ADC | DI, BX | ( )= |
| 4 | INC | WORD PTR [0100H] | ( )= |
| 5 | SUB | DL, BL | ( )= |
| 6 | SBB | DL, [0200H] | ( )= |
| 7 | DEC | BYTE PTR [DI+BX] | ( )= |
| 8 | NEG | BYTE PTR [DI]+0010H | ( )= |

| No | INSTRUCTION | Destination after execution (Destination)= contents |
| --- | --- | --- |
| 1 | MOV | AX, 1234H | ( )= |
| 2 | MOV | DX, 00A0H | ( )= |
| 3 | MOV | BX, 0020H | ( )= |
| 4 | XCHG | SI, DI | ( )= |
| 5 | MUL | CX | ( )= |
| 6 | IMUL | BYTE PTR [SI+BX] | ( )= |
| 7 | MOV | AX, F500H | ( )= |
| 8 | IDIV | BYTE PTR [SI]+0030H | ( )= |

- For the given values shown in the table  {assume the memory contents of the

addresses in between the given addresses (in the table) contains zero values} ;

| Register contents | Memory addresses (PA) | Memory contents (Hex) |
| --- | --- | --- |
| AX=0500H, | 00306 : 22 |
| BX=0200H, | 01006 : 32 |
| CX=0235H, | 10006 : 22 |
| DX=02F0H, | 10206 : D4 |
| DS=1000H, | 10306 : 4B |
| SS=1100H, | 10406 : FC |
| SI=0300H, | 11016 : E7 |
| DI=0400H, | 11206 : AC |
| BP=0010 H | 11606 : A8 |

- (i)  MOV CX,0A02H ;

(ii) SAL   AX,CL ;

| No | SOURCE OPERAND | DESTINATION OPERAND | Addressing Mode used | Flags affected (yes/no) |
| --- | --- | --- | --- | --- |
|  | Physical Address | Contents | Physical Address | Contents |  |  |
|  |  | After exec. |  | Before exec | After exec |  |  |
| (i) |  |  |  |  |  |  |  |
| (ii) |  |  |  |  |  |  |  |

- (i)  XOR AH,[SI+6] ;

(ii)  SUB DL,[BP+6] ;

| No | SOURCE OPERAND | DESTINATION OPERAND | Addressing Mode used | Flags affected (yes/no) |
| --- | --- | --- | --- | --- |
|  | Physical Address | Contents | Physical Address | Contents |  |  |
|  |  | After exec. |  | Before exec | After exec |  |  |
| (i) |  |  |  |  |  |  |  |
| (ii) |  |  |  |  |  |  |  |

- (i) MUL BH;

(ii) ADD  [BX+DI+6], AX;

| No | SOURCE OPERAND | DESTINATION OPERAND | Addressing Mode used | Flags affected (yes/no) |
| --- | --- | --- | --- | --- |
|  | Physical Address | Contents | Physical Address | Contents |  |  |
|  |  | After exec. |  | Before exec | After exec |  |  |
| (i) |  |  |  |  |  |  |  |
| (ii) |  |  |  |  |  |  |  |