King Fahd University of Petroleum & Minerals

Electrical Engineering Department

# EE390 Exam-1

| Prob.1 | Prob.2 | Prob.3 | Total |
| --- | --- | --- | --- |

Name : I.D. Section

1. Write an efficient procedure called MUL11 to multiply AX by 11 (decimal) without using MUL instructions, (just using shift, Add, and Move). The result will be returned in AX. MAX 7 lines.

MUL11 PROC MUL11 ENDP

2.  For the given values shown in the table  {assume the memory contents of the

addresses in between the given addresses (in the table) contain zero values};

| Register contents | Memory addresses (PA) | Memory contents (Hex) | Memory addresses (PA) | Memory contents (Hex) |
| --- | --- | --- | --- | --- |
| (AX)=0067H | (01100 H )= 10 H | (01201 H )= 00 H |
| (BX)=0020H | (01101 H )= 00 H | (01210 H )= 40 H |
| (CX)=0030H | (01120 H )= FF H | (01211 H )= 00 H |
| (DX)=0040H | (01121 H )= FF H | (01220 H )= 30 H |
| (DS)=0100H | (01130H )= 08 H | (01221 H )= 00 H |
| (SS)=1100H | (01131H )= 00 H | (01230 H )= 40 H |
| (SI)=0100H | (01150 H )= 02 H | (01231 H )= 00 H |
| (DI)=0200H | (01151 H )= 00 H | (01240 H )= 10 H |
| (CF)=1 | (01200 H )= 30 H | (01241 H )= 00 H |

What is the result produced in the destination operand by executing the instructions of each of the following two parts (each part starts from the same conditions above).

| No | INSTRUCTION | Destination after execution (Distination)= contents |
| --- | --- | --- |
| 1 | ADD | AL, 16H | ( )= |
| 2 | DAA |  | ( )= |
| 3 | ADC | SI, BX | ( )= |
| 4 | INC | BYTE PTR [0100H] | ( )= |
| 5 | SUB | DL, BL | ( )= |
| 6 | SBB | DL, [0200H] | ( )= |
| 7 | DEC | BYTE PTR [DI+BX] | ( )= |
| 8 | NEG | BYTE PTR [DI]+0010H | ( )= |

| No | INSTRUCTION | Destination after execution (Destination)= contents |
| --- | --- | --- |
| 1 | MOV | AX, 1234H | ( )= |
| 2 | MOV | DX, 00A0H | ( )= |
| 3 | MOV | BX, 0020H | ( )= |
| 4 | XCHG | SI, DI | ( )= |
| 5 | MUL | CX | ( )= |
| 6 | IMUL | BYTE PTR [SI+BX] | ( )= |
| 7 | MOV | AX, F400H | ( )= |
| 8 | IDIV | BYTE PTR [SI]+0030H | ( )= |

- For the given values shown in the table  {assume the memory contents of the

addresses in between the given addresses (in the table) contains zero values} ;

| Register contents | Memory addresses (PA) | Memory contents (Hex) |
| --- | --- | --- |
| AX=0500H, | 00306 : 12 |
| BX=0200H, | 01006 : 12 |
| CX=0235H, | 10006 : 32 |
| DX=02F0H, | 10206 : E4 |
| DS=1000H, | 10306 : 4A |
| SS=1100H, | 10406 : FE |
| SI=0300H, | 11016 : D7 |
| DI=0400H, | 11206 : 9C |
| BP=0010 H | 11606 : B8 |

- (i)  MOV CX,0A02H ;

(ii) SAL   AX,CL ;

| No | SOURCE OPERAND | DESTINATION OPERAND | Addressing Mode used | Flags affected (yes/no) |
| --- | --- | --- | --- | --- |
|  | Physical Address | Contents | Physical Address | Contents |  |  |
|  |  | After exec. |  | Before exec | After exec |  |  |
| (i) |  |  |  |  |  |  |  |
| (ii) |  |  |  |  |  |  |  |

- (i)  XOR AH,[SI+6] ;

(ii)  SUB DL,[BP+6] ;

| No | SOURCE OPERAND | DESTINATION OPERAND | Addressing Mode used | Flags affected (yes/no) |
| --- | --- | --- | --- | --- |
|  | Physical Address | Contents | Physical Address | Contents |  |  |
|  |  | After exec. |  | Before exec | After exec |  |  |
| (i) |  |  |  |  |  |  |  |
| (ii) |  |  |  |  |  |  |  |

- (i) MUL BH;

(ii) ADD  [BX+DI+6], AX;

| No | SOURCE OPERAND | DESTINATION OPERAND | Addressing Mode used | Flags affected (yes/no) |
| --- | --- | --- | --- | --- |
|  | Physical Address | Contents | Physical Address | Contents |  |  |
|  |  | After exec. |  | Before exec | After exec |  |  |
| (i) |  |  |  |  |  |  |  |
| (ii) |  |  |  |  |  |  |  |