King Fahd University of Petroleum & Minerals

Electrical Engineering Department

# EE-390

| Prob.1 | Prob.2 | Prob.3 | Total |
| --- | --- | --- | --- |

Answer all questions and note that more credit for more efficient programs

Name : Section : I.D.

1.	Write a sequence of instructions to check the number of zeros in each of 100 bytes stored starting from DS:[100h]. Load the number of bytes with even number of zeros in AL register and the number of bytes that have odd number of zeros in AH registers.

2.	Write a sequence of instructions that will make the contents of   all even Bits of AL register, same as the content of Bit 2 of AL register and MASK the contents of the remaining Bits of AL. Don’t assume any specific Hex number stored in AL register (should work for any Hex number)

| AL = | Bit 7 | Bit 6 | Bit 5 | Bit 4 | Bit 3 | Bit 2 | Bit 1 | Bit 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

3(a) Find the values of the listed registers below, as you execute each  line of the program. Assume the initial values are: AX= 1234H, BX=5F88H, CX=1403H, DX=0125H, SI=003BH, ZF=NZ ,  PF=PO  and  CF=CY

LEA AX, [5678H] ;		PF = ________

SBB BX, CX ; 		BX = ________

RCR DX, CL ;           		DX =________

3(b). Assume,    DS=CS=SS=ES=2000H,  AX=0400H,  BX=0500H,  CX=0600H

DX=0600H,  SI=0700H,  DI=0400H,  BP= 0020H,  SP=0AF0H,

(i) If displacement is 61H, write a program to load AX register with the content of

a DATA segment memory location, using Indexed-addressing mode.

______________________

(ii) What is the physical address of the source operand.

______________________