KFUPM-EE DEPT.

EE205: Circuits II-082

HW # 1: Due: Mon., March  16, 2009

Problem 1:

- For the circuit in the above figure, is it a balanced or unbalanced three-phase system? Explain why.

- Find I0

Problem 2:

The above figure shows a balanced three-phase Δ-connected source.

- Find the Y-connected equivalent circuit.

- Show that the Y-connected equivalent circuit delivers the same open-circuit voltage as the original  Δ-connected source.

- Apply an external short circuit to the terminals A, B, and C. Use the Δ-connected source to find the three line currents IaA, IbB, and IcC.

- Repeat (c) but use the Y-equivalent source to find the three line currents.

Problem 3:

The Δ-connected source of Problem 2 is connected to a Y-connected load by means of a balanced three-phase distribution line. The load impedance is 957+j259 Ω per phase. And the line impedance is 1.2+j12 Ω per phase.

- Construct a single-phase equivalent circuit of the system.

- Determine the magnitude of the line voltage at the terminals of the load.

- Determine the magnitude of the phase current in the Δ-source.

- Determine the magnitude of the line voltage at the terminals of the source.

Problem 4:

A three-phase positive sequence Y-connected source supplies 14kVA with a power factor of 0.75 lagging to a parallel combination of a Y-connected load and a Δ-connected load. The Y-connected load used 9 kVA at a power factor of 0.6 lagging and has an a-phase current of  A.

a) Find the complex power per phase of the Δ-connected load.

b) Find the magnitude of the line voltage.