King Fahd University of Petroleum & Minerals

Department of Electrical Engineering

EE370 Communications Engineering I

Design Project 072

Building and Testing Wireless FM Transmitter

Due: Week 9, 19-23 April

As an introduction to this project, read the information provided in this link

http://www.boondog.com

Click on Tutorials, then Wireless FM Transmitter.

      - Build the circuit!

      - Test it and make sure it is working!

      - Adjust the circuit so that it is transmitting around the following frequency:

| Sec.1 | 93 MHz | Sec. 2 | 95 MHz | Sec. 3 | 97 MHz | Sec. 4 | 99 MHz |
| --- | --- | --- | --- | --- | --- | --- | --- |

Explain your steps and note down all your observations.

      - Assume a single tone input at the microphone. Explain how this circuit works in light of what you have studied in EE370.

      - Show the signal or its spectrum at different points in the circuit. You may do that by measurements (Oscilloscope with enough Bandwidth).

Hints:

- Your short report should be self contained. The reader should not feel that you are answering questions! (Introduction, body, conclusion). Do not copy paragraphs form the provided website

- Writing style and organization are very important (Quality not Quantity!)

- Work in groups of two.

- Try to learn from the project by examining the signal in the time and in frequency domain at different locations.

- Start early to avoid any last minute problem (Enjoy the Break!).

- It will be your sole responsibility to make the components available.