Verification of Carson’s Rule (for computing the FM Bandwidth)

The Casron’s rule says that the BW of any FM signal is given by

,

where

Bm = Bandwidth of the Message Signal m(t) in Hz,

and

(f = ((/2(  = kf (mp/2( .

We can verify the Carson’s rule using a simple message signal that is a sinusoid with frequency (m. That is

,

where the magnitude of the message signal (  is a constant. The bandwidth of this signal Bm is clearly (m. The signal a(t), which is the integration of m(t), becomes

.

So, the FM signal becomes

.

Let us define a function  that is the complex–exponential form of , or

.				(1)

The second exponential above is a periodic signal with period Tm=2(/(m. So, it can be expanded using the exponential Fourier series as

.					 		(2)

where according the exponential Fourier series expansion (page 53 in your text book)

This integration can be simplified if we use the substitution

(		(

(

Let us define (  to be  . Substituting for ( and for in the integration of  Dn, we get