6.1

- Analyze the data from this experiment.

Design Expert Output

Response	1	Vibration
	        ANOVA for selected factorial model
	Analysis of variance table [Partial sum of squares - Type III]
		Sum of		Mean	F	p-value
	Source	Squares	df	Square	Value	Prob > F

Model		1641.68	3	547.23	92.02	< 0.0001	significant

A-Bit Size	1110.56	1	1110.56	186.75	< 0.0001
	  B-Cutting Speed	225.75	1	225.75	37.96	< 0.0001
	  AB		305.38	1	305.38	51.35	< 0.0001
	Pure Error	71.36	12	5.95
	Cor Total	1713.04	15

	The Model F-value of 92.02 implies the model is significant.  There is only
	a 0.01% chance that a "Model F-Value" this large could occur due to noise.

- Construct a normal probability plot of the residuals, and plot the residuals versus the predicted vibration level.  Interpret these plots.

There is nothing unusual about the residual plots.

- Draw the AB interaction plot.  Interpret this plot.  What levels of bit size and speed would you recommend for routine operation?

To reduce the vibration, use the smaller bit.  Once the small bit is specified, either speed will work equally well, because the slope of the curve relating vibration to speed for the small tip is approximately zero.  The process is robust to speed changes if the small bit is used.

6.2

- Estimate the factor effects.  Which effects appear to be large?

From the normal probability plot of effects below, factors B, C, and the AC interaction appear to be significant.

- Use the analysis of variance to confirm your conclusions for part (a).

The analysis of variance confirms the significance of  factors B, C, and the AC interaction.

Design Expert Output

Response:	Life	in hours

ANOVA for Selected Factorial Model

Analysis of variance table [Partial sum of squares]

Sum of		Mean	F

Source	Squares	DF	Square	Value	Prob > F

Model	1612.67	7	230.38	7.64	0.0004	significant

A	0.67	1	0.67	0.022	0.8837

B	770.67	1	770.67	25.55	0.0001

C	280.17	1	280.17	9.29	0.0077

AB	16.67	1	16.67	0.55	0.4681

AC	468.17	1	468.17	15.52	0.0012

BC	48.17	1	48.17	1.60	0.2245

ABC	28.17	1	28.17	0.93	0.3483

### Pure Error	482.67	16	30.17

Cor Total	2095.33	23

The Model F-value of 7.64 implies the model is significant.  There is only

a 0.04% chance that a "Model F-Value" this large could occur due to noise.

The reduced model ANOVA is shown below.  Factor A was included to maintain hierarchy.

Design Expert Output

Response:	Life	in hours

ANOVA for Selected Factorial Model

Analysis of variance table [Partial sum of squares]

Sum of		Mean	F

Source	Squares	DF	Square	Value	Prob > F

Model	1519.67	4	379.92	12.54	< 0.0001	significant

A	0.67	1	0.67	0.022	0.8836

B	770.67	1	770.67	25.44	< 0.0001

C	280.17	1	280.17	9.25	0.0067

AC	468.17	1	468.17	15.45	0.0009

Residual	575.67	19	30.30

Lack of Fit	93.00	3	31.00	1.03	0.4067	not significant

Pure Error	482.67	16	30.17

Cor Total	2095.33	23

The Model F-value of 12.54 implies the model is significant.  There is only

a 0.01% chance that a "Model F-Value" this large could occur due to noise.

Effects B, C and AC are significant at 1%.

- Write down a regression model for predicting tool life (in hours) based on the results of this experiment.

Design Expert Output

Coefficient		Standard	95% CI	95% CI

Factor	Estimate	DF	Error	Low	High	VIF

Intercept	40.83	1	1.12	38.48	43.19

A-Cutting Speed	0.17	1	1.12	-2.19	2.52	1.00

B-Tool Geometry	5.67	1	1.12	3.31	8.02	1.00

C-Cutting Angle	3.42	1	1.12	1.06	5.77	1.00

AC	-4.42	1	1.12	-6.77	-2.06	1.00

Final Equation in Terms of Coded Factors:

Life	 =

+40.83

+0.17	  * A

+5.67	  * B

+3.42	  * C

-4.42	  * A * C

Final Equation in Terms of Actual Factors:

Life	 =

+40.83333

+0.16667	  * Cutting Speed

+5.66667	  * Tool Geometry

+3.41667	  * Cutting Angle

-4.41667	  * Cutting Speed * Cutting Angle

The equation in part (c) and in the given in the computer output form a “hierarchial” model, that is, if an interaction is included in the model, then all of the main effects referenced in the interaction are also included in the model.

- Analyze the residuals.  Are there any obvious problems?

There is nothing unusual about the residual plots.

- Based on the analysis of main effects and interaction plots, what levels of A, B, and C would you recommend using?

Since B has a positive effect, set B at the high level to increase life.  The AC interaction plot reveals that life would be maximized with C at the high level and A at the low level.

6.9

Design Expert Output
Response	2	Fatigue
            ANOVA for selected factorial model
Analysis of variance table [Partial sum of squares - Type III]
		Sum of		Mean	F	p-value
	Source	Squares	df	Square	Value	Prob > F

Model		2801.25	3	933.75	16.81	0.0001	significant

A-Worker	2652.25	1	2652.25	47.75	< 0.0001
	  B-Bottle Type	100.00	1	100.00	1.80	0.2045
	  AB		49.00	1	49.00	0.88	0.3661
	Pure Error	666.50	12	55.54
	Cor Total	3467.75	15

	The Model F-value of 16.81 implies the model is significant.  There is only
	a 0.01% chance that a "Model F-Value" this large could occur due to noise.

	Values of "Prob > F" less than 0.0500 indicate model terms are significant.  
	In this case A are significant model terms.

There is an indication that one worker exhibits greater variability than the other.

6.12

- Estimate the factor effects.  Which factors appear to be large?

From the half normal plot of effects shown below, factors A, B, C, D, AB, AC, and ABC appear to be large.

Design Expert Output

Term	Effect	             SumSqr	              % Contribtn

Model	 Intercept

Model	 A	3.01888	72.9089	12.7408

Model	 B	3.97588	126.461	22.099

Model	 C	-3.59625	103.464	18.0804

Model	 D	1.95775	30.6623	5.35823

Model	 AB	1.93412	29.9267	5.22969

Model	 AC	-4.00775	128.496	22.4548

Error	 AD	0.0765	0.046818	0.00818145

Error	 BC	0.096	0.073728	0.012884

Error	 BD	0.04725	0.0178605	0.00312112

Error	 CD	-0.076875	0.0472781	0.00826185

Model	 ABC	3.1375	78.7512	13.7618

Error	 ABD	0.098	0.076832	0.0134264

Error	 ACD	0.019125	0.00292613	0.00051134

Error	 BCD	0.035625	0.0101531	0.00177426

Error	 ABCD	0.014125	0.00159613	0.000278923

- Conduct an analysis of variance.  Do any of the factors affect cracking?  Use (=0.05.

The Design Expert output below identifies factors A, B, C, D, AB, AC, and ABC as significant.

Design Expert Output

Response:	Crack Length	in mm x 10^-2

ANOVA for Selected Factorial Model

Analysis of variance table [Partial sum of squares]

Sum of		Mean	F

Source	Squares	DF	Square	Value	Prob > F

Model	570.95	15	38.06	468.99	< 0.0001	significant

A	72.91	1	72.91	898.34	< 0.0001

B	126.46	1	126.46	1558.17	< 0.0001

C	103.46	1	103.46	1274.82	< 0.0001

D	30.66	1	30.66	377.80	< 0.0001

AB	29.93	1	29.93	368.74	< 0.0001

AC	128.50	1	128.50	1583.26	< 0.0001

AD	0.047	1	0.047	0.58	0.4586

BC	0.074	1	0.074	0.91	0.3547

BD	0.018	1	0.018	0.22	0.6453

CD	0.047	1	0.047	0.58	0.4564

ABC	78.75	1	78.75	970.33	< 0.0001

ABD	0.077	1	0.077	0.95	0.3450

ACD	2.926E-003	1	2.926E-003	0.036	0.8518

BCD	0.010	1	0.010	0.13	0.7282

ABCD	1.596E-003	1	1.596E-003	0.020	0.8902

Residual	1.30	16	0.081

Lack of Fit	0.000	0

Pure Error	1.30	16	0.081

Cor Total	572.25	31

The Model F-value of 468.99 implies the model is significant.  There is only

a 0.01% chance that a "Model F-Value" this large could occur due to noise.

Values of "Prob > F" less than 0.0500 indicate model terms are significant.

In this case A, B, C, D, AB, AC, ABC are significant model terms.

- Write down a regression model that can be used to predict crack length as a function of the significant main effects and interactions you have identified in part (b).

Design Expert Output

Final Equation in Terms of Coded Factors:

Crack Length=

+11.99

+1.51	*A

+1.99	*B

-1.80	*C

+0.98	*D

+0.97	*A*B

-2.00	*A*C

+1.57	* A * B * C

(d)	Analyze the residuals from this experiment.

There is nothing unusual about the residuals.

- Is there an indication that any of the factors affect the variability in cracking?

By calculating the range of the two readings in each cell, we can also evaluate the effects of the factors on variation.  The following is the normal probability plot of effects:

It appears that the AB and CD interactions could be significant.  The following is the ANOVA for the range data:

Design Expert Output

Response:	Range

ANOVA for Selected Factorial Model

Analysis of variance table [Partial sum of squares]

Sum of		Mean	F

Source	Squares	DF	Square	Value	Prob > F

Model	0.29	2	0.14	11.46	0.0014	significant

AB	0.13	1	0.13	9.98	0.0075

CD	0.16	1	0.16	12.94	0.0032

Residual	0.16	13	0.013

Cor Total	0.45	15

The Model F-value of 11.46 implies the model is significant.  There is only

a 0.14% chance that a "Model F-Value" this large could occur due to noise.

Values of "Prob > F" less than 0.0500 indicate model terms are significant.

In this case AB, CD are significant model terms.

Final Equation in Terms of Coded Factors:

Range	 =

+0.37

+0.089	 * A * B

+0.10	 * C * D

- What recommendations would you make regarding process operations?  Use interaction and/or main effect plots to assist in drawing conclusions.

From the interaction plots, choose A at the high level and B at the low level.  In each of these plots, D can be at either level.  From the main effects plot of C, choose C at the high level.  Based on the range analysis, with C at the high level, D should be set at the low level.

From the analysis of the crack length data:

From the analysis of the ranges: