Lecture 1 B. INTRODUCTION:  SEISMIC WAVE ABSORPTION

1.a. Hilbert Transform & the Analytic Signal.

1.a.1. Instantaneous Amplitude, Frequency & Phase  Fourier Analysis is one of the most important tools of Signal Processing. For a seismic trace  the spectrum or power spectrum  describes how the energy is distributed among the different spectral components over the whole history of the process. In seismic interpretation however we are looking for instantaneous, quick lateral changes, observed over small time windows. Such changes might occur in

- Frequencies (in case, for example, of the thinning out of a sand lens;

- Amplitudes (due to a sudden change in reflectivity)

- Phase (if the reflection coefficient changes for example from r>0 to r<0 because of a sudden porosity change, or change in the pore filler.

As already recognized 25 years ago, the instantaneous properties (instantaneous amplitude , instantaneous phase , instantaneous frequency   of x(t) can be found by Hilbert Transform.

We consider the observed seismic trace as the real part of a complex-valued analytical trace (analytical signal) h(t), where

.                                                        (1.1)

In seismic processing y(t) is called the quadrature trace and, as we shall show, it can be uniquely determined from x(t) by means of the Hilbert Transform. From the instantaneous attributes are computed as follows:

(1.2.a-c)

The instantaneous attributes can be conveniently visualized using colored display.

1.a.2. The Hilbert Transform

Recall that the Fourier Transform, and inverse Fourier Transform are defined as

.                                                    (1.3)

The impulse response of a physically realizable system is always causal:  for  (Discussion: Difference between physically realizable and causal systems.) The Fourier Transform of the impulse response of a linear system is called the complex Transfer Function:

.                              (1.4)

The Hilbert Transform of a function  f(t) and its inverse transform are defined as

(1.5)

.                               (1.6)

Notes

- Both integrals (1.5 & 1.6) are meant in the sense of the  Cauchy principal value. The Cauchy principal value of a finite integral of a function f about a point  is given by

.

b) Taking the Fourier transform of Eq. (1.6) by means of the Convolution Theorem, and recalling that  (i.e. +i for positive, and –i for negative frequencies), we see that in the spectrum of the Hilbert transform all  original cosine components are transformed into negative sines, and all sines into cosines.

The analytic signal associated with a real function f(t) is the complex function

.                                                  (1.7)

The instantaneous amplitude (envelope), instantaneous phase, and instantaneous frequency, of  f(t)  are:

.         (1.8.a-c)

THEOREM: The complex Transfer Function of a casual system satisfies the dispersion relation between the imaginary and real parts of the transfer function:

(1.9)

.                                   (1.10)

Proof Because of causality, where H is the Heaviside step function, and g(t) is some arbitrary real-valued function. Write f(t) uniquely as the sum of its even and odd parts:

As and , it follows that

Comparing this with  we indeed get Eqs. (1.9-10).

Exercise 1.1.  Let the impulse response function of a causal system be

- What is the complex transfer function F(f)?

- Write up the dispersion  relation between .

1. b. Viscoelasticity & the Quality Factor Q

In elementary Seismics, the materials are assumed linear elastic (stress & strain are linearly proportional). In linear viscoelastic  materials the stress-strain relation also depends on the rate of the application of stress, that is on the time derivatives. The three most important models of   linear viscoelasticity are

Maxwell solid           (1.11.a)

Voigt solid               (1.11.b)

Standard lin. solid   (1.11.c)

Here  are additional elastic moduli   and   is viscosity. The standard linear solid is often represented with the "spring & dashpot system" whose displacement vs. force equation is the same as Eq. (1.11.c):

Exerciose 1.2.   Find the physical dimension of  from any of the Eqs. (1.11) using the rule that in a physically meaningful equation only quantities of equal dimension can be added together.

It can be shown that for a wave propagating in a viscoelastic solid the displacement is given by

,                          (1.12)

and that stress and strain are out of phase:

.                      (1.13.a, b)

The ratio of stress-to-strain is the complex modulus, .

The quality factor Q is a measure of how dissipative is the material. (The stronger is the dissipation, the smaller is Q.) It is defined in terms of the complex modulus as:

(1.14)

1. c. Some equivalent expressions for :

If W is the peak strain energy, is the energy dissipation per cycle, then

.                                                (1.15.a)

In terms of the absorption coefficient  in Eq. (13.12):

,                                                  (1.15.b)

where V is velocity, f is frequency.

In terms of the amplitude loss per cycle of an oscillatory signal with period T is:

,                                       (1.15.c)

( is called logarithmic decrement).

In terms of the phase delay between stress and strain (Eq. 1.13):

.                                                (1.15.d)

1. d. Wave attenuation in the standard linear solid

In case of a simple sinusoid wave

.                                      (1.16)

By Eq. (1.11.c)  where the complex frequency-dependent modulus is:

.                                     (1.17)

In the low-frequency- and high-frequency limits:

.                                     (1.18)

Exercise 1.3. Derive Eq. (1.17) by Fourier-transforming Eq. (1.11.c) and using the rule .

As both limits in (1.18) are frequency-independent real numbers, in these limiting cases we have elastic behavior. In between, the modulus can be written as

(1.19.a-d)

Exercise. 1.4. Derive (1.19.b) & (1.19.c) from (1.19.a).

Putting these Eqs. in the defining equation (1.14) of the quality factor Q:

.                        (1.20a)

The maximum attenuation occurs at the frequency and its value is

,                        (1.20b)

as schematically shown in the Figure:

1. e. Constant Q mechanism

It has been found experimentally over the frequency range of that in rocks the absorption is a near-linear function of frequency: (however, this has never been proven theoretically!). Substituting to (1.15.b) we see that in this case

(1.21)

If for  we have a constant-Q mechanism,  then the complex modulus and Q are related as

(1.22.a, b)

1. f. Velocity dispersion for the near-constant Q model

It can be proved that, in a nearly-constant-Q model and over a limited range of frequencies ,  the velocities are also frequency dependent. Their dispersion is:

.                (1.23)

Exercise 1. 5. Typical values for Q are:

| Lithology | Q | Range of for |
| --- | --- | --- |
| Igneous rocks | 75-150 |  |
| Sedimentary rocks | 20-150 |  |
| Sedimentary rocks containing gas in their pores | 5-50 |  |

Complete the Table!

1. g. The Kramers-Kronig relation between velocity dispersion and Q

Suppose we have a viscoelastic relation between stress and strain in the form

,                                         (1.24)

where r(t) is the relaxation function. Fourier transforming (13.24):

(1.25)

where is the complex modulus. But r(t) is causal, that is the Hilbert transform theorem of causal functions gives:

.                     (1.26)

Rewriting this in terms of the quality factor, , we get the general dispersion relations:

(1.27.a, b)

The Figure shows the schematic dispersion relations, for different viscoelastic models, computed from Eq, (1.27.b) and from measured velocity and attenuation values at 1 kHz & 1 MHz frequencies. Note that for all models when

1.h. Estimation of  Q  by the spectral ratio method

If the amplitude spectrum of the propagating wave changes with distance as

,        (1.28)

we can compare the amplitude spectra at different distances, and find Q from the slope of the logarithm of the ratio of the two amplitude spectra vs. frequency plot:

.                                     (1.29)

(See the schematic Figure below. Note that we can only use sufficiently high frequencies for this analysis.).

1. i. The power spectrum method Suppose we consider wavelets s(t) on a seismogram in two time-gates corresponding to depths . In the two time-gates the signal spectra are

(1.30)

where the factor  corresponds to frequency independent losses (such as spherical divergence). The factor "2" in the exponent is due to the fact that the wave traversed the layer twice, in the and the  directions. For a more stable spectral estimate we use the power spectrum

,                   (1.31)

where  is the autocorrelation function of s(t). From (1.30 & 1.31)

.                              (1.32)

The constant  can be found from the assumption that . Example: Power spectra above and below an oil deposit:

The absorption coefficient is found from the slope, using  Eq. (1.32).

# Footnotes

Based on: G. Mavko, T. Mukerji & J. Dvorkin, The Rock Physics Handbook. Tools for Seismic Analysis in Porous Media. Cambridge University Press, Cambridge, 1998, 329; G. Korvin, Signal Processing for Earth Scientists. Lecture Notes of a Short Course, KFUPM, Earth Sci. Dept., Dhahran, March 16-27, 1996.

See Topic 14.

M.T. Taner, F. Koehler & R.E.  Sheriff, "Complex seismic trace analysis", Geophysics, 4(1979):  1041-1063.

R.N. Bracewell. The Fourier Transform and its Applications. McGraw-Hill Book Co., New York, 1978,  pp. 267-272.

C. Zener, Elasticity and Anelasticity of Metals. University of Chicago Press, Chicago, 1984.

L. Knopoff, "Q". Rev. Geophys. 2(1964): 625-660.

C. Zener, Elasticity and Anelasticity of Metals. University of Chicago Press, Chicago, 1984.

Fig. 3.6.3 on G. Mavko, T. Mukerji & J. Dvorkin, The Rock Physics Handbook. Tools for Seismic Analysis in Porous Media. Cambridge University Press, Cambridge, 1998, p. 74.

P.B. Attewell & Y.V. Ramana "Wave attenuation and internal friction as functions of frequency in rocks". Geophysics 31(1966): 1049.

E. Kjartanson, "Constant Q wave propagation and attenuation". J. Geophys. Res. 84(1979): 4737-4748.

H.P. Liu, D.L. Anderson & H. Kanamori, "Velocity dispersion due to anelasticity: Implication for seismology and mantle composition." Geophys. J. Royal Astr. Soc. 47(1976): 41-58.

H.A. Kramers, Nature 117(1926): 775; R. de L. Kronig, J. Opt. Soc. Amer. 121(1926): 547.

T. Bourbié, O. Coussy & B. Zinszner, Acoustics of Porous Media, Gulf publishing Co., Houston, 1987.

N. Lucet, 1989, Ph. D. Dissertation, University of Paris.

G. Korvin, Signal Processing for Earth Scientists. Lecture Notes of a Short Course, KFUPM, Earth Sci. Dept., Dhahran, March 16-27, 1996.