Problem #2 from GK -HW-2

By measuring the total amplitude of the pulse on the cable  as a function of termination resistance Rt.

For a single reflection in a coaxial cable,  pulse total amplitude  Atot  for of an incident pulse amplitude A0 is given by  :

Atot = Aincident +Areflec;      where  Aincident= A0

Areflec= (Aincident where reflection coefficient (=(Rt-Z0)/ (Rt+Z0)

Where Rt is termination resistance and Z0 is characteristic impedance of the cable. Then

Atot = Aincident +Areflec= A0+( A0= A0(1+ ((Rt-Z0)/ (Rt+Z0)))

For A0= 5V  and Z0 = 50 ( , figure below shows the reflected amplitude and total amplitude of a 5V step as a function of Rt.

Check below Table of GK of reflected amplitude for various values of Rt.

| Rt | Reflected Amplitude |
| --- | --- |
| 0 | -A0 |
| 0-Z0 | -A0 to 0 |
| Z0 | 0 |
| Z0 to ( | 0 to + A0 |
| ( | + A0 |