Summary of chapter 8

- There are two types of potential energies in Phys101: One is gravitational and the other is elastic (spring).

- The work done by a conservative force is related to the change in potential energy by the relation:

- The weight (Fg) and the spring force (Fs) are both conservative forces.

- The force of friction is non-conservative force.

- The work done by a conservative force on a particle moving between two points, A and B, does not depend on the path taken by the particle.

A					   B

If the Force is conservative, then W1 = W2. The work is path independent!

- For a conservative force we have a relation between the force and the change in potential energy:	 (in one dimension).

- The change in gravitational potential energy of the Earth-object system is therefore:

If yf > yi Ug > 0

If yf < yi Ug < 0

y is the vertical distance traveled by the object.

- If the object is moving up, y is positive and U is positive.

- If the object is moving down, y is negative and U is negative.

- The potential energy at any location y is given by:

- The change in elastic potential energy of the block-spring system is:

If xf > xi Us > 0

If xf < xi Us < 0

- The potential energy of the spring is given by:

- If only conservative forces act on a particle, then the mechanical energy is conserved, E = K + U = Constant, and the change in mechanical energy is zero:	E = K + U = 0

- If only a conservative force act on a particle, and U(x) is given, then the force acting on the particle can be found by:

You can check this relation for yourself in the case of the weight and the spring force.

In the case of the spring force , then  and this is the force of the spring (Hooke's law)

- Work done by non-conservative forces:

The work energy theorem of chapter 7 says:

Where Wc is the work of conservative forces (force of gravity or spring force) and Wa is the work of the applied force. But Wc = ( U, so:

or

Where E = K+U is the mechanical energy of the system

E = K+U is the change in mechanical energy of the system

- Friction force:

If only a single friction force exist in the problem, then the change in mechanical energy is:

(Mechanical energy dissipated by the force of friction fk).

# Text boxes

Prepared by Dr. A. Mekki

W1

W2