|  | Formula | Comments |
| --- | --- | --- |
| Coulomb’s law |  | to find the electric force between two charges (F is a vector so, the direction should be considered ) |
| Line charge density (if we have a charge distributed on a line) |  | dq |
| Surface charge density (if we have a charge distributed over a surface ) |  |  |
| Volume charge density (if we have a charge distributed on a volume ) |  |  |
| Electric field |  | It is also a vector; direction must be considered. The superposition principle applies in case of many charges. |
| The force and electric field |  |
| Gauss law | The Gauss surface has the symmetry of the real charge distribution and E should be constant over this surface. | To use Gauss’s Law we should have a symmetric charge distribution and the most popular symmetries are cylindrical and spherical |
| The curl of the electric field = zero |  |  |
| The electric field can diverge |  |  |
| Relation between E and V |  |  |
| Relation between E and V |  |  |
| Relation between E and V |  |  |
| Potential |  | V is continuous at the boundary |
| Poisson’s equation |  | Which can be reduced to laplace equation if the charge density = zero |

# Text boxes

Real surface

Gauss surface