## Slide 1: Data Representation
COE 205
Computer Organization and Assembly Language
Dr. Aiman El-Maleh
College of Computer Sciences and Engineering
King Fahd University of Petroleum and Minerals
[Adapted from slides of Dr. Kip Irvine: Assembly Language for Intel-Based Computers]

## Slide 2: Outline
Introduction
Numbering Systems
Binary & Hexadecimal Numbers
Base Conversions
Integer Storage Sizes
Binary and Hexadecimal Addition
Signed Integers and 2's Complement Notation
Binary and Hexadecimal subtraction
Carry and Overflow
Character Storage

## Slide 3: Introduction
Computers only deal with binary data (0s and 1s), hence all data manipulated by computers must be represented in binary format.
Machine instructions manipulate many different forms of data:
  Numbers:
    Integers: 33, +128, -2827
    Real numbers: 1.33, +9.55609, -6.76E12, +4.33E-03
  Alphanumeric characters (letters, numbers, signs, control characters): examples: A, a, c, 1 ,3, ", +, Ctrl, Shift, etc.
  Images (still or moving): Usually represented by numbers representing the Red, Green and Blue (RGB) colors of each pixel in an image,
  Sounds: Numbers representing sound amplitudes sampled at a certain rate (usually 20kHz).
So in general we have two major data types that need to be represented in computers; numbers and characters.

## Slide 4: Numbering Systems
Numbering systems are characterized by their base number.
In general a numbering system with a base r will have r different digits (including the 0) in its number set. These digits will range from 0 to r-1
The most widely used numbering systems are listed in the table below:

## Slide 5: Binary Numbers
Each digit (bit) is either 1 or 0
Each bit represents a power of 2
Every binary number is a sum of powers of 2

## Slide 6: Converting Binary to Decimal
Weighted positional notation shows how to calculate the decimal value of each binary bit:
Decimal = (dn-1  2n-1) + (dn-2  2n-2) + ... + (d1  21) + (d0  20)
d = binary digit
binary 10101001 = decimal 169:
(1  27) + (1  25) + (1  23) + (1  20) = 128+32+8+1=169

## Slide 7: Convert Unsigned Decimal to Binary
Repeatedly divide the decimal integer by 2. Each remainder is a binary digit in the translated value:
37 = 100101
stop when quotient is zero
least significant bit
most significant bit

## Slide 8: Another Procedure for Converting from Decimal to Binary
Start with a binary representation of all 0’s
Determine the highest possible power of two that is less or equal to the number.
Put a 1 in the bit position corresponding to the highest power of two found above.
Subtract the highest power of two found above from the number.
Repeat the process for the remaining number

## Slide 9: Another Procedure for Converting from Decimal to Binary
Example: Converting 76d to Binary
  The highest power of 2 less or equal to 76 is 64, hence the seventh (MSB) bit is 1
  Subtracting 64 from 76 we get 12.
  The highest power of 2 less or equal to 12 is 8, hence the fourth bit position is 1
  We subtract 8 from 12 and get 4.
  The highest power of 2 less or equal to 4 is 4, hence the third bit position is 1
  Subtracting 4 from 4 yield a zero, hence all the left bits are set to 0 to yield the final answer

## Slide 10: Hexadecimal Integers
Binary values are represented in hexadecimal.

## Slide 11: Converting Binary to Hexadecimal
Each hexadecimal digit corresponds to 4 binary bits.
Example: Translate the binary integer 000101101010011110010100 to hexadecimal

## Slide 12: Converting Hexadecimal to Binary
Each Hexadecimal digit can be replaced by its 4-bit binary number to form the binary equivalent.

## Slide 13: Converting Hexadecimal to Decimal
Multiply each digit by its corresponding power of 16:
Decimal = (d3  163) + (d2  162) + (d1  161) + (d0  160)
d = hexadecimal digit
Examples:
  Hex 1234 = (1  163) + (2  162) + (3  161) + (4  160) =
  Decimal 4,660
  Hex 3BA4 = (3  163) + (11 * 162) + (10  161) + (4  160) =
  Decimal 15,268

## Slide 14: Converting Decimal to Hexadecimal
Decimal 422 = 1A6 hexadecimal
stop when quotient is zero
least significant digit
most significant digit
Repeatedly divide the decimal integer by 16. Each remainder is a hex digit in the translated value:

## Slide 15: Integer Storage Sizes
What is the largest unsigned integer that may be stored in 20 bits?
Standard sizes:

## Slide 16: Binary Addition
Start with the least significant bit (rightmost bit)
Add each pair of bits
Include the carry in the addition, if present
0
0
0
0
0
1
1
1
0
0
0
0
0
1
0
0
+
0
0
0
0
1
0
1
1
1
(4)
(7)
(11)
carry:
0
1
2
3
4
bit position:
5
6
7

## Slide 17: Hexadecimal Addition
Divide the sum of two digits by the number base (16). The quotient becomes the carry value, and the remainder is the sum digit.
36 28 28 6A
42 45 58 4B
78 6D 80 B5
1
1
21 / 16 = 1, remainder 5
Important skill: Programmers frequently add and subtract the addresses of variables and instructions.

## Slide 18: Signed Integers
Several ways to represent a signed number
  Sign-Magnitude
  1's complement
  2's complement
Divide the range of values into 2 equal parts
  First part corresponds to the positive numbers (≥ 0)
  Second part correspond to the negative numbers (< 0)
Focus will be on the 2's complement representation
  Has many advantages over other representations
  Used widely in processors to represent signed integers

## Slide 19: Two's Complement Representation
8-bit Binary value | Unsigned value | Signed value
00000000 | 0 | 0
00000001 | 1 | +1
00000010 | 2 | +2
. . . | . . . | . . .
01111110 | 126 | +126
01111111 | 127 | +127
10000000 | 128 | -128
10000001 | 129 | -127
. . . | . . . | . . .
11111110 | 254 | -2
11111111 | 255 | -1
Positive numbers
  Signed value = Unsigned value
Negative numbers
  Signed value = Unsigned value - 2n
  n = number of bits
Negative weight for MSB
  Another way to obtain the signed value is to assign a negative weight to most-significant bit
  = -128 + 32 + 16 + 4 = -76
1
0
1
1
0
1
0
0
-128
64
32
16
8
4
2
1

## Slide 20: Forming the Two's Complement
Sum of an integer and its 2's complement must be zero:
00100100 + 11011100 = 00000000 (8-bit sum)  Ignore Carry
The easiest way to obtain the 2's complement of a binary number is by starting at the LSB, leaving all the 0s unchanged, look for the first occurrence of a 1. Leave this 1 unchanged and complement all the bits after it.
starting value | 00100100 = +36
step1: reverse the bits (1's complement) | 11011011
step 2: add 1 to the value from step 1 | + 1
sum = 2's complement representation | 11011100 = -36

## Slide 21: Sign Bit
Highest bit indicates the sign. 1 = negative, 0 = positive
If highest digit of a hexadecimal is > 7, the value is negative
Examples: 8A and C5 are negative bytes
A21F and 9D03 are negative words
B1C42A00 is a negative double-word

## Slide 22: Sign Extension
Step 1: Move the number into the lower-significant bits
Step 2: Fill all the remaining higher bits with the sign bit
This will ensure that both magnitude and sign are correct
Examples
  Sign-Extend 10110011 to 16 bits
  Sign-Extend 01100010 to 16 bits
Infinite 0s can be added to the left of a positive number
Infinite 1s can be added to the left of a negative number
10110011 = -77
11111111 10110011 = -77
01100010 = +98
00000000 01100010 = +98

## Slide 23: Two's Complement of a Hexadecimal
To form the two's complement of a hexadecimal
  Subtract each hexadecimal digit from 15
  Add 1
Examples:
  2's complement of 6A3D = 95C3
  2's complement of 92F0 = 6D10
  2's complement of FFFF = 0001
No need to convert hexadecimal to binary

## Slide 24: Two's Complement of a Hexadecimal
Start at the least significant digit, leaving all the 0s unchanged, look for the first occurrence of a non-zero digit.
Subtract this digit from 16.
Then subtract all remaining digits from 15.
Examples:
  2's complement of 6A3D = 95C3
  2's complement of 92F0 = 6D10
  2's complement of FFFF = 0001
F F F 16
6 A 3 D
--------------
9 5 C 3
F F 16
9 2 F 0
--------------
6 D 1 0

## Slide 25: Binary Subtraction
When subtracting A – B, convert B to its 2's complement
Add A to (–B)
0 0 0 0 1 1 0 0 0 0 0 0 1 1 0 0
0 0 0 0 0 0 1 0 1 1 1 1 1 1 1 0 (2's complement)
0 0 0 0 1 0 1 0 0 0 0 0 1 0 1 0 (same result)
Carry is ignored, because
  Negative number is sign-extended with 1's
  You can imagine infinite 1's to the left of a negative number
  Adding the carry to the extended 1's produces extended zeros
Practice: Subtract 00100101 from 01101001.
–
+

## Slide 26: Hexadecimal Subtraction
When a borrow is required from the digit to the left, add 16 (decimal) to the current digit's value
Last Carry is ignored
Practice: The address of var1 is 00400B20. The address of the next variable after var1 is 0040A06C. How many bytes are used by var1?
C675
A247
242E
-1
-
16 + 5 = 21
C675
5DB9 (2's complement)
242E (same result)
1
+
1

## Slide 27: Ranges of Signed Integers
The unsigned range is divided into two signed ranges for positive and negative numbers
Practice: What is the range of signed values that may be stored in 20 bits?

## Slide 28: Carry and Overflow
Carry is important when …
  Adding or subtracting unsigned integers
  Indicates that the unsigned sum is out of range
  Either < 0 or > maximum unsigned n-bit value
Overflow is important when …
  Adding or subtracting signed integers
  Indicates that the signed sum is out of range
Overflow occurs when
  Adding two positive numbers and the sum is negative
  Adding two negative numbers and the sum is positive
  Can happen because of the fixed number of sum bits

## Slide 29: Carry and Overflow Examples
0
1
0
0
0
0
0
0
0
1
0
0
1
1
1
1
+
1
0
0
0
1
1
1
1
79
64
143
(-113)
Carry = 0 Overflow = 1
1
1
0
0
1
1
1
0
1
1
1
0
1
1
0
1
0
+
0
1
1
1
0
1
1
1
218 (-38)
157 (-99)
119
Carry = 1 Overflow = 1
1
1
1
We can have carry without overflow and vice-versa
Four cases are possible
1
1
1
1
1
0
0
0
0
0
0
0
1
1
1
1
+
0
0
0
0
0
1
1
1
15
245 (-8)
7
Carry = 1 Overflow = 0
1
1
1
1
1
0
0
0
0
1
0
0
0
0
0
0
0
1
1
1
1
+
0
0
0
1
0
1
1
1
15
8
23
Carry = 0 Overflow = 0
1

## Slide 30: Character Storage
Character sets
  Standard ASCII: 7-bit character codes (0 – 127)
  Extended ASCII: 8-bit character codes (0 – 255)
  Unicode: 16-bit character codes (0 – 65,535)
  Unicode standard represents a universal character set
    Defines codes for characters used in all major languages
    Used in Windows-XP: each character is encoded as 16 bits
  UTF-8: variable-length encoding used in HTML
    Encodes all Unicode characters
    Uses 1 byte for ASCII, but multiple bytes for other characters
Null-terminated String
  Array of characters followed by a NULL character

## Slide 31: ASCII Codes
Examples:
  ASCII code for space character = 20 (hex) = 32 (decimal)
  ASCII code for ‘A' = 41 (hex) = 65 (decimal)
  ASCII code for 'a' = 61 (hex) = 97 (decimal)

## Slide 32: Control Characters
The first 32 characters of ASCII table are used for control
Control character codes = 00 to 1F (hex)
Examples of Control Characters
  Character 0 is the NULL character  used to terminate a string
  Character 9 is the Horizontal Tab (HT) character
  Character 0A (hex) = 10 (decimal) is the Line Feed (LF)
  Character 0D (hex) = 13 (decimal) is the Carriage Return (CR)
  The LF and CR characters are used together
    They advance the cursor to the beginning of next line
One control character appears at end of ASCII table
  Character 7F (hex) is the Delete (DEL) character

## Slide 33: Parity Bit
Data errors can occur during data transmission or storage/retrieval.
The 8th bit in the ASCII code is used for error checking.
This bit is usually referred to as the parity bit.
There are two ways for error checking:
  Even Parity: Where the 8th bit is set such that the total number of 1s in the 8-bit code word is even.
  Odd Parity: The 8th bit is set such that the total number of 1s in the 8-bit code word is odd.