KING FAHD UNIVERSITY OF PETROLEUM & MINERALS
COMPUTER ENGINEERING DEPARTMENT

COE 205 Computer Organization & Assembly Language

Term 043 Lecture Breakdown

|  | Date | Topics | Ref. | Lab |
| --- | --- | --- | --- | --- |
|  | S 2/7 |  |  | Introduction, using MASM |
| 1 | S 2/7 | Syllabus. Introduction. Computer System, CPU, Memory, CPU-Memory Interface, Data Bus, Address Bus, Control Bus. Memory Hierarchy: RAM, Cache. | Chapter1 (Organization) & Chapter 1 (Assembly) |  |
| 2 | U 3/7 | Registers. Machine Language, Assembly Language. Instruction Formats, Opcode, Operands. Stored Program Concept, Fetch-Execute Cycle, Instruction Pointer. Instruction Register. | Chapter1 (Organization) & Chapter 1 (Assembly) |  |
|  | M 4/7 |  |  | Introduction, using MASM |
| 3 | M 4/7 | Why assembly language programming. Data Typing in High Level and Assembly Language, Assembler, Linker, Debugger. Programmer’s view of the computer, Instruction Set Architecture (ISA). i8086 processor characteristics, Control Unit & Datapath. Interfacing the CPU to memory & I/O. Types of Buses. One and Two-bus Architectures. | Chapter1 (Organization) & Chapter 1 (Assembly) |  |
| 4 | T 5/7 | Number representation: Binary, Octal, Hex. base conversion, fraction representation, unsigned and signed numbers. Sign-magnitude, 1’s complement, 2’s complement. | Appendix A & E (Assembly) |  |
| 5 | W 6/7 | Ranges of unsigned and signed number representation. Overflow detection for unsigned and signed numbers. Character Representation. ASCII Code. Even and Odd Parity. | Appendix A & E (Assembly) |  |
|  | S 9/7 |  |  | Assembly Format &Data Representation |
| 6 | S 9/7 | Assembly language syntax & Program Structure. Variable Declaration: DB, DW. (Quiz#1) | Chapter 3 & Section 12.5 (Assembly) |  |
| 7 | U 10/7 | Variable Declaration: DW, DD. Offset and PTR operators. Constant declaration using EQU. DUP operator. Input/Output using INT 21H. Reading character, displaying character, displaying a string. | Chapter 3 & Section 12.5 (Assembly) |  |
|  | M 11/7 |  |  | Input/Output |
| 8 | M 11/7 | Input/Output using INT 21H.: Reading character, Displaying character, Displaying a string, Reading a string. Loop Instruction. | Chapter 3 & Section 12.5 (Assembly) |  |
| 9 | T 12/7 | 8086 registers. Memory Segmentation, Logical & Physical Address. (Quiz#2) | Chapter 3 & 5 (Assembly) |  |
|  | S 16/7 |  |  | Segment. & Addressing Modes |
| 10 | S 16/7 | 8086 Addressing Modes: Immediate, Register, Direct, Register-Indirect, Based, Indexed, Based-Indexed. | Chapter 3 & 5 (Assembly) |  |
| 11 | U 17/7 | Pentium Registers. Pentium Addressing Modes. Status & Flags Register. | Chapter 3 & 5 (Assembly) |  |
|  | M 18/7 |  |  | Array indexing & Pentium Address. Modes |
| 12 | M 18/7 | Basic Pentium Instructions: MOV, XCHG, LEA, MOVZX, MOVSX, BSWAP, XLATB. (Quiz#3) | Chapter 3 & 5 & 6 (Assembly) |  |
| 13 | T 19/7 | Basic Pentium Instructions: ADD, SUB, INC, DEC, NEG, ADC, SBB, CMP. Introduction to flow control instructions. | Chapter 3 & 5 & 6 (Assembly) |  |
|  | S 23/7 |  |  | Arithmetic Instructions |
| 14 | S 23/7 | Multiplication Instructions: MUL, IMUL. Pentium IMUL instructions. Division Instructions: DIV, IDIV. Sign Extension Instructions: CBW, CWD, CDQ, CWDE. | Chapter 6 & 3 (Assembly) |  |
| 15 | U 24/7 | Applications of Multiplication & Division instruction. Logical Instructions: NOT, AND, OR, XOR, Test. Applications of logic instructions. (Solution of ExamI). | Chapter 3 & 6 & 8 (Assembly) |  |
|  | M 25/7 |  |  | Logical & Bitwise Instructions |
| 16 | M 25/7 | Shift Instructions: SHL, SAL, SHR, SAR. Applications of using shift instructions in performing multiplication. Applications of using shift instructions in performing division. SHLD, SHRD. | Chapter 3 & 6 & 8 (Assembly) |  |
| 17 | T 26/7 | Rotate Instructions: ROL, ROR, RCL, RCR. Applications of rotate instructions. (Quiz#4) | Chapter 3 & 6 & 8 (Assembly) |  |
|  | S 30/7 |  |  | Flow Control Instructions |
| 18 | S 30/7 | Flow Control Instructions: Unconditional JMP. Types of jump target: Short, Near, Far. Conditional Jump instructions: Signed and Unsigned. Single-flag jump instructions. Loop Instructions: Loop, Loope/Loopz, Loopne/Loopnz. High-Level Decision Control Structures: IF-Then-Else, For Loop, Case. | Chapter 7 & 4 (Assembly) |  |
| 19 | U 31/7 | Case, While Loop, Repeat Until. Indirect Jump Example. The Stack: PUSH and POP instructions, PUSHA, POPA, PUSHAD, POPAD, PUSHF, POPF, PUSHFD, POPFD. Introduction to Procedures: CALL and RET. | Chapter 7 & 4 (Assembly) |  |
|  | M 1/8 |  |  | Procedures & Macros |
| 20 | M 1/8 | Procedure Definition, Near and Far Procedures, RET n instruction. Passing Parameters to Procedures. Examples of Procedures. (Quiz#5) | Chapter 7 & 4 (Assembly) |  |
| 21 | T 2/8 | Introduction to Macros. Macro Definition & Expansion. Pseudo parameters in macros. Macros versus procedures. Macro Library. Examples of Macros. REP and IRP macros. Conditional assembly. List Control Directives. | Chapter 10 (Assembly) |  |
|  | S 6/8 |  |  | String Instructions |
| 22 | S 6/8 | String Instructions: MOVS, MOVSB, MOVSW, MOVSD. REP Prefix. CMPS, CMPSB, CMPSW, CMPSD, SCAS, SCASB, SCASW, SCASD, LODS, LODSB, LODSW, LODSD, STOS, STOSB, STOSW, STOSD, REPE, REPNE. Applications of string instructions. | Chapter 9 (Assembly) |  |
| 23 | U 7/8 | Input/Output: IN and OUT instructions, Direct and Indirect I/O. Introduction to Interrupts. Difference between interrupts and procedures. Types of Interrupts: Hardware. Software, Exceptions. Maskable and non-maskable Interrupts, Interrupt Flag. (Quiz#6) | Chapter 12 (Assembly) |  |
|  | M 8/8 |  |  | Interrupts |
| 24 | M 8/8 | IVT, Interrupt Processing, Bios and DOS interrupts. CPU Design: Control unit and Data Path. Register Transfer. Data-Path Design. Connecting Registers using Muxs. Connecting Registers using a tri-state bus. Examples of register transfer: MOV, XCHG, ADD. | Chapter 12 (Assembly) Chapter 2 & 4 (Organization) |  |
| 25 | T 9/8 | Register Transfer Timing: Estimating Minimum Clock Period. Single-Bus CPU Data path design. Single-Bus CPU design: Fetch Control Sequence, Synchronous vs. Asynchronous Memory Transfer, Execution Control Sequence for MOV, ADD, XCHG, INC, ADD with register indirect addressing mode, unconditional Jump. | Chapter 2 & 4 (Organization) |  |
|  | S 13/8 |  |  | Video Memory |
| 26 | S 13/8 | Execution Control Sequence for conditional Jump, CMP, and LOOP. Performance Considerations. Two-Bus CPU: Fetch Control Sequence, Execution Control Sequence for ADD with register indirect addressing mode, unconditional and conditional Jump. Three-Bus CPU: Fetch Control Sequence, Execution Control Sequence for ADD, unconditional and conditional Jump Instructions. | Chapter 2 & 4 (Organization) |  |
| 27 | U 14/8 | Control Unit Design: Hardwired Control Unit, General Hardwired Control Unit Organization, Generation of Control Signals. Solution of Exam II. | Chapter 4 (Organization) |  |
|  | M 15/8 |  |  | Using the Mouse |
| 28 | M 15/8 | Deriving Rout & Rin Signals. CPU-Memory Interface Circuit. | Chapter 4 (Organization) |  |
| 29 | T 16/8 | Microprogrammed Control Unit Design: Control Word, Control Store, Microinstruction, Microroutine. General Organization of Microprogrammed Control Unit, Micro Program Counter, Micro Instruction Register. Sequencer, Branching Address. Horizontal, Vertical and Field-encoded control store. | Chapter 2 & 4 (Organization) |  |
|  | S 20/8 |  |  | Serial Port |
| 30 | S 20/8 | Vertical control store. Microroutine for Add instruction with 8 addressing modes. Wide branch addressing and Multiway branching. Bit Oring. Comparison of Hardwired vs. Microprogrammed control unit. | Chapter 2 & 4 (Organization) |  |
| 31 | U 21/8 | Simple CPU Design Example. Review. |  |  |
| 32 | M 22/8 | No Class. |  |  |