COE 205, Term 082

Computer Organization & Assembly Programming

HW# 2

# Show the content of the memory allocated based on the following directives, assuming that the first byte is allocated at address 0000H in the data segment.

I 	DB	-1, 255

DW	0FAh

DD	-250

J	DB	`24`

K         EQU    24

DW	`24`

DW	offset J

DB	2 dup (2,4,2 dup(`24`))

# Suppose that you have the following initial content of the registers and memory locations, assuming that variables i and j are defined as byte variables:

AX=F2E9H		BX=0002H		CX=08A0H		DX=F1E0H

SI   =0016H		DI =0010H		BP=C2E1H		SP  =1330H

DS =1EC0H		ES =2FF4H		CS=3FDFH		SS  =5000H

IP  =E731H

Memory Address (hex)      	             Contents (hex)

2000: 	 i	0010				1E

0011				3F

0012				BC

j	0013				58

0014				30

0015				8A

0016				D3

0017				F7

0018				00

## Show the contents of the registers and memory locations modified after the execution of each of the following instructions. Use the initial content of the registers and memory locations for the execution of each instruction. Furthermore, specify the addressing modes of the source and destination operands in each instruction.

### ADD AX, [BX+16]

### MOV BH, Byte PTR i+4

### ADD CL, [SI-2]

### MOV BYTE PTR [BX+DI+1], -1

### MOV Word PTR i,  offset j

### MOV DX, [BX][SI]

## Determine the starting and ending addresses of the code segment. What is the physical address of the next instruction to be fetched from memory.

## Determine the physical address of the source operand in the following instruction:

MOV AX, [BX+DI+1]

## Show the contents of AX, BX, and the flags (O,S,Z,A,P, and C) at the end of  executing the ADD  instruction

MOX AX, ABCEH

MOV BX,  4816H

ADD BX, AX

## Show the contents of AX, BX, and the flags (O,S,Z,A,P, and C) at the end of  executing the SUB instruction

MOX AX, 6A57H

MOV BX,  74DAH

SUB  AX, BX