COE 205, Term 991

Computer Organization & Assembly Programming

HW# 2

Due date: Wednesday, Oct. 6

# Show the content of the memory allocated based on the following directives, assuming that the first byte is allocated in address 0000H in the data segment.

I 	DB	0,1,2

DW	0,1,2

DD	0,1,2

J	DB	`A`, `B`

DB	`AB`

DW	`AB`

DW	offset J

DB	2 dup (`AB`)

# Suppose that you have the following initial content of the registers and memory locations:

AX=0312H		BX=0012H		CX=0010H		DX=0210H

SI   =0010H		DI =0012H		BP=0200H		SP  =0300H

DS =2000H		ES =3000H		CS=1000H		SS  =4000H

IP  =1220H

Memory Address      	             Contents (hex)

2000: 	0010				12

0011				34

0012				56

0013				78

0014				9A

0015				BC

0016				DE

0017				F0

## Show the contents of the registers and memory locations modified after the execution of each of the following instructions. Use the modified contents of the registers and memory locations as initial values for the subsequent instructions. Furthermore, specify the addressing modes of the source and destination operands in each instruction.

### ADD BX, 0001H

### MOV DL, [0011]

### ADD CX, [SI]

### MOV [DI], BL

### MOV AX, 0001H[BX]

### MOV [BX][DI], CL

## Determine the starting and ending addresses of the code segment. What is the physical address of the next instruction to be fetched from memory.

## Show the contents of AX, BX, and the flags (O,S,Z,A,P, and C) at the end of  executing the following  instructions

MOX AX, 7FDBH

MOV BX,  8799H

ADD AX, BX

## Show the contents of AX, BX, and the flags (O,S,Z,A,P, and C) at the end of  executing the following  instructions

MOX AX, 7FDBH

MOV BX,  8799H

SUB  AX, BX

# Write an 8086 assembly program to prompt the user to enter a lower-case letter, read the letter entered and display the corresponding upper-case letter. The program should convert the letter to its upper-case equivalent and display it on a new line. The C version of the program is given below. Use the INT 21H routine, for character input, character output, and string output.

C version:

Main()

{

int c;

printf(``Enter a lower-case letter:``);

c=getchar();

c= c - 32; /* convert to lower case */

printf(``\n The upper-case equivalent is: %c ``,c);

}