COE 205, Term 992

Computer Organization & Assembly Programming

HW# 2

Due date: Sat., Feb. 19

# Show the content of the memory allocated based on the following directives, assuming that the first byte is allocated at address 0000H in the data segment.

I 	DB	-21, 233

DW	-21

DD	-15

J	DB	`12`

K         EQU    20

DW	`12`

DW	offset J

DB	2 dup (`12`)

# Suppose that you have the following initial content of the registers and memory locations, assuming that variables i and j are defined as byte variables:

AX=0E22H		BX=0001H		CX=01F0H		DX=F1E0H

SI   =0016H		DI =0014H		BP=0200H		SP  =0300H

DS =2000H		ES =3000H		CS=5F2FH		SS  =4000H

IP  =E731H

Memory Address (hex)      	             Contents (hex)

2000: 	 i	0010				A1

0011				E2

0012				AF

j	0013				C2

0014				11

0015				3C

0016				5D

0017				71

## Show the contents of the registers and memory locations modified after the execution of each of the following instructions. Use the initial content of the registers and memory locations for the execution of each instruction. Furthermore, specify the addressing modes of the source and destination operands in each instruction.

### ADD AX, [BX+16]

### MOV DX, WORD PTR i+2

### ADD CX, [SI-2]

### MOV BYTE PTR [BX+DI], -1

### MOV AX,  offset j

### MOV j, CL

## Determine the starting and ending addresses of the code segment. What is the physical address of the next instruction to be fetched from memory.

## Determine the physical address of the source operand in the following instruction:

MOV AX, [BX+DI+1]

## Show the contents of AX, BX, and the flags (O,S,Z,A,P, and C) at the end of  executing the ADD  instruction

MOX AX, 7FACH

MOV BX,  7438H

ADD BX, AX

## Show the contents of AX, BX, and the flags (O,S,Z,A,P, and C) at the end of  executing the SUB instruction

MOX AX, 6C38H

MOV BX,  72F9H

SUB  AX, BX

# Write an 8086 assembly program to prompt the user to enter a 2-digit number and then displays the 2 digits in reverse, i.e., if the user enters the number 29, the program displays the number 92. Use the INT 21H routine for character input, character output, and string output.