Name:									Id#

COE 205, Term 012

Computer Organization & Assembly Programming

Quiz# 1

Date: Sunday, March  3, 2002

# Q1. Consider an 8-bit register that has the binary number 11000011. Determine the decimal value of the number if it represents:

## An unsigned number.

## A signed number in sign-magnitude representation.

## A signed number in 1’s complement representation.

## A signed number in 2’s complement representation.

## A character where the most significant bit is a parity bit. Is the parity bit even or odd parity. Note that the ASCII code of character ‘A’ is 41H.

# Q2. Perform the following arithmetic operations assuming that numbers are represented using 8-bit 2’s complement representation. Determine the decimal values of the numbers and the result. Indicate in your answer when an overflow occurs.

## i.  01110101 + 11001100

## ii. 11111101 - 01111110

# Q3.  Complete the following sentences:

## (1) The instruction register is a register in the CPU that ………………………….………

## (2) The program counter is a register in the CPU that …………………………………….

## (3) In the fetch-execute cycle, the instruction is read from memory in the ………… phase, and its operands are read from memory in the ……….……… phase.

## (4) After fetching an instruction from memory, the instruction pointer is always incremented by ……………………………...

## (5) Assuming 8-bit 2`s complement representation, the smallest (negative) number in binary is …………….. and in decimal is ……………….. and the largest (positive) number in binary is …………………. and in decimal is ………………...

## (6) The ASCII code representation of the decimal number 64 is expressed in hexadecimal as …………. Note that the ASCII code for the digit 0 is 30H.

## (7) A CPU with a 32-bit address bus and a 64-bit data bus can access a memory of size ………………... bytes, and transfer a maximum of ………. bytes in a read or write cycle.

## (8) The instruction set architecture of a computer consists of ……………………………………………………………………………………………..,

## …………………………………………………………….……………………………….,

## and …………………………………………………………………………………….……