Name:									Id#

COE 205, Term 021

Computer Organization & Assembly Programming

Quiz# 1

Date: Wednesday, Oct. 2, 2002

# Q1. Consider an 8-bit register that has the binary number 11000110. Determine the decimal value of the number if it represents:

## An unsigned number.

## A signed number in sign-magnitude representation.

## A signed number in 1’s complement representation.

## A signed number in 2’s complement representation.

# Q2. Perform the following arithmetic operations assuming that numbers are represented using 8-bit 2’s complement representation. Indicate in your answer when an overflow occurs.

## i.  01111111 + 00000001

## ii. 11111111 - 01111111

# Q3.  Indicate whether the following is true or false, and if it is false correct it:

## (1) (True, False)	The instruction register is a register in the CPU that contains the address of the next instruction to be executed by the CPU.

## (2) (True, False)	In the fetch-execute cycle, the instruction is read from memory in the fetch phase, and its operands are read from memory in the execution phase.

## (3) (True, False)	The instruction pointer is always incremented by 1 after fetching an instruction from memory.

## (4) (True, False)	Assuming 6-bit 2`s complement representation, the smallest (negative) number is 111111 and the largest (positive) number is 011111.

## (5) (True, False)	The ASCII code representation of the decimal number 64 is expressed in hexadecimal as 3634. Note that the ASCII code for the digit 0 is 30H.

## (6) (True, False)	A CPU with a 32-bit address bus and a 64-bit data bus can access a memory of size 4 Gbit, and transfer a maximum of 6 bytes in a read or write cycle.

## (7) (True, False)	The instruction register and the program counter are part of the instruction set architecture of a computer.

## (8) (True, False)	The binary number 11000110 represents character f, and uses an odd parity bit. Note that the ASCII code of character A is 41H and that of character a is 61H.