Name: KEY									Id#

COE 205, Term 051

Computer Organization & Assembly Programming

Quiz# 1

Date: Monday, Sep. 26, 2005

# Q1. Fill the blank in each of the following questions:

## The Instruction Pointer (IP) register holds the address of the next instruction to be fetched from memory.

## The Instruction (IR) register holds the fetched instruction to be executed.

## The Memory Address (MAR) register is connected to the address bus in the CPU memory interface.

## The Memory Data (MDR) register is connected to the data bus in the CPU memory interface.

## The Instruction Set Architecture (ISA) of a computer consists of Instruction Set, Memory, and Programmer-accessible registers.

## The size of the address bus in the 8086 processor is 20 bits while in the Pentium Processor it is 32 bits.

## The size of the data bus in the 8086 processor is 16 bits while in the Pentium Processor it is 64 bits.

## Reading an instruction from Memory is performed in the Fetch phase.

## Reading operands from Memory is performed in the Execute phase.

## Incrementing the Instruction Pointer is performed in the Fetch phase.

## Decoding an instruction is performed in the Execute phase.

## With an address bus size equal to 32 bits, the memory address space is 4G Bytes.

## With a data bus size equal to 32 bits, the maximum number of bytes that is transferred between the CPU and memory per a read/write cycle is  4 Bytes.

## After reading an instruction whose size is 16 bits, the instruction pointer is incremented by 2

## The CPU is divided into two main units called Control Unit and Data Path Unit

## Two of the reasons for why it is important to program in Assembly Language are   it gives us full control of the machine resources which allows us to do things that could not be done with high-level languages and for writing very efficient code for certain functions.

## The Cache memory is faster than the RAM and slower than the Registers.

## The program that translates assembly language into machine language is called Assembler.