Name:									Id#

COE 205, Term 071

Computer Organization & Assembly Programming

Quiz# 1

Date: Monday, Sep. 24, 2007

# Q1. Fill the blank in each of the following questions:

## The program that translates assembly language into machine language is called ____________________.

## There is a one-to-one mapping between assembly language and ____________________.

## Two of the reasons for why it is important to program in Assembly Language are   _____________________________________________________________________      and   ________________________________________________________________.

## Two advantages of programming in high-level language are _____________________________________________________________________      and   ________________________________________________________________.

## The _________________________ register holds the address of the next instruction to be fetched from memory.

## The Instruction Set Architecture (ISA) of a computer consists of __________________________________, _______________________________, and __________________________________________.

## The _______________________________ provides an interface between hardware and software.

## The CPU is divided into two main units called _____________________ and ____________________.

## With an address bus size equal to 36 bits, the memory address space is ____________ Bytes.

## With a data bus size equal to 64 bits, the maximum number of bytes that is transferred between the CPU and memory per a read/write cycle is   ____________ Bytes.

## In ________________ memory, data is lost when device is powered off while ________________ memory stores information permanently.

## In ______________ RAM, each cell is made up of 6 transistors and it is faster but less dense than __________________ RAM.

## The need for memory hierarchy is due to ____________________________________________________________________.

## The Cache memory is faster than ____________________ and slower than _______________________.

## Given a magnetic disk with the following properties:

  - Rotation speed = 7200 RPM (rotations per minute)

  - Average seek = 8 ms, Sector = 512 bytes, Track = 200 sectors

Then, Time of one rotation (in milliseconds) = _____________________________

Average time to access a block of 64 consecutive sectors = __________________________________________________________________________________________________________________________________________

## The 6-bit binary number 110100 in sign-magnitude representation represents the decimal value _______________ while in 1's complement representation it represents the decimal value _______________ and in 2's complement representation it represents the decimal value  _______________.

## Assuming 8-bit 2's complement representation, the largest positive number that can be stored in decimal is ____________ and in binary it is ____________ while the smallest number that can be stored in decimal is ___________ and in binary is _______________.

## Assuming 8-bit 2's complement representation, the following operation A9 – 70 produces the results ______________ and the overflow flag will be equal to __________.