Name:									Id#

COE 205, Term 991

Computer Organization & Assembly Programming
Quiz# 1

Date: Saturday, Sep. 25

# (I) Consider the following two numbers A=-200 and B=-121

## Express the two numbers in both sign-magnitude and 2`s complement notations, assuming 9-bit representation.

## Perform the operation A+B twice, once for sign-magnitude notation and once for 2`s complement notation. Indicate in your answer when an overflow occurs.

## Perform the operation A-B twice, once for sign-magnitude notation and once for 2`s complement notation. Indicate in your answer when an overflow occurs.

## Determine, in binary and decimal, the smallest (negative) number and the largest (positive) number that can be stored using the sign-magnitude notation, assuming 9-bit representation.

## Determine, in binary and decimal, the smallest (negative) number and the largest (positive) number that can be stored using the 2`s complement notation, assuming 9-bit representation.

# (II) Indicate whether the following is true or false, and if it is false correct it:

## (1) (True, False)	The instruction register is a register in the CPU that contains the address of the next instruction to be fetched from memory.

## (True, False)	The fetch-execute cycle refers to the process of fetching the operands of an instruction from memory and then executing the instruction.

## (True, False)	The program counter is the register in the CPU counting the number of instructions executed so far by the CPU.

## (True, False)	The instruction set architecture includes the instruction set, the machine`s memory, and all the registers in the machine.

## (True, False)	There is a one-to-one mapping from an assembly instruction to a machine instruction, but a one-to-many mapping from a high-level language to a machine language.

## (True, False)	Assembly programs written for the Intel 8086 family processors can run on the Motorolla 68000 processors using the Motorolla assembler and linker programs.