Name: KEY									Id#

COE 205, Term 031

Computer Organization & Assembly Programming

Quiz# 1

Date: Tuesday, Sep. 23, 2003

# Q1. Explain the function of each of the following:

## Instruction Pointer (IP).

The Instruction Pointer is a register that holds the address of the next instruction to be fetched from memory.

## Instruction Register (IR).

## The Instruction Register is a register that is used to store temporarily the fetched instruction for execution.

## Assembler.

The Assembler is a program that translates from assembly language to machine language.

## Memory Address Register (MAR).

The Memory Address Register is a register in the CPU connected to the address bus in the CPU-Memory interface. It is used to store the address to be read from or written to.

## Q2. Describe what is meant by the Instruction Set Architecture (ISA) of a computer.

The Instruction Set Architecture (ISA) of a computer is the collection of assembly/machine instruction set of the machine and the machine resources (memory and programmer-accessible registers) that can be managed with these instructions.

## Q3. Which of the following 8086 registers is part of the ISA: Instruction Pointer (IP), Instruction Register (IR), Memory Address Register (MAR), AX, SP.

The following 8086 registers are part of the ISA:  Instruction Pointer (IP), AX, SP.

# Q4.  Determine the machine type and the size of the address bus and the data bus for the 8086 and the Pentium processors.

| Processor | Machine Type | Address Bus | Data Bus |
| --- | --- | --- | --- |
| 8086 | 16-bit | 20 bit | 16 bit |
| Pentium | 32-bit | 32 bit | 64 bit |

# Q5.  Determine whether the following operations are performed in the fetch or execute phase: Reading an instruction from Memory, Reading Operands from Memory, Decoding an Instruction, Incrementing the Instruction Pointer.

| Operation | Phase |
| --- | --- |
| Reading an instruction from Memory | Fetch phase |
| Reading Operands from Memory | Execute phase |
| Decoding an Instruction | Execute phase |
| Incrementing the Instruction Pointer | Fetch phase |

## Q6.  Order the following storage devices once in terms of speed and once in terms of capacity: RAM, Registers, Tape, Hard Disk, and Cache.

The order from fastest to slowest is:	Registers, Cache, RAM, Hard Disk, Tape.

The order from lowest capacity to highest is:	Registers, Cache, RAM, Hard Disk, Tape.