Name: KEY									Id#

COE 205, Term 032

Computer Organization & Assembly Programming

Quiz# 1

Date: Tuesday, Feb. 24, 2004

# Q1. Fill the blank in each of the following questions:

## The Instruction Pointer register holds the address of the next instruction to be fetched from memory.

## The Instruction register holds the fetched instruction to be executed.

## The Memory Address register is connected to the address bus in the CPU memory interface.

## The Memory Data register is connected to the data bus in the CPU memory interface.

## The Instruction Set Architecture (ISA) of a computer consists of the instruction set, the machine’s memory, and the programmer’s accessible registers.

## The size of the address bus in the 8086 processor is 20 bits while in the Pentium Processor it is 32 bits.

## The size of the data bus in the 8086 processor is 16 bits while in the Pentium Processor it is 64 bits.

## Reading an instruction from Memory is performed in the fetch phase.

## Reading operands from Memory is performed in the execute phase.

## Incrementing the Instruction Pointer is performed in the fetch phase.

## Decoding an instruction is performed in the execute phase.