Name: KEY									Id#

COE 205, Term 043

Computer Organization & Assembly Programming

Quiz# 1

Date: Saturday, July 9, 2005

# Q1. Explain the function of each of the following:

## Instruction Pointer (IP).

A register that holds that address of the next instruction to be fetched from memory.

## Instruction Register (IR).

A register that holds that instruction fetched from memory.

## Assembler.

A program that translates assembly language to machine language.

## Memory Address Register (MAR).

A register connected to the address bus and holds the address of memory location that is to be read from or written to.

## Q2. Describe what is meant by the Instruction Set Architecture (ISA) of a computer.

The Instruction Set Architecture of a computer is the set of instructions of the computer, 	the memory and the  programmer accessible registers.

## Q3. Which of the following 8086 registers is part of the ISA: Instruction Pointer (IP), Instruction Register (IR), Memory Data Register (MDR), CX, SI, Y.

IP, CX, SI

# Q4.  Determine the machine type and the size of the address bus and the data bus for the 8086 and the Pentium IV processors.

| Processor | Machine Type | Address Bus | Data Bus |
| --- | --- | --- | --- |
| 8086 | 16-bit | 20-bit | 16-bit |
| Pentium IV | 32-bit | 36-bit | 64-bit |

# Q5.  Determine whether the following operations are performed in the fetch or execute phase: Reading an instruction from Memory, Reading and Writing Operands from/to Memory, Incrementing the Program Counter, Performing Arithmetic Operations e.g. subtraction.

| Operation | Phase |
| --- | --- |
| Reading an instruction from Memory | Fetch |
| Reading and Writing Operands from/to Memory | Execute |
| Incrementing the Program Counter | Fetch |
| Performing Arithmetic Operations e.g. subtraction | Execute |

## Q6.  Order the following storage devices once in terms of speed and once in terms of capacity: RAM, Registers, Hard Disk, and Cache.

SPEED: Registers, Cache, RAM Hard Disk 	(order from highest speed to lower)

CAPACITY: Hard Disk, RAM, Cache, Registers	(order from higher capacity to lower)