Name: KEY									Id#

COE 205, Term 052

Computer Organization & Assembly Programming

Quiz# 1

Date: Wednesday, Feb. 22, 2006

# Q1. Explain the function of each of the following registers

## Instruction Pointer (IP).

A register that holds that address of the next instruction to be fetched from memory.

## Instruction Register (IR).

A register that holds that instruction fetched from memory.

# Q2. Suppose that the Instruction Pointer (IP) content is 0005 and that the instruction stored starting at that address is MOV AX, 5, which has a corresponding machine code B80005. Determine the content of the Instruction Pointer (IP) after fetching this instruction.

Since the size of the fetched instruction is 3 bytes, then the IP will be incremented by 3 to point to the address of the next instruction i.e., IP=0005+3=0008.

## Q3. Give two advantages of programming in assembly language compared to high-level languages (e.g. Java).

## One can write more efficient programs with smaller code size than those written in high-level languages and translated into assembly by compilers.

## Full control of machine resources.

## Q4. Which of the following 8086 registers is part of the ISA: Instruction Pointer (IP), Instruction Register (IR), Memory Address Register (MAR), Memory Data Register (MDR), AX, DL, SI, SP, BP, Y, Z.

The following registers are part of the ISA:

Instruction Pointer (IP), AX, DL, SI, SP, BP.

# Q5.  Determine the machine type and the size of the address bus and the data bus for the 8086 and the Pentium IV processors.

| Processor | Machine Type | Address Bus | Data Bus |
| --- | --- | --- | --- |
| 8086 | 16-bit | 20-bit | 16-bit |
| Pentium IV | 32-bit | 36-bit | 64-bit |

# Q6.  Determine whether the following operations are performed in the fetch or execute phase: Reading an instruction from Memory, Reading and Writing Operands from/to Memory, Incrementing the Program Counter, Performing Arithmetic Operations e.g. subtraction.

| Operation | Phase |
| --- | --- |
| Reading an instruction from Memory | Fetch |
| Reading and Writing Operands from/to Memory | Execute |
| Incrementing the Program Counter | Fetch |
| Performing Arithmetic Operations e.g. subtraction | Execute |

## Q7.  Order the following storage devices once in terms of speed and once in terms of capacity: RAM, Registers, Hard Disk, and Cache.

SPEED: Registers, Cache, RAM Hard Disk 	(order from highest speed to lower)

CAPACITY: Hard Disk, RAM, Cache, Registers	(order from higher capacity to lower)