Name: KEY									Id#

COE 205, Term 062

Computer Organization & Assembly Programming

Quiz# 1

Date: Saturday, March 3, 2007

# Q1.What is the Instruction Set Architecture (ISA) of a computer?

## The Instruction Set Architecture (ISA) of a computer consists of Instruction Set, Memory, and Programmer-accessible registers.

# Q2.What is Assembly Language and how it is different from Machine Language?

Assembly language is the set of instructions a CPU can execute using symbolic names to represent operations, registers and memory locations. Each assembly language instruction corresponds to a single machine language instruction. Machine language is the set of instructions that a CPU can execute represented in binary format.

# Q3.Give two advantages for programming in Assembly Language and two advantages for programming in High-Level Language.

## Two advantages for programming in assembly language are:

- Accessibility to system hardware

- Space and time efficiency

## Two advantages for programming in High-Level  language are:

- Program development is faster and program maintenance is easier

- Programs are portable

# Q4. Fill the blanks in the following questions:

## Assuming 8-bit 2`s complement representation, the smallest (negative) number is 10000000 in binary and -128 in decimal and the largest (positive) number is 01111111 in binary and +127 in decimal.

## Consider an 8-bit register that has the binary number 10010110. The decimal value of this number as a signed number in sign-magnitude representation is -22 while in 1’s complement representation it is -105 and in 2’s complement representation it is -106.

## Assuming 8-bit 2`s complement representation, the number F0 represents the decimal number -16.

## The binary number 01100100 represents character d and uses an ODD parity bit. Note that the ASCII code of character A is 41H and that of character a is 61H.

# Q5. Perform the following arithmetic operations assuming that numbers are represented using 8-bit 2’s complement representation. Indicate in your answer when an overflow occurs.

## 8F + FC = 8B

There is no overflow since we are adding two negative numbers and we got a negative number.

## ii. 6E – E0= 6E + 20 = 8E

There is overflow since we are adding two positive numbers and we got a negative number.